## Slide 1: Generic use of service-level-AA procedure
TEI19 proposal

## Slide 2: Outline
Rel-17 feature summary
Rel-17 limitation
Objectives
Proposals

## Slide 3: Rel-17 Feature summary
During ID_UAS, API based Authentication/Authorization procedure was introduced
  Service-level AA procedure (SM NAS, TS 24.501) + Nnef service (TS 29.256) + Naf service (TS 29.255)
  For future-proofness, stage-3 WGs have specified the protocol for generic purpose not limited to ID_UAS features. Any services requiring Authentication/Authorization procedure with 5GS/EPS, rel-17 mechanism will be used as baseline
    CT1 has defined Service-Level-AA Container (SLAC) to cope with any vertical services requiring authentication/authorization
    Nnef service and Naf service carry a transparent payload for authentication/authorization not specific to certain services
UE
SMF
NEF
AF
SM NAS: Service-level AA procedure
(SLAC)
Nnef_authentication
(auth msg + others)
Naf_authentication
(auth msg + others)
NOTE: For details of SLAC encoding and Nnef/Naf API data model, please see Annex
NOTE: UUAA procedure during NAS registration procedure is supported for ID_UAS specific requirement

## Slide 4: Rel-17 Overall procedural steps for UUAA
Upon app layer request, the UE includes SLAC in the PDU session establishment message with service-level device ID set to CAA-level UAV ID
SMF checks UE subscription if it is required for UUAA, and trigger UUAA procedure by invoking Nnef_auth services (including service-level device ID)
UAS-NF(NEF) triggers Naf_auth services with including the service-level device ID
USS(AF) trigger Naf_auth notification service to UAS-NF(NEF) with including authentication msg
UAS-NF(NEF) triggers Nnef_auth notification services to SMF with including authentication msg
SMF sets the service-level AA payload of the SLAC to the received authentication msg, and includes the SLAC in the Service-Level Authentication Command msg
UE forwards the received service-level AA payload to the upper layer
The upper layer of the UE provides UUAA payload then the UE sets the service-level AA payload of the SLAC to the received UUAA payload and includes the SLAC in the Service-Level Authentication Complete msg
SMF forwards the service-level AA payload to UAS-NF(NEF) by invoking Nnef_auth service (including authentication msg)
UAS-NF(NEF) triggers Naf_auth services with including the authentication msg
USS(AF) sends authentication result by invoking Naf_auth notification service
UAS-NF(NEF) triggers Nnef_auth notification services to SMF with including the authentication result
SMF sends PDU session establishment accept message with including SLAC where the service-level-AA result (SLAR field) is set to successful
UE forwards the result of service-level AA procedure and proceed NAS procedure
(TS 24.501, 29.256, 29.255)
Miscellaneous details are omitted

## Slide 5: Rel-17 limitation (by design)
UE and NW
  UE operation: it is specified that the UE supporting UAS services can include service-level device ID which will trigger service-level AA procedure
  NW operation: it is specified that the SMF checks UE SM subscription data only for UAS e.g., accepts the request and trigger UUAA procedure, or rejects the request from the UE with cause ‘UAS services not allowed’
  SLAC: two types of payload are specified in NAS specification - UUAA and C2 authorization
UE and NW operation for AA procedure (trigger, accept, reject) are not specified for generic use cases. No support for services other than UAS services
Nnef
  Data models are UAS specific
  The scope of TS 29.256 is specific to UAS, but the applicability is not restricted
 Although ‘authmsg’ can be used for any services, data model and descriptions are UAS specific
Naf
  Data models are UAS specific
  The scope of TS 29.255 is specific to UAS, but the applicability is not restricted
 Although ‘authmsg’ can be used for any services, data model and descriptions are UAS specific

## Slide 6: Objectives, uses cases, assumptions
Rel. 17 limitation were introduced because the procedure was required only for UAVs: there is no technical limitation to adopting the mechanism to generic authorization and authentication by an 3rd party external AF
Aim is at extending the usage of Service-level-AA procedure to any services requiring 3GPP assisted authentication/authorization
Main use case:
  User service connectivity request for e.g. enterprise service like virtual office or health care e.g., services with higher cyber security requirement, that do not support EAP mechanism

## Slide 7: Comparison to existing mechanism
PAP/CHAP
  Supports only a very specific authentication mechanism
  Out-of-date and possible susceptible to Man-in-the-middle or eavesdropping attack
Secondary authentication
  Focused on EAP/AAA authentication mechanisms
NSSAA
  Requires 3rd party to get assigned a dedicated slice (S-NSSAI)
GUSLAP enables API-based authentication, supporting any mechanisms beyond EAP/AAA that may be required by 3rd party services and providers

## Slide 8: Objectives, uses cases, assumptions
Basic assumptions
  Service-level user ID is required for those services: Management of service-level user ID is out of 3GPP scope but service provider scope
    NOTE that the service-level user ID is equivalent to the service-level device ID that has been defined for ID_UAS rel-17.
  UE subscription-based control to determine whether to perform service-level AA procedure for those services
Control plane (UE and Network) enhancement for services requiring AA procedure
  Existing SM NAS procedure and information can be enhanced to support service-level AA procedure for general purpose
    How to determine the services requiring service-level AA procedure
  Further enhancement for the case where multiple services (requiring AA procedure) are available for the UE
    How to identify the target application function/target services (both uplink and downlink)
Network exposure function enhancement
  Adding NEF services for generic purpose service-level AA procedure in TS 23.502
    Currently, NEF_auth is defined in TS 23.256 only with specific description for UAS.
  How to discover target network function e.g., target NEF or target AF for the requested service
    Especially if multiple services are available for the UE for the DNN/S-NSSAI

## Slide 9: Why TEI 19 proposal
Rel-17 ID_UAS stage-2 requirement on specifying generic container/procedure/API for AA procedure were implemented in stage-3
  However, limitation is observed as shown in slide 5.
Minimal architecture impact or end-to-end procedure changes are expected
  Enhancement of existing stage-3 tools (IE, procedures, APIs) can support the feature for any services
The scope is not ID_UAS specific but general support for any services, new TEI-19 work item is appropriate approach
Support of multiple services needs stage-2 requirement
  How to identify the service and how to discover NF for the service are subject to stage-2 scope

## Slide 10: Supporting companies
Qualcomm
Verizon Wireless

## Slide 11: Annex

## Slide 12: Encoding of SLAC
Service-level-AA container IE
Service-level-AA device ID
Service-level-AA server address
Service-level-AA response
Service-level-AA payload type
Service-level-AA pending indication
Service-level-AA payload
“UUAA payload”
“C2 authorization payload”
SLAR
C2AR

## Slide 13: Nnef_Auth data model
Nnef_auth data model
UAVAuthinfo
AuthNotification
UAVAuthResponse
UAVAuthFailure
AuthResult
Notify Type
  GPSI, Service-level device ID, IP of UE, Auth msg, PEI, Auth Server Address, Auth notification URI, DNN, S-NSSAI, UE location info, nf type (AMF/SMF)
  GPSI, Service-level device ID, Auth msg, auth session correlation ID, notification type, revoke cause
  GPSI, Auth result, Auth msg, Service-level device ID, auth session correlation ID
  Error, UAS resource release indication
  Success
  Re-auth, update of authorization data, revoke

## Slide 14: Naf_Auth data model
Naf_auth data model
UAVAuthinfo
UAVAuthResponse
AuthResult
Re-auth or Revoke Notify
Notify Type
Problem Details
Authenticate Authorize
  GPSI, Service-level device ID, IP of UE, Auth msg, PEI, Auth notification URI, Notification correlation ID, UE location info, supported feature
  GPSI, Service-level device ID, IP of UE, Auth msg, Notification correlation ID, Notify type
  Success
Additional Info
Authenticate Authorize
Revoke Cause
  GPSI, Auth result, Auth msg, Service-level device ID, supported feature
  UAS resource release indication
  Re-authentication, Re-authorization, revoke