## Slide 1
Congestion control question in CT3 LS
Nokia, Nokia Shanghai Bell, Ericsson
SA WG2 Meeting S2-159
13-17 November, 2023, Chicago, IL, USA
S2-2312075

## Slide 2: Background (1/2)
The LS from CT3 (S2-2310102/ C3-233649) asks SA2 that:
Question: For the Congestion information, Data Rate and PDV, does it mean that the measurement failure also needs to be reported if no measurement result is available?
This slide-set analyses the scenario to propose a way forward.
Assumptions:
  RAN is not aware whether the congestion report is requested for L4S or congestion exposure towards the AF. RAN reports in the same manner towards UPF for both L4S marking and congestion exposure towards the AF.
  TS 23.501 states “This NG-RAN reported information is common to support congestion information exposure and to support ECN marking for L4S in PSA UPF as described in clause 5.37.3.3.”

## Slide 3: Background (2/2)
Snippets from TS 23.501 relevant for this question:
“SMF also indicates to NG-RAN to report the congestion information (i.e. a percentage of packets that UPF uses for ECN marking for L4S) of the QoS Flow on UL and/or DL directions via GTP-U header extension to PSA UPF.”
“For a given QoS Flow, if the target NG-RAN supports congestion information reporting, the target NG-RAN shall report congestion information to UPF once it is available.”
“For the UL and/or DL congestion information monitoring (see clause 5.45.3), based on the PCC rule from PCF, the SMF requests the NG-RAN to report the information via GTP-U header to PSA UPF. This NG-RAN reported information is common to support congestion information exposure and to support ECN marking for L4S in PSA UPF as described in clause 5.37.3.3. In the case of congestion information exposure, the PSA UPF exposes the UL and/or DL congestion information via Nupf_EventExposure service or via SMF/PCF/NEF as described in clause 5.8.2.18. “

## Slide 4: Congestion report from RAN
RAN
UPF
Inter-NFs*
AF
Req. Congestion info
Req. Congestion info
No congestion, no reports
10% of PDUs to be ECN marked
Congestion report
Congestion report
10% of PDUs to be ECN marked
Congestion report update
Congestion report update
20% of PDUs to be ECN marked
Congestion report update
Congestion report update
Congestion trigger in RAN
0% of PDUs to be ECN marked
No congestion
No congestion
Congestion trigger update
Congestion trigger update
No congestion
No further reports until there is a congestion trigger in RAN
No report is assumed to be “no congestion”
*Inter-NFs = SMF/PCF/NEF or only NEF.

## Slide 5: Observations and Way forward
Observations:
RAN reports towards the UPF whenever the percentage value is subject to a change.
No report from the RAN can be assumed as “previously reported value is still valid” thus marking by the UPF operates on the previously reported value, no report towards the AF is necessary. AF assumes the “previously reported value is still valid”. No need for periodic reporting for congestion control.
No information report from RAN shall not be considered as measurement failure. Requiring RAN to report periodically when there is “nothing new to report” is useless, which can even lead to unnecessary congestion in the RAN.
Given the agreed encoding of the RAN information [two decimal point %] it is very unlikely that the RAN information will not be updated for a significant time. This is due to fast changing resource conditions at the RAN.
UPF cannot derive measurement failure due to lack of reports from RAN. In other words, UPF deriving measurement failure due to lack of congestion reports will lead to incorrect reporting towards trusted/untrusted AF.
Proposed way forward:
Measurement failure towards AF shall not apply for congestion report from RAN.
Periodic reporting shall not apply for congestion report from RAN.