## Slide 1: Discussion for work tasks on 5GS and TSN integration
Ling Zhang
Siemens

## Slide 2: Introduction
IEC/IEEE 60802 TSN Profile for Industrial Automation
  “defines time-sensitive networking profiles for industrial automation. The profiles select features, options, configurations, defaults, protocols, and procedures of bridges, end stations, and LANs to build industrial automation networks.”
  When integrated with TSN, the 5GS is regarded as an IA-Station (Industrial Automation Station) that follows IEC/IEEE 60802 TSN profile. IA-Station (5GS) supports the required capabilities with digital data sheets modeled with YANG. The CNC provides configuration information via NetConf/YANG.

## Slide 3: Discussion
Technical scope (issues) of relevant work tasks in the SID for TRS/TSC&URLLC/LAN enhancements:
  How are the IEC/IEEE 60802 TSN configuration information translated to the TSN-related configurations within 5GS (WT-4.3)
    Enable 5GS to receive and handle the required IEC/IEEE 60802 YANG configurations
    Translate/map YANG configurations with the PMIC/UMIC information
  How 5GS is enhanced for functions/capabilities required as common features in IEC/IEEE 60802
    Whether and how 5GS needs enhancements to support the industrial traffic types (especially the required traffic types) (WT-4.3)
    Enhancements to support Multiple Spanning Tree Protocol (WT-4.1.3)

## Slide 4: Proposal
In Rel-19 “Study on enhancement of Timing Resiliency, TSC&URLLC, and LAN”, support for IEC/IEEE 60802 is proposed as:
  Justifications:
  IEC/IEEE 60802 “Time-sensitive networking profile for industrial automation” requires the support of MSTP (Multiple Spanning Tree Protocol), both configuration and protocol, for loop prevention. In 5G-VN, two UEs (one at the begin and one at the end of a conveyor belt), may make a ring out of the linear topology of the Ethernet LAN over the 5GS. Additionally, this setup allows a media redundancy using the 5GS – if the wireline breaks, every node is still reachable through the 5GS. 5GS enhancements for support of MSTP needs to be studied in order to support prevention of loops.
  To achieve better interoperability with respect to industrial automation in integrated 5G/TSN networks, it is beneficial to study the enhancements of 5GS for alignment on common industrial features including industrial traffic, and NetConf/YANG configurations defined in IEC/IEEE 60802.
  Objectives (in WT-4):
  - WT-4.1.3: Support of Multiple Spanning Tree Protocol to ensure loop prevention
  - WT-4.3: Enhancements to 5GS TSN support to align with IEC/IEEE 60802 Time-sensitive networking profile for industrial automation

## Slide 5: Reference for YANG Data Modules, Features, and Nodes required from 5GS logical bridge (for information only)

## Slide 6: Common YANG modules, features, and nodes
IEEE standard for Ethernet
    Selected nodes from ieee802-ethernet-interface YANG module (IEEE Std 802.3.2-2019)
Station and MAC connectivity discovery
    Selected nodes from ieee802-dot1ab-lldp YANG module (IEEE Std 802.1ABcu-2021)
Time Synchronization
    Selected features and nodes from ieee1588-ptp YANG module (IEEE P1588e)
    Selected nodes from ieee802-dot1as-ptp YANG module (IEEE P802.1ASdn)
Security configuration
    Selected features and nodes from ietf-keystore YANG module (IETF draft-ietf-netconf-keystore)
    Selected nodes from ietf-netconf-acm YANG module (IETF RFC 8341)
    Selected features and nodes from ietf-truststore YANG module (IETF draft-ietf-netconf-trust-anchors)
IA-Station capabilities
    Nodes from iecieee60802-ia-station YANG module (IEC/IEEE 60802)

## Slide 7: Common YANG modules, features, and nodes
IA-Station management
    Selected nodes from ietf-system-capabilities YANG module (IETF RFC 9196)
    Selected nodes from ietf-yang-library YANG module (IETF RFC 8525)
    Selected features and nodes from ietf-yang-push YANG module (IETF RFC 8641)
    Selected nodes from ietf-notification-capabilities YANG module (IETF RFC 9196)
    Selected features and nodes from ietf-subscribed-notifications YANG module (IETF RFC 8639)
    Selected nodes from ietf-netconf-monitoring YANG module (IETF RFC 6022)
    Selected nodes from ietf-system YANG module (IETF RFC 7317)
    Selected nodes from ietf-hardware YANG module (IETF RFC 8348)
    Selected nodes from ietf-interfaces YANG module (IETF RFC 8343)
    Selected features and nodes from ieee802-dot1q-bridge YANG module (IEEE Std 802.1Q-2022, Clause 48 + IEEE P802.1Qcw)
    Nodes from iecieee60802-bridge YANG module (IEC/IEEE 60802)
    Nodes from iecieee60802-ethernet-interface YANG module (IEC/IEEE 60802)
    Selected features and nodes from ietf-netconf-server YANG module (IETF draft-ietf-netconf-client-server)
    Selected nodes from ietf-subscribed-notifications YANG module (IETF RFC 8639)
    Nodes from iecieee60802-subscribed-notifications YANG module (IEC/IEEE 60802)
    Selected nodes from ieee802-dot1q-psfp-bridge YANG module (per stream filtering and policing) (IEEE P802.1Qcw)

## Slide 8: Conditionally mandatory YANG data models, features, and nodes
Scheduled traffic
    Selected features and nodes from ieee802-dot1q-sched YANG module (IEEE P802.1Qcw)
    Nodes from iecieee60802-sched-bridge YANG module (IEC/IEEE 60802)
Frame preemption
    Selected features and nodes from ieee802-dot1q-preemption YANG module (IEEE P802.1Qcw)
Credit-based shaper
    ieee-cbs YANG module (IEEE P802.1Qdx)
Frame replication and elimination for reliability (FRER)
    Selected nodes from ieee802-dot1cb-stream-identification YANG module (IEEE Std 802.1CBcv-2021)
    Selected nodes from ieee802-dot1cb-frer YANG module (IEEE Std 802.1CBcv-2021)