## Slide 1: Rel-19 Discussion on enhancing roaming service in edge computing Ph#3
3GPP SA2#160
Agenda Item : 30.1
SK Telecom
S2-2312035

## Slide 2
Background
There are two types of roaming architectures in 3GPP:
  local-breakout : it fully utilizes the visited operator network which is not common in live network due to charging and QoS control issues.
  Home-routed : Home-routed is primarily used in live network but QoS significantly decreases because all data traffic is routed to home operators(physically located within the domestic region), even though application servers(e.g., Youtube) are near the roaming customers.
  there is a need for enhancing roaming service to satisfy QoS and control charging/policy in HPLMN.
With the advancements in cloud technology, operators can now utilize hyperscaler's overseas regions for deploying 5G Core equipment, eliminating the need to build their own data centers abroad.
In the past(4G era), PGW had both the Control Plane and User Plane integrated, making it costly and less secure to deploy the Control Plane abroad. However, with the application of CUPS (Control and User Plane Separation) technology, deploying only the User Plane abroad has eliminated the risk of customer information exposure.
S2-2312035

## Slide 3
International roaming service that deploys UPF at the edge using a public cloud global region
(1) The UPF(HPLMN) is physically located overseas, while the SMF(HPLMN) is physically located domestically for home-routed roaming.
- Policy and Charging control is done by HPLMN
- User traffic is locally break-out near VPLMN for out-bound roamers
(2) Data latency on Global CP(Contents Provider) is improved, and domestic service is provided at the same level to the present.
(3) AS-IS : Home-routed roaming architecture and all traffic is routed to domestic area
TO-BE : Home-routed roaming architrecture and all traffic is locally break-out
Core NFs
(Policy/Charging)
youtube.com
(overseas)
<As-Is>
youtube.com
(domestic)
UE
MME
SGW
H-SMF
Core NFs
(Policy/Charging)
UE
AMF
VPLMN(Overseas)
V-SMF
V-UPF
Latency is significantly reduced
<To-Be>
naver.com
(domestic)
Signal Path
Bearer Path
HPLMN(domestic)
HPLMN(domestic)
HPLMN(Overseas)
VPLMN(Overseas)
Use Case
DNS
DNS
H-UPF
PGW
S2-2312035

## Slide 4
Proposal(add new Work-Task)
WT-6 : Study for enhancing roaming service utilizing data center(ex. public cloud) in overseas regions, aiming to enhance QoS
  WT-6a : Deploy H-UPF to data center in overseas region to handle outbound roaming subscriber traffic locally for enhancing QoS. This study include how H-SMF select overseas H-UPF, how H-UPF select a nearby DNS/H-EASDF and transmitting it to the UE via H-SMF.
  WT-6b : Study on how H-UPF monitors V-UPF per serving PLMN and report it to H-SMF to minimize service impact when network failure.
Rel-19 study on Edge Computing (Ph3)
S2-2312035