## Slide 1: Discussion about URSP over EPS (eUEPO)
Oracle, Verizon UK Ltd., Ericsson
3GPP TSG-SA WG2 Meeting #160
Chicago, USA, November 13 – 17, 2023
S2-2312063
(Was previously S2-2308554 in SA# 158 (was not handled))

## Slide 2
Slide #3 illustrates UE Policy Association Establishment on 5G side (taken from 29.513 for clarity’s purpose, however, reflects also 23.502 4.16.11)
Slide #4 illustrates URSP provisioning - E2E mobility from 5GS to EPS
Claim #1: (as shown in slide #3) during UE Policy Association Establishment on 5G side, the UE-PCF needs to:
  Register itself in the BSF. Let’s denote this as (*)
  Check whether the UE Policy container includes indication of UE support for EpsUrsp (i.e URSP over EPS). If positive, store indication of UE support for EpsUrsp in the UDR. Let’s denote this as (**)
  Justification for claim #1:
  1. (*) above will enable step 5 in slide #4 – This seems to be already captured in 23.502 4.16.11 step 4 “…The (H-)PCF in roaming and the PCF in non-roaming may register to the BSF as the PCF serving this UE, if not already registered at the AM Policy Association establishment.” – so no CR is needed for that.
  2. (**) above will enable step 4 in slide #4 - Seems to be missing in stage 2.. Hence, a new alignment CR is required to fix that (S2-2312062).
Claim #2: Both SM-PCF and UE-PCF need to store their ability to support EpsUrsp in the NRF (i.e URSP over EPS). Denoted as (***)
Justification for claim #2:
If (***) does not take place, then steps 2 and 8 in slide #5 the Discovery &selection of SM-PCF and UE-PCF by the SMF+PGW-C and by SM-PCF respectively can not be done via the NRF - Hence, two new CRs are required to enable that (S2-2312060(23.501)/S2-2312061 (23.502)).
DP for URSP over EPS (by Oracle – 10/31/2023)

## Slide 3
29.513 Figure 5.6.1.2-1: UE Policy Association Establishment procedure - Non-roaming
Enhanced UE Policy Association Establishment on 5G side (Based on 23.502, 29.512, 29.525, 29.513)
As we can see below that step 16 (the action of storing indication of UE's support for ‘URSP provisioning in EPS’ in the UDR (by the UE PCF)) is already captured in stage 3. hence what stage 2 needs is an alignment CR.
29.525 4.2.2.2.1.1
During Initial Registration and 5GS Registration during UE mobility from EPS to 5GS, …
The (H-)PCF, … for the UEs .., may store in the UDR, as specified in 3GPP TS 29.519 [17]:
……
e) if the "EpsUrsp" feature defined in 3GPP TS 29.519 [17] is supported, the indication of UE's support for URSP provisioning in EPS included in the "UE STATE INDICATION" message as described in the Annex D of 3GPP TS 24.501 [15], if available. //btw, language seems here seems a bit messed up…

## Slide 4
Note: The ‘E2E mobility’ scenario is not a subsequent scenario to ‘initial UE attach in EPS’. Hence, SM-PCF is not assumed to have yet an N43 association with UE-PCF for that subscriber.
URSP provisioning - E2E mobility from 5GS to EPS (Based on 23.502, 29.512, 29.525, 29.513)

## Slide 5
Initial URSP provisioning - E2E Initial Attach procedure in EPC (Based on 23.502, 29.512, 29.525, 29.513)

## Slide 6
Continue… Initial URSP provisioning - E2E Initial Attach procedure in EPC (Based on 23.502, 29.512, 29.525, 29.513)