## Slide 1: Discussion on PDU Set handling for UL
China Mobile, Tencent
S2-2312363
TSG SA2#160,
Nov, 2023, Chicago

## Slide 2: PDU set handling for UL
Editor's note: [XRM] The applicability and details of supporting PDU Set handling in uplink direction may be updated based on RAN WG's progress.
As a key feature in R18, PDU set handling for DL enables differentiated handling for efficient resource scheduling. It is esstential to introduce PDU Set handling for UL to achieve the complete end-to-end mechanism of PDU set handling for XR services.
RAN2/3 and CT1 have sent LSs to SA2 for PDU set UL handling. The XR awareness has been agreed in RAN2, which needs SA2 to define related parameters for RAN and UE:
  “RAN2 assumes that PDU Set based parameters and PDU Set related information may be used for better support of XR services. RAN2 can consider both UL and DL directions.” in [R2-2209215]
  “RAN2 has also agreed that the UE needs to be able to identify PDU Sets / Bursts but that in-band marking of PDUs in the uplink over Uu (the equivalent of downlink marking in GTP headers) is not needed.” in [R2-2213225]
  “RAN2 considers that the PDU set concept is applicable to both UL and DL.” in [R2-2302010]
9.12.2 | S2-2311953 | LS In | Action | LS from CT WG1: LS on uplink PDU Set | CT WG1 (C1-237936) | Rel-18 | XRM
9.12.2 | S2-2311967 | LS In | Action | LS from RAN WG3: Provisioning separate DL and UL PDU Set QoS Parameters to NG-RAN | RAN WG3 (R3-235890) | Rel-18 | NR_XR_enh-Core
9.12.2 | S2-2311981 | LS In | Action | LS from RAN WG2: LS on XR awareness | RAN WG2 (R2-2311590) | Rel-18 | NR_XR_enh-Core
Observation 1: RAN has decided PDU Set handling is applicable to both UL and DL. Therefore, SA2 should consider to support the PDU Set handling for UL in Rel-18, and if needed, define associated parameters for NG-RAN and/or UE.

## Slide 3
Tdoc | Company | Main Content
S2-2310724 | Qualcomm | 1)UE reporting capability indication to 5GC in SM capability; 2)UL PDU set QoS handling is independent with DL PDU set QoS handling; Both are optional 3)PSIHI indicates UL and DL individually 4)SMF may include the Protocol Description in the QoS rule provided to the UE 5)UE shall start PDU set UL handling when UE indicates the capability as well as receives the QoS paramters and Protocol Description from 5GC. 6) How UE support the PDU set UL handling is depending on RAN specification
proposal in draft folder | Google | 1)UE implementation to determine whether to perform PDU Set UL handling 2)Protocol Description may be received from the upper layers of the UE or SMF 3)NG-RAN provides the UE with an indication of whether the PDU Set based handling is supported
proposal in draft folder | Huawei | 1)SMF optionally provides Protocol Description together with the QoS rule to the UE
proposal in draft folder | vivo | 1)UE implementation to support PDU set UL handling 2)CN determines whether PDU Set QoS is applied in UL or not based on UE capability,i.e. UE should provide the capability to 5GC 3)Not separate the UL/DL PDU set handling 4)Not support CN provides PDU Set QoS parameters to the UE
proposal in draft folder | OPPO | 1)SMF provides PDU Set UL Identification Indication to UE in the QoS rule, which is used to activate the PDU Set identification in the UE for the uplink direction of the QoS Flow
S2-2310669 | China Mobile | 1)UE provide the capability indication for UL PDU set handling; 2)SMF provides PDU Set QoS parameters and Protocol Description to UE
S2-2310244 | Samsung | When PDU Set Parameters are applied for the QoS flow, UE uses the same UE derived QoS rule for all PDUs of a PDU Set
Observation 2: people cannot agree with the following aspects:
Whether UE provides the capability indication for PDU set UL handling to 5GC
Whether the UE gets the Protocol Description from 5GC, i.e. NAS signaling.
Whether UE shall support PDU set UL handling once the parameters are sent from 5GC.
Whether UL and DL PDU set parameters are the same or not, when the UL/DL PDU set handling are supported.
Observation 3: If consensus cannot be achieved by SA2, then SoH will be needed to determine the way forward.
In last meeting as well as in the draft folder, several companies have submitted the CRs to solve this, detailed as below:

## Slide 4: SoH Questions (1)-Related with UE
Whether UE provides the capability indication for PDU set UL handling to 5GC
Whether the UE gets the Protocol Description from 5GC, i.e. via NAS signaling.
Whether UE shall support PDU set UL handling once the parameters are sent from 5GC.
Notes: 标红项需确认

## Slide 5
Whether UL and DL PDU set parameters are the same or not, when both the UL and DL PDU set handling are supported.
SoH Questions (2)-Related with RAN
Notes: 标红项需确认