## Slide 1: Leveraging VFL Distributed Collaborative Learning to predict Signaling Storm and QoE OPPO, KDDI, China Telecom, China Unicom
S2-2312674

## Slide 2: Agenda
VFL Use Case#1: Leveraging Inter-domain VFL to support Application QoE Prediction
VFL Use Case#2: Leveraging Intra-5GC VFL to support Signaling Storm
Conclusions
Local Model
Local Model
Local Model

## Slide 3
Use Case#1: Leveraging Inter-domain VFL to support Application QoE Prediction
Local Model
Local Model
Local Model

## Slide 4: How 5G Cross-domain AI Learning Works? (Use Case: Application QoE Prediction)
Problem Statement:
QoE is a subjective information, measured in KQI, and cannot be expressed quantitatively (i.e. objectively, mathematically expressed)
Network performance parameters in the form of QoS metrics (e.g. packet delay, jitter, packet loss etc.) cannot identify specific service
Application cannot identify the user experience (i.e. QoE) until the service is delivered
NWDAF relies on AF to provide input data, i.e. QoE, to derive the analytics, however, AF may not want to share the QoE target directly with 5GC, by leveraging the VFL, AF indicate the feature related to the QoE to 5GC without sharing the objective of the QoE target.
QoE has been defined by ITU-T SG12 (2007) as “the overall acceptability of an application or service, as perceived subjectively by the end user”, and it is closely related to the specific service delivery. It includes the total end-to-end system effects, and it may be influenced by user expectations and degree of delight or annoyance during the fruition of a service
EXAMPLE of Illustration on how to address this Application QoE Prediction Issue:
Specify the mappings of various QoS metrics (quantifiable), measured in KPI, to be corresponding to QoE performance metric (expected user experience), measured in KQI
Apply ML and Analytics to determine the KPI
Perform the mapping of KPI to KQI in order to predict the QoE
See Backup Slides for Examples of KPI to KQI mapping to support the Application QoE Prediction for 5G Voice and Video Streaming services

## Slide 5: EXAMPLE for How Cross-domain Collaborative AI Learning Works & How it could impact 5GS?
Model Participant/Organizer
(AF)
5G
Network
A
B
1
Cross-domain FL preparation
Entit(ies) involved in
the Operation
3GPP
Impact
AI/ML Operation Descriptions
Selecting FL Member UEs
Initiating Cross-domain FL operation
5GC local FL operation
Model Update/ Inference report
Cross-domain FL Operation
1
2
3
4
5
2
4
5
AF determines the QoE (i.e. Label) for the target application and the required features in each domain (e.g. UE, 5GC) and the corresponding KPIs for the features
AF
None
AF may directly or leverage the Member UE selection criteria to 5GC to select one or more UEs to perform the cross-domain FL.
AF, 5GC,
Re-use existing Member UE selection
AF triggers the cross-domain FL operations towards the 5GC and UE by sending the local training model, the features and the KPIs corresponding to the specific target domain.
AF, 5GC, UE
Extend 5GC Service Provisioning
Note that, AF communication with UE should be at the application layer.
5GC performs the feature mapping to select the proper target NF(s) to collect the required dataset corresponding to the features and the Member UEs. It then triggers the local training/inference operation by referring to the KPIs.
5GC
AF collects the intermediate data or inference results to perform the training/inference aggregation to derive the QoE. AF may trigger another round of FL operation.
AF
None
NF selection and performing local training (e.g. at NWDAF) by referring to the specified KPI. UE’s local training is at application layer.
3”
3
QoE = f(KPI1(QoS1), KPI2(QoS2), …, KPIn(QoSn))
KPI => QoE (KQI)

## Slide 6: Benefits for VFL support For QoE Prediction
Enable QoE prediction with minimum system impacts without any UE impact based on the existing 5GC mechanism
Provide privacy for both AF and 5GC w.r.t. their training data, label and training model

## Slide 7
VFL Use Case#2: Leveraging Intra-5GC VFL to support Signaling Storm
Local Model
Local Model
Local Model

## Slide 8: 5G Core SBA Architecture w.r.t. NWDAF
RAN
NWDAF
PCF
NRF
UDM
NEF
AF
AUSF
AMF
SMF
NCACF
UPF
UE
DNN
NWDAF SBA Support
5G Core Network Interface
Reference to 3GPP TS 23.288 ….

## Slide 9: Today NWDAF Supports for Horizontal Federated Learning
Sending encrypted gradients, no raw data
Secure aggregation
Sending back model updates
Updating models
Federated learning among multiple NWDAFs is a machine learning technique in core network that trains an ML Model across multiple decentralized entities holding local data set, without exchanging/sharing local data set. This approach stands in contrast to traditional centralized machine learning techniques where all the local datasets are uploaded to one server, thus allowing to address critical issues such as data privacy, data security, data access rights.
NOTE 1: Horizontal Federated Learning is supported among multiple NWDAFs, which means the local data set in different FL client NWDAFs have the same feature space for different samples (e.g. UE IDs).
For Federated Learning supported by multiple NWDAFs containing MTLF, there is one NWDAF containing MTLF acting as FL server (called FL server NWDAF for short) and multiple NWDAFs containing MTLF acting as FL client (called FL client NWDAF for short), the main functionality includes:
FL server NWDAF:
- discovers and selects FL client NWDAFs to participant in an FL procedure
- requests FL client NWDAFs to do local model training and to report local model information.
- generates global ML model by aggregating local model information from FL client NWDAFs.
- sends the global ML model back to FL client NWDAFs and repeats training iteration if needed.
FL client NWDAF:
- locally trains ML model that tasked by the FL server NWDAF with the available local data set, which includes the data that is not allowed to share with others due to e.g. data privacy, data security, data access rights.
- reports the trained local ML model information to the FL server NWDAF.
- receives the global ML model feedback from FL server NWDAF and repeats training iteration if needed.
FL server NWDAF or FL client NWDAF register to NRF with their FL capability information as described in clause 5.2.
According to 3GPP TS 23.288, clause 5.3 ….
Basic Architecture Framework for Federated Learning is supported in TODAY 5G Core

## Slide 10: Why Vertical Federated Learning (VFL) Within 5G Core?
Automate Network Operation & Management
    By enabling collaborative distributed ML in the FL client to be trained using the local data for the target 5G Core network functions, it facilitates NWDAF to assist more adaptive and proactive closed loop network operation and management to authorized data consumers (i.e. NFs). As a result, it simplifies network configuration to perform network optimization and troubleshooting.
Enhance Accuracy on Data Analytics
Accurate analytics requires extensive time and statistic for data collection to derive the reliable predictions. With the support of the collaborative distributed ML in the FL client to be trained with the local data for the relevant target 5G Core network functions stringent the quality of statistics collections to be used by NWDAF for network performance predictions.
Heighten Data Privacy and Integrity Protections
With the collaborated distributed ML in the FL client on the local data, it enhances NF data localization to be limited for the local training/inference operation. Only the encrypted gradients/intermediate data to be shared with the FL server, it heighten the privacy and integrity protections for the local data.
Expedite Training and Analytics Performance
The collaborative distributed ML in FL client on the local data offers divide-and-conquer tactic to accelerate the learning pace overall which in turn allows the NWDAF to present accurate analytics to consumers more efficiently and promptly.

## Slide 11: Use Cases & Differences Between HFL & VFL Initiated by NWDAF
SMF1
NWDAF Server
SMF2
SMF3
SMFn
AMF
NWDAF Server
SMF
PCF
UPF
UEn
UEn
UE1
UE3
UE2
UE1
. . .
UEn
UE1
. . .
UEn
UE1
. . .
UEn
UE1
. . .
Use Case: Connection establishment performance for specific AoI => Leveraging Horizontal FL
Use Case: Signaling Storm Detection & Source of Isolation => Leveraging Vertical FL
UE1
UE3
UE3
UEn
DL: Model download/update, weight factor etc.
Model download, aggregate intermedia data and update the “Global” model before updating/sending the local model to SMFs
UL: Intermediate data update.
SMFx receives the local model from NWDAF, performs the training/inference with the local data set. SMFx sends the intermediate data to NWDAF for aggregation.
DL: Download the “initial” local model to different NFs, indicate the loss status
Download initial model to different NFs and specify the required features to NFs. Send the loss status to NFs after processing the intermediate data
UL: Intermediate data update.
NFx receives the initial model from NWDAF, performs the training/inference with the local data set. NFx updates its local model based on the loss status.
Area Of Interest (AoI)
NWDAF Client
NWDAF Client
NWDAF Client
NWDAF Client
NWDAF Client
NWDAF Client
NWDAF Client
NWDAF Client
NOTE:
Whether the NWDAF client imbedded into the NF or being standalone is implementation decision and is not subject to be standardized.
In case of standalone NWDAF client, it may serve more than a NF instance and it is local implementation decision and not subject to be standardized.

## Slide 12: Benefits for VFL support For Signaling Storm Prediction
Simplify Multi-vendor training model and training data interoperability
  Different NFs from different vendors would have their own specific implementation which could impact the design of the training mode and dataset. Leveraging VFL requires only the coordination of the training output across vendors’ NFs.
Significant reductions of the signaling traffic for AI/ML training and inference operation (compared against NWDAF direct collection of the raw data from 5GC NFs)
Provide privacy for local training data and training model
Furthermore, the above benefits are not limited to the signaling storm prediction. Many other analytics also benefit from VFL

## Slide 13: Conclusions
The mechanism and the benefits of VFL to support distributed collaborative learning have been well studied by many researchers. This presentation further demonstrates how to leverage the VFL approach to enable efficient and effective signaling storm and QoE prediction.
One should recognize the valuable 5GC feature for supporting VFL distributed collaborative learning feature in 5G system in Rel-19 in order provide a more robust and reliable 5G advanced system.

## Slide 14: Backup Slide

## Slide 15: Algorithm of Vertical Federated Learning
In a VFL system, K data owners collaboratively train a machine learning model while keeping their respective private data {D1, ...DK} local. We use D = D1 ∪ ... ∪ DK to denote the collection of their data. We further denote the features space as X , the label space as Y, and sample ID space as I. Thus, Dk , (Xk, Yk, Ik) is the dataset owned by party k.
After the feature alignment, participating parties can start training the VFL model using the aligned samples. The most common training protocol is using gradient descent, which requires parties to transmit local model outputs and corresponding gradients instead of local data. Algorithm 1 describes a general VFL training procedure based on neural networks using stochastic gradient descent (SGD). Specifically, each party k computes its local model output Hk = Gi(xk, θk) on a mini-batch of samples x and sends Hk to the active party.
With all the {Hk} K k=1, the active party computes the training loss following Eq. (4). Then, the active party computes the gradients ∂/∂ψK of its Hosting module and updates its Hosting module using ∂/∂ψK . Next, the active party computes the gradients ∂`/∂Hk for each party and transmits them back. Finally, each party k computes the gradient of its local model θk as follows:
and updates its local model. This procedure iterates until convergence.

## Slide 16: How NWDAF Supports VFL Distributed Collaborative Training?
1.The client NWDAF associated with a particular NF will register with NRF for its client NWDAF service to support the training of the ML model on local data for the given VFL service-X (i.e. supporting specific target feature(s) for the given ML training)
2. Server NWDAF discovers Client NWDAF for particular NF which supports the VFL service-X via NRF
NOTE: More than one NF instances of the same NF type can be served by the “same” Client NWDAF to support the VFL service-X which has access to the NF’s local data to support the local training
3-5 Server NWDAF requests confirmation from Client NWDAF for its intent for initiating VFL service-X training/inference operation and the Client NWDAF could be selected to participate in the training/inference operation. Client NWDAF ensures its feasibility (e.g. feature alignment to support the target function for training with its local data, operation condition etc.) before responding to the Server NWDAF.
6. Server NWDAF selects the target client NWDAF(s) to participate in the VFL service-X training/inference.
NOTE: The client NWDAF selection determination can refer to 3GPP TS 23.288 clause 6.2.c
7a. Server NWDAF sends the initial model to be referred for the local training to the requested Client NWDAF.
7b.Server NWDAF provision the model descriptor to the different Client NWDAF to trigger the VFL in case of the model is already configured in the local NWDAF client.
8. Client NWDAF continues to provide Server NWDAF the intermediate data while training the local model for VFL service-X. In response, the Server NWDAF provides the intermediate training loss to the Client NWDAF. The local training continues until pre-defined epoch number or an accuracy condition is reached.
9. Server NWDAF informs Client NWDAF about the completion of the model training.
Server
NWDAF
Client
NWDAF
NF
NRF
1. Registration to support VFL service-X
2. Discover Client NWDAF-Y for NF-Y to support VFL service-X
3. Request to support VFL service-X
5. Response for VFL service-X
7. Model initialization to each discovered NF for VFL service-X
6. Selecting Client NWDAF for VFL service-X training/inference
8. Client NWDAF updates Server NWDAF of the intermediate data while training the local model for VFL service-X and receives the training loss update until epoch number or accuracy condition is reached.
4. Feature(s) alignment for VFL service
9. model training completion Indication
Local Training Operation

## Slide 17: How VFL Distributed Collaborative Learning Support Signaling Storm Detection?
Example on how to apply VFL Distributed Collaborative Learning to support automatic Signaling Storm Detection and Mitigation
Server
NWDAF
Client
NWDAF
NF
UE
Connection Establishment Request
NF: AMF, SMF, UPF, PCF, AUSF etc.
Establish VFL training with target NFs corresponding to Connection Establishment Requests for UEs at target AoI/DNAI
Through the training, building/adjusting the KPI profile for Mobility signaling storm detection by tuning the threshold and anomaly metric for signaling storm detection algorithm’s parameters based on historical data set of the group of UEs
Trigger Signaling storm analytics
Predict anomaly based on prior KPI profile
Trigger Policy Update to specific target NF(s)
Training Phase
Inference Phase
A boom in various extreme mobility scenarios, such as the high-speed rails during rush hours and unexpected network failure could trigger signaling storm. The example figure on the right demonstrates how to leverage the VFL collaborative distributed training with NWDAF to detect and to mitigate the signaling storm caused by unexpected mobility failure.
The sequence can be divided into two phases: i.e. Training Phase & Inference Phase.
The objective of the training phase is to build the KPI profile for each 5GC NF (e.g. AMF, SMF, UPF etc.) which is involved in the Connection Establishment operation via their historically collected local data for a group of UEs. Within this phase, tuning the detection algorithm’s parameters are used to adjust the threshold for anomaly metric for signaling storm detection.
The objective of the inference phase is to predict the signaling storm which could be happened for a period according to the KPI profile which was determined during the training phase. Consequently, the pre-defined policy would be triggered to update the target NF(s) and the corresponding connection establishment request which may be either accepted or rejected dependent on the policy to avoid signaling storm.
NOTE: In case the signaling storm detection is focusing on the NG-RAN, the NWDAF can coordinate with MDAF to detect signaling storm in RAN.
Connection Establishment Request
Connection Establishment Accept/Reject

## Slide 18: EXAMPLE of KPI/KQI Video Streaming Service Relationship
SERVICE KPI
(KQIs)
Accessibility
Retainability
Throughput
Integrity
Jitter
PLR
Cell
Availability
Mobility
Resource
Utilization
Delay
Network KPI
(3GPP TS 32.450, TS 32.455)
CONNECT TIME
(Session Setup)
AVAILABILITY
(Session Active)
VIDEO/AUDIO
QUALITY
(Session Active)
RESPONSE TIME
(Session Active)

## Slide 19: EXAMPLE of KPI/KQI Voice Service Relationship
SERVICE KPI
(KQIs)
Accessibility
Retainability
Throughput
Integrity
Jitter
PLR
Cell
Availability
Mobility
Resource
Utilization
Latency
Network KPI
(3GPP TS 32.450, TS 32.455)
SERVICE
AVAILABILITY
SPEECH
QUALITY
(MOS)
END TO END
DELAY
SIR