## Slide 1: Remote UE accessing services provided by PIN (RUASP)
Huawei, HiSilicon

## Slide 2: Use Cases - Overview
Use Cases :
Case1：ToB, mobile office case
Case2: ToH, IoT devices in smart home , e.g. Network Attached Storage (NAS), home security device, VR/XR device, etc.
Use Cases for RUASP:
toB：For the remote UE, i.e. the employee’ UE outside the office, it can communicate with the office equipment located in his private network no matter where the user is, in order to support mobile office.
toH：IoT devices or non-3GPP devices (e.g. NAS server, smart home security device, XR/VR terminal, etc) are connected to 5GC via residential Gateway which supports cellular or wireline access. The mobile phone outside the home network (i.e. remote UE) may be authorized to access these IoT devices or non-3GPP devices when needed.

## Slide 3: Problem and existing solution
Problem description, taking toH case as an example:
For the security and limited number of IPv4 addresses issue, the IoT devices in smart home will use the private IP address, which may be allocated by residential gateway (e.g. PEGC) or by 5GC, or firewall will be deployed in the network side. Therefore, the UE cannot connect the devices behind the NAT directly when the UE is in the offsite area (called remote UE).
NAT type as defined by RFC 3489 includes four types, full cone, restricted cone, port restricted cone, and symmetric, the success rate of NAT traversal based on the STUN technology (RFC 5389) is about 50% to 80%.
Existing solution to solve the NAT issue:
The common solution in the industry is to deploy the relay node in the network side (e.g. in public cloud) to fully solve the NAT traversal issue. However, there are some disadvantages for this solution, to see the details in the next slide.
Existing solution based on the relay node
NAT traversal failure

## Slide 4: Requirement
The disadvantages for the existing solution (Red path) as below:
Issue1： High cost of relay node deployment, especially for the high bandwidth service, e.g. NAS service, home monitoring.
Issue2：The inferior path that cost wastes of resources; Shared transport link affects service experience.
Issue3: Security risks for privacy disclosure.
Requirement: To overcome the above disadvantage for the relay-based solution and bring new revenue to the operators, a non-OTT based solution needs to be defined by 5GC (Green path).

## Slide 5: PIN solution in R18
Excerpts from subclause 5.5 of TR 22.895: When considering the gateway with 5G capability for accessing 5G services, it is important to enable the support of the secure connectivity for allowing authorized users from anywhere in the world to access authorized services provided by these IoT devices or none-3GPP devices in terms of user authentication and authorization.
Traffic routing requirement from Stage 1:
Traffic routing for PIN as defined in TS 23.501 Annex P.2:
- For PIN indirect communication N19-based traffic forwarding is not used i.e. the PIN traffic is forwarded using:
- N6-based traffic forwarding method, where the UL/DL traffic for the PIN communication is forwarded to/from the DN;
- local switching as depicted in Figure P.2-1 below, following the principles of local switching of traffic for 5G VN LAN-type service.
To solve the NAT issue, the N6-based solution (e.g. a relay node deployed in the public cloud) can be applied, but its disadvantages are obvious, as mentioned in page 4.
Another way to solve the NAT issue is to establish the cross-domain tunnel between UPFs, but the N19-based solution cannot be used for PIN, because:
  The remote UE can be in any place, the statically configured N19 tunnel cannot satisfy the mobility requirement.
  As the PIN group is per user, the tunnel is only used by a single remote UE, not like N19 established for all the UEs in 5GLAN group.
Analysis
Observation:
  To sum up, N6-based and N19-based solution are not good for PIN traffic routing.

## Slide 6: Gap
What is already defined for PIN?
What is missing?
5G VN group management is reused by PIN, so there is a group subscription data for PIN group in UDM.
Local-switch based user plane is supported by PIN, and dedicated DNN and S-NSSAI is allocated to each PIN.
PEGC/UE can establish PDU session for the PIN based on URSP.
Table 5.2.3.3.1-2: Group Subscription data types
Figure P.2-1: Local-switch based user plane architecture for PIN
  It is not supported how a remote UE can efficiently access the PIN services, based on local switching mechanism.
  NOTE: Considering the PIN group is per user, it is impractical to configure the static SMF information in NRF for PIN related DNN and S-NSSAI.

## Slide 7: Objective
5G CPE/PEGC registers to the 5GC and establishes the PDU session for the dedicated DNN and S-NSSAI for a PIN. The UDM stores the SMF information in the Group Subscription data for the PIN.
Remote UE registers to the 5GC and establishes the PDU session for the same DNN and S-NSSAI as 5G CPE.
AMF obtains the SMF information from UDM for the PIN, and selects the same SMF to serve the remote UE. If it cannot establish the direct connection to the target SMF, then the I-SMF is allocated.
The Remote UE and the 5G CPE connect to the same SMF and UPF, then the local switching is applied to route the traffic between the remote UE and the 5G CPE.
  Objective: Enhance the 5GC to support selection of the same SMF and UPF for PIN related PDU sessions, so that local switching can be used for remote UE accessing PIN services.

## Slide 8: WID Summary
Main objective of this TEI19 is to enhance the 5G System to support remote UE accessing services provided by PIN.
To support the remote UE, i.e. the UE outside the campus/home, to communicate with the PIN element behind the PEGC (e.g. residential Gateway located in the campus/home) via 5GC, the following enhancements are needed:
  In the Group Subscription data for PIN, the SMF information (i.e. SMF IP Address and SMF NF Id) is stored. This SMF information identifies the SMF applied by the PEGC for the PIN related PDU session, and this PEGC is treated as the primary PEGC in the PIN.
  In the UE Subscription data, the SMF selection subscription data is extended to include the Internal Group Identifier for the PIN which indicates to obtain the SMF information from this Group Subscription data. Then the AMF can select this SMF as retrieved from the UDM. A indication is introduced to indicate that this PEGC’s SMF information is used for all UEs/PEGCs for this PIN.
  NOTE 1: I-SMF is needed if the AMF cannot directly connect to the selected SMF, i.e. ETSUN mechanism can be reused to support this case.
  For the PIN related DNN and S-NSSAI, the SMF selects the same PSA UPF for all the UEs/PEGCs belonging to the same PIN.
This TEI19_WID requires 1 TU.
Impacted specifications include TS 23.501 and TS23.502