## Slide 1: SoH on PDU Set handling for UL
China Mobile, Tencent
S2-2313370
TSG SA2#160,
Nov, 2023, Chicago

## Slide 2: PDU set handling for UL
Editor's note: [XRM] The applicability and details of supporting PDU Set handling in uplink direction may be updated based on RAN WG's progress.
As a key feature in R18, PDU set handling for DL enables differentiated handling for efficient resource scheduling. It is esstential to introduce PDU Set handling for UL to achieve the complete end-to-end mechanism of PDU set handling for XR services.
RAN2/3 and CT1 have sent LSs to SA2 for PDU set UL handling. The XR awareness has been agreed in RAN2, which needs SA2 to define related parameters for RAN and UE:
  “RAN2 assumes that PDU Set based parameters and PDU Set related information may be used for better support of XR services. RAN2 can consider both UL and DL directions.” in [R2-2209215]
  “RAN2 has also agreed that the UE needs to be able to identify PDU Sets / Bursts but that in-band marking of PDUs in the uplink over Uu (the equivalent of downlink marking in GTP headers) is not needed.” in [R2-2213225]
  “RAN2 considers that the PDU set concept is applicable to both UL and DL.” in [R2-2302010]
9.12.2 | S2-2311953 | LS In | Action | LS from CT WG1: LS on uplink PDU Set | CT WG1 (C1-237936) | Rel-18 | XRM
9.12.2 | S2-2311967 | LS In | Action | LS from RAN WG3: Provisioning separate DL and UL PDU Set QoS Parameters to NG-RAN | RAN WG3 (R3-235890) | Rel-18 | NR_XR_enh-Core
9.12.2 | S2-2311981 | LS In | Action | LS from RAN WG2: LS on XR awareness | RAN WG2 (R2-2311590) | Rel-18 | NR_XR_enh-Core
Observation 1: RAN has decided PDU Set handling is applicable to both UL and DL. Therefore, SA2 should consider to support the PDU Set handling for UL in Rel-18, and if needed, define associated parameters for NG-RAN and/or UE.

## Slide 3
Tdoc | Company | Main Content
S2-2313144 | China Mobile | 1)UE reporting capability indication to 5GC in SM capability; 2)SMF may include the Protocol Description in the QoS rule provided to the UE
S2-2312363 | MTK | NOTE 2:For the uplink direction, the identification of PDU Sets is left to UE implementation. The protocol description may be communicated to the UE by the application client
S2-2312032 | Qualcomm | 1)UE indicates support of RTP header extension-based UL PDU Set QoS enforcement in the 5GSM Capability. 2)SMF may include the Protocol Description in the QoS rule provided to the UE 3) a UE that has indicated support of RTP header extension-based UL PDU Set QoS enforcement receives a QoS rule with Protocol Description shall start detecting PDU Sets based on the Protocol Description for the traffic matching the Packet Filter Set of the QoS rule
S2-2312952 | Huawei | 1)SMF optionally provides Protocol Description together with the QoS rule to the UE NOTE: How the UE deals with the Protocol Description is up to UE implementation.
S2-2312094 | vivo | NOTE 3:The UL PDU Set Identification is optional feature for a UE. Whether and how to identify the PDU Set Information in UL direction is left to UE implementation. When the PSDB/PSER/PSIHI can be used for UL
S2-2312749 | OPPO | 1)SMF provides PDU Set UL Identification Indication to UE in the QoS rule, which is used to activate the PDU Set identification in the UE for the uplink direction of the QoS Flow
S2-2310244 S2-2312695 | Samsung | When PDU Set Parameters are applied for the QoS flow, UE uses the same UE derived QoS rule for all PDUs of a PDU Set or UE identify the PDU set follow RAN specification i.e. How the UE determines PDU Set information is UE implementation specific.
S2-2313179 S2-2313185 | Nokia | 1) PDU Set Handling indication from UE. 2)SMF provides the PDU Set QoS Parameters and Protocol Description (if available) together with the QoS rule to the UE that the UE shall the Protocol Description use for PDU Set identification and PDU Set handling on UE Or Only remove the EN
S2-2312105 | CATT | The QoS Flow level QoS parameters signalled to the UE may include the PDU Set QoS Parameters described in this clause (see clause 5.7.1.5).

## Slide 4: 5GC assisted information for PDU set UL handling in UE
Background: In the uplink, the UE may identify PDU Sets dynamically, How this is done is left up to UE implementation.
Question: Whether in R18, the SMF may send Protocol Description associated with the QoS rule to UE to assist the identification of the PDU set for UL
NOTE: The use or not of the Protocol Description is left to UE implementation
Yes: (S2-2313371)
No:
Notes: 标红项需确认