## Slide 1: Comparison of Proposals for NF selection in target PLMN
Ericsson(see S2-2402321) and Nokia (see S2-2402981 and S2-2402982)

## Slide 2: Common Target: Target PLMN should be able to use indirect communication (models C or D) with SCP in target PLMN performing NF selection (e.g. based on load, capacity)
Different Communication Models possibel in different PLMN (see Annex E in TS 23.501)

## Slide 3: Common Target: NF selection in Target PLMN Indirect communication with SCP in target PLMN
SEPP
SEPP
Source PLMN
Target PLMN
Network:
Any communication model
(direct, indirect with/without delegated discovery)
SCP(s)
(with/without delegated discovery,
For inbound requests)
Request
sbi-discovery-*
(WITH del. disc)
Request
sbi-discovery-*
(WITH del. disc)
To target or to
Intermediate SCP
  For Model D, the source PLMN does not need to obtain the NF profiles from target PLMN
  For Model C, the NFp profiles are required in the source PLMN to performed initial selection

## Slide 4: Nokia proposal (S2-2402981 and S2-2402982)
Based on operator's policy and support of related capabilities indicated by the NRF in the local PLMN, the NRF in the remote PLMN may return an indication that indirect communication with delegated discovery with NF (re)selection at target PLMN (Model D in Annex E with SCP in target PLMN doing NF (re)selection) and/or indirect communication without delegated discovery with NF (re)selection at target PLMN (Model C in Annex E with SCP in target PLMN doing NF (re)selection) is requested and for delegated discovery in target PLMN omit NF profiles .
Based on operator’s policy and configuration, the NRF in the local PLMN may also determine without interaction with the NRF in the remote PLMN that indirect communication with delegated discovery with NF (re)selection at target PLMN is requested for communication for that remote PLMN.
Request for NF selection in target PLMN is propagated from NRF in local PLMN to NF consumer or SCP in local PLMN.
The service request is sent to an SCP in target PLMN with appropriate discovery headers, and that SCP performs NF (re)selection.

## Slide 5: Ericsson proposal (S2-2402321)
Inter-PLMN delegation capabilities are config in target SEPP, are provided to the source SEPP
WITH delegated discovery
WITHOUT delegated discovery
Source SCP gets inter-PLMN delegation capabilities from Source SEPP
Source SCP determines whether delegation should be done to the target PLMN, based on the Target PLMN delegation capabilities.
With delegated discovery: if delegation is possible, then the source SCP does not perform NRF discovery but forwards the request to the target network where initial selection and reselection is performed
Without delegated discovery: if delegation is possible, the source NF needs to performs initial selection anyway (then NRF discovery is required). The source SCP forwards the request with target NF instance or NF Set or both, and therefore initial selection or reselection is delegated to the target PLMN.

## Slide 6: Comparison of impacts
 | Ericsson | Nokia
SEPP impacted | YES New service proposed (to be defined in SA2 since this is related to signalling routing not to security) New interaction SEPP-SEPP | NO
NRF impacted | NO | YES New parameters in NRF Discovery request and response
Source NRF to target NRF communication required (if delegation to target is applicable) | YES (for Model C, to obatin NF profiles) NO (for Model D) | If option to configure source NRF is used for model D : NO Otherwise: YES (see Discussion point 2)
Source NRF to target NRF communication required (if delegation to target is NOT applicable) | YES | YES
New configuration required | Target SEPP (SCP does not need to be configured, but functionality is enabled per PLMN with enhanced SCPs) | If option to configure source NRF is used: Source NRF Otherwise: Target NRF (see Discussion point 2)
Behavior if new capabilities are not supported | Fallback to existing behavior with NF selection in source PLMN (How source SEPP can determine that target SEPP does not support new interaction is still beeing invetigated) | Fallback to existing behavior with NF selection in source PLMN

## Slide 7: Discussion point 1: For Communication Model B in source PLMN: Should NF consumers support delegated (re)selection in target PLMN Communication?
  Currently included as option in Nokia proposal and excluded in Ericsson proposal, but both proposals could be adjusted.
  Pro: Enables support of deployments with Communication Model B in source PLMN
  Con: Updates of NF consumer required for requests to other PLMN:
  Determine target PLMN requirements for indirect commincation (via NRF or SEPP)
  Supply appropriate information (e.g. discovery headers) in request to enable indirect communication
 | Ericsson | Nokia
NFc is impacted | YES NF gets Inter-PLMN capability from SEPP | YES NF discovery via NRF is impacted

## Slide 8: Discussion point 2: Negotiation of communication model between Source and Target PLMN or configuration in source PLMN?
Currently both variants included as options in Nokia proposal and negotiation assumed in Ericsson proposal, but both proposals could be adjusted.
Pro Negotiation: More flexibility in negotiation and possibly less configuration (if different target PLMNs have different requirements about NF selection)
Pro Configuration in source PLMN: Less Inter-PLMN procedures (might be sufficient should operator community agree on communication model applicable for inter-PLMN communication)