## Slide 1: FS_AIML_CN KI#3 summary & potential way forward proposal
vivo (Rapporteur) MediaTek Inc. (Rapporteur)

## Slide 2: KI#3: NWDAF-assisted policy control and QoS enhancement
 | Alt a: Assistance information in NWDAF | Alt b: Recommendation in NWDAF | Alt c: Reinforcement Learning in PCF | Alt d: PDU set assistance via NWDAF
Goal | Assist PCF in QoS determination and modification of QoS parameters | recommend the action that could be taken by the PCF directly | Provide NW state and reward to PCF to learn appropriate actions | Assist PCF in determination of default PDU set QoS parameeters
Output | One or multiple set(s) of candidate QoS parameters | Recommended QoS parameters combination(s) | NW state (e.g. slice load, NW performance, OSE) | (Enhanced) exisiting analytics (e.g. DN performance) to provide average/ maximum packet delay per PDU set or average packet loss per PDU set in form of statistics or predictions.
 | A combination of (enhanced) existing analytics (e.g. finer granularity QoS KPI, traffic characteristics) |  |  | 
 |  |  | Reward (the Reward of the action applied by the PCF) | 
 | Duration and number of usages of QoS Flow |  |  | 
Service | Enhance existing service or new service (FFS) | New service (new logical function) | New service ? | Enhance existing service (s)
Entity | NWDAF (containing AnLF) | a new logical function (e.g. ReLF) | NWDAF or PCF? | NWDAF (FFS)
Observation:
  NWDAF shall not be aware of PCF internal logic regardless which alternative(s) is selected
  It looks more time needed for KI#3, especially Recommendation/Reinforcement Learning in PCF to help interested companies better understand the solutions

## Slide 3: KI#3: NWDAF-assisted policy control and QoS enhancement
4 alternative solutions on the table:
  Alt a: enhance NWDAF existing service (or new service) to provide assistance information for PCF's determination of QoS policy.
  Alt b: In addition to MTLF/AnLF, a new logical function(or new service) is introduced to recommend QoS parameters to PCF.
  Alt c: NWDAF new service to provide NW state and reward to PCF to learn appropriate actions
  Alt d: enhance NWDAF existing services to provide PDU set assistance information for PCF
Way forward:
  NWDAF shall not be aware of PCF internal logic regardless which alternative(s) is selected
  Regarding Alt a and and Alt d , it looks we may conclude the following:
    A combination of (enhanced) existing analytics that are valid during the same validity period, including the Observed service experience, QoS sustainability, UE Communication, Network Performance analytics
    Whether and how to provide PDU set assistance for XRM-service is FFS.
  Alt b, Alt c need more time. However it seems the following part could have a chance to be concluded
    The PCF may send request to NWDAF, including one or multiple sets of QoS parameters, target QoE/ service experience/performance information of a service, etc.
    NWDAF may include one or multiple set(s) of candidate QoS parameters associated with the corresponding priorities and predicted target QoE/ service experience/performance information.
    It is FFS whether to introduce new service or reuse existing service for providing candidate QoS.

## Slide 4: BACKUP