## Slide 1: Way Forward for FS_5G_ProSe_ph3 Open Issues
AT&T (Rapporteur)
S2-2407106

## Slide 2: Open Issue for KI#1
Per first round of NWM discussion, most companies agreed to use solutions 1, 2 and 7 to derive the common solution principles for KI#1, e.g., inclusion of the hop-count in discovery message, the configuration of a Hop-Limit in the Intermediate Relay, U2N Relay and Remote UEs, End-to-End QoS handling.
Second round of NWM was focusing on the one key difference between the solutions (solution 1 vs solutions 2&7), 14 feedback received, 7 companies support discovery mechanism defined in solution 1 and 7 companies support the discovery mechanism defined in solutions 2 & 7.
Open issue: Should the remote UE select (be aware of) the end to end path or the remote UE just select the immediate Intermediate Relay?
Way forward:
  For Model A discovery & link setup/management, we follow solution 1;
  For Model B discovery & link setup/management, we follow solution 2 &7
  How to support the validation of the path and the security aspect of connection setup need further study.

## Slide 3: Open Issue for KI#2
During second round of NWM discussion, 14 feedback received, 8 companies support MANET only solution; 4 companies prefer PC5 based solution for point-to-point communication and ok with MANET based solution for point to multi-point communication; one company prefer PC5 based solution for point-to-point communication however if MANET based solution is selected for point-to-multi-point communication, then it should be MANET for both; one company prefer PC5 based solution.
Open issue: Should we support MANET based solution only or should we support both MANET based solution and PC5 based solution?
Way forward: For IP based network we will develop MANET only based solution in normative phase; for Unstructured and Ethernet type of network will continue to develop PC5 based solution for normative phase.