## Slide 1: Edge_Ph2 Issues related to DNS over TLS and DNS over DTLS Discussion Paper
Sony
S2-2406089

## Slide 2: Background
The UE may indicate in ePCO “DNS server security information indicator” (0x0031h) support for secure DNS and the SMF may respond with different independent alternative DNS server security configuration to the UE with the same ePCO number.
Since SA3 has defined two alternative transports 1) TLS and 2) DTLS in addition to this the UE may indicate which one it supports in another ePCO “DNS server security protocol support” (0x0039h) and this ePCO is only allowed from the UE to the network.
The network then provides the DNS server security information based on both these ePCO from the UE.

## Slide 3: Background – ePCO 0031h
24.008 ePCO:
From the UE to SMF:
- 0031H “DNS server security information indicator”
From SMF to UE:
- 0031H “DNS server security information with length of two octets” and one or more sub containers with:
Content ID | Value | Description
00 | Security Protocol | 
 | 00 | TLS (RFC 7858)
 | 01 | DTLS (RFC 8094)
01 | Port Number | RFC 6056
02 | FQDN | RFC 1035
03 | SPKI Pin Set | X 690.3
04 | Root Certificate | X 690.3
05 | Raw Public Key | X 690.3

## Slide 4: Background – ePCO 0039h
24.008 ePCO:
From the UE to SMF:
0039H “DNS server security protocol support” (new from Rel-17)
From SMF to UE:
0039H Not allowed
Content ID | Description
01 | TLS (RFC 7858)
02 | DTLS (RFC 8094)

## Slide 5: Issues 1(2)
Observation 1:
We allow two types of Secure DNS configurations, first which secure DNS protocol to use and second the different alternative security configurations for that protocol. For the first part CT1 has specified how the UE indicates which protocol(s) that is supported. For the second part there is no information from the UE which security mechanism that is supported. However, CT1 has specified how the network send different types of security configuration to the UE without to know what the UE is supporting.
Proposal 1:
Similar to ePCO “DNS server security protocol support” (0039H), we should support that the UE could indicate to the network which security mechanism that is supported since we specify several independent different security mechanisms.
If we later supports additional security mechanisms or secure DNS protocols, then this list could be updated in future releases.

## Slide 6: Issues 2(2)
Observation 2:
23.501 specify how the “UE indicate support of DNS with security” to the network but nothing related to which protocols that is supported. The capability signaling mechanism on how to indicate what is supported is not specified in 23.501 nor in SA3 specifications.
Proposal 2:
Update 23.501 so the capability negotiation mechanism is described in 23.501 or describe that this is defined in the CT specification (24.008).
This could be done in future meeting when the other issue is addressed.