## Slide 1
Ambient IoT Limitations Analysis
SA2#163
Fukuoka, Japan
S2-2406523
May 2024

## Slide 2: Abstract
We present an analysis of AIoT harvesting devices and NW limitations that should be considered when designing an AIoT standard for ultra-low power and low-complexity energy harvesting-based Ambient IoT devices and networks.
Some limitations are not physical or mathematical, but rather some common, current technology features found by our analysis with significance to Ambient IoT devices.
We suggest considering such analysis when choosing between several options for the Ambient IoT standard
S2-2406523

## Slide 3: AIoT Harvesting Device Energy Scheme
The energy scheme of an AIoT harvesting device defines multiple minimum levels for different device operations.
The energy is accumulated when an energy source is available, and the harvesting block is active.
Energy dissipation happens on every operation: Rx, Tx, memory retention, and other functionality, as well as due to device leakage.
The device availability, for Rx or Tx, depends on the device energy level at the required time.
AIoT device charging rate is a function of the energy source, device distance from the source, and tag orientation (polarity), the further the device the slower the charging.
S2-2406523

## Slide 4: Environment where devices harvest energy
Devices that harvest energy are active for communication at different points in time (due to energy dissipation)
If the comm protocol waits for all devices to be active for communication prior to activating the MAC protocol then the MAC protocol is like standard protocols
However, if the comm protocol activates the MAC protocol together with the energizing of the devices then the MAC protocol must take into account, that at a given point in time, not all devices may be active, thus for this case at a given point in time not all devices will participate in medium access. This impacts concepts like explicit grouping and direct targeting of devices as an addressed device may not be active upon addressing
S2-2406523

## Slide 5: Non-Volatile Memory - Solutions
An alternative to retaining memory is the use of non-volatile memory.
One such component is OTP, which allows for a device to write once and then read multiple times.
This component can be integrated into the Si, without the need to increase the complexity of the device.
However, it is basically a one-time write, so multiple writes can be done only a few predetermined times.
Today, MTP (Multiple-time programming) integrated into the Si (on-die) solutions are usually larger and more power expensive.
Adding MTP as external memory will increase the device BOM and complexity significantly.
S2-2406523

## Slide 6: Non-Volatile Memory – Write Operation
An example of a AIoT device transmission of 30us with EIRP=-10dBm:
  The energy spread to the air = 3nJ
  In order to transmit, an actual device's total energy consumption of about 30nJ is reasonable
Our analysis revealed that OTP components can consume as much as 50-500uJ per writing of 32 bits. This is orders of magnitude more energy compared to the energy used by the transmission as seen above.
There are two ways to perform OTP Write:
  Very high current and voltage for a short period
  Moderate current and voltage (they will probably remain relatively high but acceptable for an Ambient device) for a very long time
In a controlled environment (e.g. production line), the write operation is done using the first option above.
Successful NVM Write operation to an AIoT device in the field, with low current and voltage might be very slow, or even impractical.
RRAM NVM is a new promising technology, the energy/bit is scaling to 1pJ [2] [3] .
Write operation of ~1kbit of NVM + overhead of operation is achievable in ~nJ range.
* No offering exists yet, but it is doable and can be made in the future.
S2-2406523

## Slide 7: Impact of Memory Retention
Ambient IoT devices are required to support energy harvesting power delivery.
This means these devices are not always powered on, and most of the time are either powered off or work on the remaining energy from the last energizing
One of the biggest energy-consuming blocks is memory.
While on a dynamic power regime, the memory power consumption is comparable to the rest of the circuitry operating within the Ambient IoT devices.
But while staying non-active/standby (meaning no transmit or receive) any requirement to retain memory values is energetically expensive - especially if this is required for long times [1].
Various SRAM technologies with low retention power consumption exist, but between 20-200fW/bit are achievable in commercial products.
So, holding 1Kbyte for 1 minute takes 10nJ, which is comparable to the transmission energy as seen in slide 8.
S2-2406523
Notes: fW = 10^-15 W

## Slide 8: Summary
A few possible limitations of Ambient IoT harvesting-based devices and NW were presented:
  The device availability, for Rx or Tx, depends on the device energy level at the required time
  MAC protocol must consider that at a given point in time, not all devices may be active.
  Successful NVM Write operation to an AIoT device in the field, with low current and voltage might be very slow, or even impractical.
  The amount of energy required to hold 1Kbyte for 1 minute is comparable to the transmission energy
We suggest considering these limitations when comparing different options and solutions for adoption in the standard
S2-2406523

## Slide 9: References
  J. Kwong, et al, “A 65 nm sub-Vt microcontroller with integrated SRAM and switched-capacitor DC-DC converter,” in IEEE Int. Solid-State Circuits Conf. (ISSCC) Dig. Tech. Papers, 2008, pp. 318–319.
  C. Cagli et al., "Study of the Energy Consumption Optimization on RRAM Memory Array for SCM Applications," 2017 IEEE International Memory Workshop (IMW), Monterey, CA, USA, 2017, pp. 1-4, doi: 10.1109/IMW.2017.7939106. keywords: {Programming;Energy consumption;Resistance;Memory management;Aging;Hafnium compounds;Random access memory},
  Zahoor, Furqan, Tun Zainal Azni Zulkifli, and Farooq Ahmad Khanday. "Resistive random access memory (RRAM): an overview of materials, switching mechanism, performance, multilevel cell (MLC) storage, modeling, and applications." Nanoscale research letters 15 (2020): 1-26.
S2-2400081