## Slide 1: Discussion on user identity activation for R19 FS_UIA_ARC KI#1
CATT

## Slide 2: User identity activation related Architectural Assumptions
When the user identifier applies to a human, only a single user identifier is active with a UE subscription at a given time and it is assumed that the specific user identifier is associated with all of the UE's traffic during the time that specific user identifier is active with the UE's subscription.
NOTE 2: A user is considered active if the associated user identifier has been authenticated and authorized to use a linked subscription to access the 5GS.
(TR 23.700-32 clause 4.1)

## Slide 3: User identity activation related Architectural Requirements
When the user identifier applies to human, the 5GS should be able to support user authentication for a User Identifier (e.g. when requested by a 3rd party or to identity the current active user for an UE).
(TR 23.700-32 clause 4.2)

## Slide 4: User identity activation related security assumptions
For the human user of the UE:
The user authentication and primary authentication are independent. The user authentication procedure will not impact UE primary authentication procedure.
(TR 33.700-32 clause 4)

## Slide 5: User identity activation by using NAS or not?
If not using NAS (i.e. interactions between the UE and CN), how can the architectural requirement of “support user authentication for a User Identifier” be fulfilled?

## Slide 6: User identity activation using NAS-SM messages?
Since the user (identity) profile is associated with all of the UE’s traffic, it applies per UE, not per PDU Session. Including User Identity in SM messages (e.g. every PDU Session establishment request/accept messages) to activate User Identity/profile is redundant and of low efficiency.
If the user identity activation is performed during SM procedures (e.g. PDU Session establishment procedure), it means that the user identity authentication/authorization is performed during PDU Session establishment. Again, it is redundant to perform user identity authentication/authorization per PDU Session, and it may impact the performance of PDU Session establishment (e.g. prolonged PDU Session establishment time, failure of PDU session establishment if user identity authentication/authorization fails).

## Slide 7: User identity activation using NAS-SM messages? (Cont.)
If the user identity activation is performed during SM procedures (e.g. PDU Session establishment procedure), it is unclear how the existing PDU Session(s) are handled (e.g. when/how to trigger the release of existing PDU Session(s)) as the existing PDU Session(s) and the PDU Session via which the user identity is activated are independent.

## Slide 8: User identity activation using Registration messages?
During initial registration procedure, the UP connection between the UE and AF has not been established yet, i.e. it is possible that no interactions between the UE and AF over application layer has been performed and therefore no user identity available yet. So user identity activation may not be possible during initial registration.
If user identity activation is done during registration update procedure, it means user authentication/authorization procedures are performed during the registration update procedure, which may impact the performance of registration (e.g. prolonged registration time, failure of registration update if user identity authentication/authorization fails).

## Slide 9: User identity activation using Registration messages? (Cont.)
Whether registration update messages or other NAS-MM messages (e.g. new NAS-MM messages) are to be used for user identity activation, may also depend on whether the user identity activation is triggered by the network or the UE.

## Slide 10: Proposal/Conclusion
If NAS messages are to be used for user identity activation:
  Use NAS-MM messages instead of NAS-SM messages.
  Initial registration request message is not supposed to be used.
  Which NAS-MM messages (e.g. registration update messages or new NAS-MM messages) to use needs further discussion and to be determined during normative phase.