## Slide 1: FS_AIML_CN KI#1 summary & potential way forward proposal
vivo (Rapporteur) MediaTek Inc. (Rapporteur)

## Slide 2: KI#1: AI based positioning and existing analytics
 | Existing Analytics | AI based positioning
Goals | To get thing’s statistical patterns or to predict future trends | To get UE location with high accuracy
Type of output | Statistics and prediction based on ML model | Location Calculation based on ML model
Applicable time | Either in past or in future | Current time
Inference/Location calculation entity | AnLF | enhanced LMF or LMF (collocated with enhanced AnLF)
Observation
  AI based positioning is little bit different from the existing analytics which only comprise statistics and predictions.
Two alternative solutions for AI based positioning:
  Alt a: enhanced LMF is to perform Location Calculation based on ML model
  Alt b: LMF(collocated with enhanced AnLF) is to perform Location Calculation based on ML model
Way forward
  LMF determines the location of UE directly using an ML model i.e. calculate location per the trained ML model
  Further discussion about option selection e.g. only Alt a or Alt b or both

## Slide 3: KI#1: Data collection/Model accuracy monitoring
Option 1 (P#1.1): LMF calculating location + LMF model training(i.e. LMF have to support AI computing and big volume data storage)
Option 2 (P#1.2): LMF calculating location + MTLF model training
Option 3 (new): LMF calculating location + OAM model training
Observation
  data collection is the common part for all the options
Way forward
  Further discussion about option selection e.g. only option 1 or only option 2 or both
  Data collection procedures for training model is the common part and need to be specified
    The data for model training, inference and model performance monitoring will be decided by RAN WGs and SA2 will align with RAN WGs and standardize the potential SA2 impact
  Model accuracy monitoring will be concluded in normative phase, taking into consideration related input of RAN WGs.
Note1: Additional optional data that may be collected is UE ID (from AMF), past UE location, positioning methods, LCS QoS (from GMLC), UE trajectory, GNSS info (from AF) and UE speed, UE orientation (from OAM).
 | Option 1 | Option 2 | Option 3(SA5)
Training entity | LMF | MTLF | OAM
Data sources | UE, RAN and PRU | UE, RAN and PRU (via LMF) | UE, RAN and PRU
Data collection for Model training triggered by who | LMF | MTLF | OAM
granularity | Per area (any UE) | Per UE or per area (any UE) | Per area (any UE)
Model accuracy monitoring | LMF | Either LMF or MTLF | OAM

## Slide 4: BACKUP

## Slide 5: KI#1:Data collection for AI based positioning (2/3)
RAN agreement in RAN1-116bis meeting on training data (which could include new measurement data)
RAN agreement in RAN1-116bis meeting on training data sources: (for information)

## Slide 6: KI#1: Data collection for AI based positioning for Option 1 (3/3)
How to initiate data collection for model training by the LMF, since the LMF has no UE ID and no LCS correlation ID from AMF?
Discussion and comparing of different alternatives for LMF Data collection
Note: MTLF triggered data collection for option2 is already captured in TR (e.g. via GMLC/AMF or directly)
New data for AI positioning
Stores data for training
Fig ：Positioning procedure extracted from TS 23.273
Alt 1: data collection based on existing LCS procedure(passive)
Backward compatibility i.e. legacy LMF cannot handle new data for AI positioning
UE and RAN always report new measurements data (developed for AI positioning) without differentiating whether traditional or AI positioning is really performed by NW.
LMF doesn’t initiative data collection but waiting for real LCS service happening;
Alt 2: data collection initiated by the LMF (active)

## Slide 7: KI#1: potential Spec impacts analysis for AI based positioning
 | Option 1 | Option 2 | Option 3(SA5 scope)
Potential SA2 Spec impacts | Extend LMF functional description with AI based positioning, including location calculation, monitoring, model training and data collection for training (e.g. TS 23.237) Call flow of data collection for model training (e.g. TS 23.502) AMF selects LMF for AI pos, if multiple LMFs with different capability deployed in NW (e.g. TS 23.501, 502) | Extend LMF functional description with AI based positioning, including location calculation, monitoring, and data collection for training (e.g. TS 23.237) Call flow of data collection for model training (e.g. TS 23.502) AMF selects LMF for AI pos, if multiple LMFs with different capability deployed in NW (e.g. TS 23.501, 502) Model retrieval from MTLF by LMF(TS 23.288) | SA5 study model training for AI positioning （e.g. how OAM trigger data collection and model sharing with LMF） Coordination between SA2 and SA5
Option 1 (P#1.1): LMF calculating location +LMF model training(i.e. LMF have to support AI computing and big volume data storage )
Option 2 (P#1.2): LMF calculating location +MTLF model training
Option 3 (new): LMF calculating location + OAM model training