## Slide 1: Discussion on the VFL sample and feature alignment
OPPO
S2-2407640

## Slide 2: Current conclusion in the TR 23.700-84
P#2.2: For registration and discovery of VFL entities:
NOTE 1:Whether and how Vendor specific feature information in P#2.2.1 is included will be determined in the normative phase.
P#2.3: For sample alignment for VFL:
NOTE 2: Whether and how the feature alignment is supported will be determined in normative phase.
NOTE 3: The procedure to perform sample alignment is not agreed yet, i.e. it can be done in a standalone procedure or part of the preparation phase, which will be determined in normative phase.
NOTE 4: How NEF assists sample alignment in P#2.3.3 will be determined in normative phase.
NOTE 5: For P#2.3.2 and P#2.3.3, whether and how NEF supports to be involved in generating the intersection of candidate samples is to be discussed in normative phase.
Observation：
Many notes in the conclusion mentioned the sample and feature alignment need further discussion. Since the TU is very limit during the WID phase, a consensus way forward is needed.

## Slide 3: Summary of current status of sample and feature alignment solution
Sample alignment Option1
Sample alignment is separated with the discovery procedure.
Discovery is used to discover the client has VFL capability and supported analytics ID.
Sample alignment is happened before the client collected the data. i.e. Server can check UDM to know the client serving UE list, then determine the final sample set.
Evaluation:
It assumed if the entity serving such UE, then it can collected such UE data. It maybe not always true since based on the user consent, even serving some UE, the UE is not agreed to let client to collect the UE related data.
The logic will be much clear if separated the discovery procedure and the sample alignment procedure.

## Slide 4: Summary of current status of sample and feature alignment solution
Sample alignment Option2
Sample alignment is separated with the discovery procedure. Discovery is used to discovery the client has VFL capability and supported analytics ID.
Sample alignment is happened after the client collected the data. i.e. only the client collected the available data, it can be determined what the exactly sample the client can support.
Evaluation:
It ensured the sample alignment can be performed successfully since all the data is already available.
The problem is that some collected data maybe useless. If the server just select the sub set of the UE for that client as the final sample set.

## Slide 5: Summary of current status of sample and feature alignment solution
Sample alignment Option3
Sample alignment is together with the discovery procedure. i.e. server use one message to do the discovery with the NRF and also with the UDM.(Seems this can only be used when the NEF is involved. NEF help AF to check with NRF and UDM)
Evaluation :
Do not clear if NWDAF is the server, how to use one message to check both NF(NRF and UDM). If for untrusted AF, AF only need to send one preparation request message to NEF. Then NEF can check with UDM and NRF separately. Only one message between the NEF and AF.

## Slide 6: Summary of current status of sample and feature alignment solution
Feature alignment Option 1
No need to specify the feature alignment. It can be assumed that each VFL entity already pre-configured some part of the VFL model. Based on the analytics ID, VFL entity can determine which local model to be used and feature dimension is tightly related to the local model. So if VFL entity can determine the local model, they will know what feature they need to use.
Evaluation :
Model need to be configured to the each entity first.
It is assumed all the UE related feature with such local model can be collected to do the local model training before really collected those data.

## Slide 7: Summary of current status of sample and feature alignment solution
Feature alignment Option 2
Feature alignment is needed. But Feature related info can be register to the NRF i.e. using Feature ID to identify what the feature can be supported by the VFL entity. Then feature alignment is also performed in the discovery procedure. Server get all the feature info supported by the discovered entity and determine which feature is used for which entity.
Evaluation :
It assumed feature is a stable information, not related to the sample. The assumption is not always true since feature is tightly related to the sample.
It need the server to notify the client what the feature will be used.

## Slide 8: Summary of current status of sample and feature alignment solution
Feature alignment Option 3
Feature alignment is needed. Feature related info is a dynamic info and it is tightly related to the sample. Since we usually call it “The feature of the sample” Therefore, only the client collected the available data for both the sample and feature, the feature alignment can be performed. Therefore, sample and feature alignment is performed together after the client collected the available data.
Evaluation :
The sample and feature alignment can be performed together.
It need the negotiate between the server and client. Client based on the collected data to determine what sample and feature it can support. Then send those info to server. Server determine the final sample and feature to be used then notify to client.

## Slide 9: Way forward
Sample alignment and Feature alignment should be separated with the VFL discovery procedure. Sample and Feature alignment will be performed after the VFL discovery.
Sample alignment and feature alignment can be performed together, it is not mandatory to perform the data collection before if the VFL client already has the available data or can determine which sample or feature can support.
Feature alignment is optional.
No feature related info will be registered to the NRF.
Feature alignment need the negotiation between the VFL server and the client. Feature itself is a vender specific information and it can be considered as the part of the ML Model Interoperability Information. No need to specify what the value of the feature.