## Slide 1: S2-2407857 Source: Nokia, Title: KI#2, UDP_Connect from UPF and Questions Document for: Discussion Agenda Item: 19.3 Work Item / Release: FS_XRM Ph2 / Rel-19

## Slide 2
IETF design for draft-ietf-masque-quic-proxy
Slide from IETF 115 for masque-quic-aware-proxying-using-http
VCID Virtual CID(s) are used between the client and the proxy but real CID(s) are used between Proxy and target and within the client towards the actual QUIC layer

## Slide 3
3GPP design when UDP-connect & QUIC-aware-proxying initiated by UPF
Basically when UDP-connect would be initiated by UPF the IETF client is split up between UE and UPF while the Proxy and the target may be merged at AS. See next slide
The issue is that the UPF lacks knowledge that in IETF design is local to the client
See next slide
UE
UPF
AS

## Slide 4
3GPP design when UDP-connect & QUIC-aware-proxying initiated by UPF
UE
Client (UPF)
Proxy
Target (AS)
QUIC Initial
Connect-UDP+ Proxy-QUIC-Forwarding=?1+capsule(REGISTER_CLIENT_CID)+HTTP Datagram(QUIC Initial)
HTTP datagram (QUIC Initial)
200 OK+Proxy-QUIC-Forwarding=?1+Capsule(ACK_CLIENT_CID)
QUIC Initial
QUIC Initial
QUIC Initial
Can the client(UPF) Detects a new QUIC connection ?
Capsule (REGISTER_TARGET_CID)
Can the client (UPF) gather the target CIDs here?
Capsule (ACK_TARGET_CID)
QUIC SH (Target CID)
QUIC SH (Client CID)
QUIC SH (Target CID)
QUIC SH (Client CID)
QUIC SH (Virtual Target CID)
QUIC SH (Virtual Client CID)
Is this mapping of Target CID to Virtual Target CID possible?

## Slide 5
Change of CID during the lifetime of the connection
when UDP-connect & QUIC-aware-proxying initiated by UPF
Text in italics is from draft-ietf-masque-quic-proxy-03
Since QUIC connection IDs are chosen by the receiver, an endpoint needs to communicate its chosen connection IDs to its peer before the peer can start using them. In QUICv1, this is performed using the NEW_CONNECTION_ID frame [which is ciphered thus that UPF can’t detect/understand, hence UPF can’t be aware of new client or server CID].
Prior to informing the target of a new chosen client CID, the client [would need to be UPF] MUST send a REGISTER_CLIENT_CID capsule to the proxy containing the new client CID. [and UPF is unable to do so as the UPF is not aware that a new Client CID has been selected].

## Slide 6
Change of CID during the lifetime of the connection
When UDP-connect & QUIC-aware-proxying initiated by UPF
Text in italics is from draft-ietf-masque-quic-proxy-03
The client can also initiate new REGISTER_CLIENT_CID or REGISTER_TARGET_CID exchanges at any time. UPF is unable to do so as the UPF is not aware that a new Target CID has been selected

## Slide 7
Change of CID during the lifetime of the connection
When UDP-connect & QUIC-aware-proxying initiated by UPF
Analysis
Default behavior (no support of forward mode OR no mapping VCID-CID) is tunneled mode
When AS changes of allocated (=to be received) CID, the UE issues QUIC traffic to the AS address with the new CID. The UPF receives this traffic on the PDU session of the UE and thus it is the traffic of this UE that gets now tunneled (no DoS from another UE). This works but degrades the performances (Tunnel instead of forwarding)
When UE changes of allocated (=to be received) CID, the AS issues DL QUIC traffic to the collocated internal proxy with the new CID allocated to the UE. IF The collocated internal proxy decides to tunnel (should be the default when there is no CID-VCID mapping), the traffic TO UE gets now tunneled. This works but degrades the performances (Tunnel instead of forwarding)
In short going to tunnel mode when AS or UE changes of CID could work (with a change of mode forward --> tunnel on the fly) but degrades strongly the performances
Another question is whether this 3GPP specific deployment would raise Security issues.

## Slide 8
Questions
UPF needs to rely on QUIC initial connect message from to learn Client CID and issue REGISTER_CLIENT_CID?
How UPF can learn target CID? (sniffing the QUIC initial packet received from Proxy=AS)
What happens when new CIDs are assigned by client and target during the life time of the QUIC connection?