## Slide 1: Analysis of SA2-SA5 work split for energy consumption
Qualcomm Incorporated

## Slide 2: Work split between SA2 and SA5 for energy consumption
The following 3 aspects were discussed in the NWM and closely related to the KI#1 conclusion for TR 23.700-66:
  Collection and calculation of User Plane energy consumption
  Exposure of energy consumption to 5GC NF
  Exposure of energy consumption to Application Function
The following granularities were discussed to support for the above 3 aspects:
  Average per UE
  Per specific UE
  Per PDU session of the UE
  Per QoS flow of the UE
  NF
  Network slice
  Renewable energy Info

## Slide 3: Standard status for different granularities
Already supported in SA5 TS 28.554 in Rel-18
  5GC EC (clause 6.7.3.2)
  Network Slice EC (clause 6.7.3.3)
  NG-RAN EC (clause 6.7.3.4)
Not supported in current standard
  Renewable energy consumption for different granularities
  Average per UE
  Per specific UE
  Per PDU session of the UE
  Per QoS flow of the UE
Both the Renewable EC and average per UE need further study in SA5.
Controversial granularities for the work split between SA2 and SA5: per specific UE, per PDU session of the UE and the per QoS flow of the UE.

## Slide 4: Formula of UE related EC
The current common understanding of the UE related Energy Consumption formula
ECx=ECran,x+ ∑ECupf,x,
ECNF,x=*ECNF
Per specific UE,
ECUE=ECran,UE+ ∑ECupf,UE= *Ecran+ ∑ *ECupf
Per PDU session of the UE,
ECPDU=ECran,pdu+ ECupf,pdu= *ECran+ *ECupf
Per QoS flow of the UE,
ECQos=ECran,Qos+ ECupf,Qos= *ECran+ *ECupf

## Slide 5: Formula of UE related EC
A general issue is that currently RAN cannot provide the data volume for specific UEs, PDU sessions or QoS flows.
Another general assumption in this release is
DVran,UE= DVupf,UE

## Slide 6: Parameters in the formula that are already supported by SA5
Per specific UE
  OAM: ECran, , ECupf
  CHF:
    Cell ID served for UE
    for each PDU session,
      UPF ID
Per PDU session of the UE
  OAM: ECran, , ECupf
  CHF: Cell ID served for UE, UPF ID,
per QoS flow of the UE
  OAM: : ECran,, , ECupf
  CHF: Cell ID served for UE, UPF ID,

## Slide 7: Where to perform the calculation
It is obvious that OAM + CHF have all the parameters in the formula for the UE related EC calculation.
Proposal 1: It is proposed that OAM calculates all the granularities that have been discussed in the NWM.
  New impact to SA5: CHF sends the related parameters to OAM for UE related EC calculation.

## Slide 8: How to expose EC information to 5GC
SA5 sent an LS to SA2 regarding network energy related information exposure (S2-2400072).
SA5 has already supported parameter exposure to 5GC NF by using Service Based Management Architecture (SBMA)
Proposal 2: SBMA architecture can be reused by OAM to expose the EC information to 5GC.

## Slide 9: How to expose EC information to AF
It depends on SA5 to determine how to expose data to AF.
It appears that the Exposure Governance Management Function (EGMF) can be used to expose data from OAM to the 3rd party as described in TS 28.533 (to be confirmed by SA5).