## Slide 1: Discussion on Energy Efficiency and Energy Saving
CATT

## Slide 2: Energy Consumption per Network Slice
Estimation & Exposure
  Defined in SA5/OAM. See TS 28.554 clause 6.7.3.3.
  Exposed to the AF (via the NEF), and to other 5GC NFs
  Network exposure mechanism defined in SA2 (see TS 23.502 clause 4.15) can be used.
  Exposed to the AF for charging (see SP-241003)
Use for Energy Saving
  As information for charging of the third party (e.g. network slice tenant/service provider) based on SLA
  AF may use this information to adjust e.g. application specific parameters (e.g. QoS requirements), policies (e.g. influence on traffic routing, guidance on URSP, BDT Policy) that pertain to the Network Slice.
  Other 5GC NFs (e.g. PCF, SMF, AMF) may use this information to make policy decisions, perform SM / MM control, etc., that pertain to the Network Slice.

## Slide 3: Energy Consumption per Network Function
Estimation & Exposure
  Defined in SA5/OAM. Here ECVNF cannot be measured hence is estimated. See TS 28.554 clause 6.7.3.1.
  Exposed within 5GC (i.e. not exposed to external AF)
  Network exposure mechanism defined in SA2 (see TS 23.502 clause 4.15) can be used.
Use for Energy Saving
  5GC NFs (e.g. PCF, SMF) may use this information to make policy decisions (e.g. QoS parameters), adjust UP paths (e.g. selecting/reselecting UPF/DNAI), etc., for the PDU Session(s) and UE(s) (to be) served by the NF.

## Slide 4
Whether it is useful to calculate / expose energy consumption (EC) per UE
  Average energy consumption per UE
    Cannot differentiate the energy consumption between different UEs
    If available, it could be used as another metrics for evaluating EC / EE per network slice, per application/service, per NF, etc.
  Energy consumption per specific UE
    Can differentiate the energy consumption of different UEs
    If available, it can be used for e.g. energy related subscription/application/policy control, UP path selection, per specific UE.
Energy Consumption per UE

## Slide 5: Energy Consumption per specific UE
Estimation & Exposure
  Estimated EC per specific UE in a network slice (or PLMN): Can be estimated using EE of NG-RAN, EE of UPF(s) serving the UE (or EE of eMBB Network Slice, or EE of 5GC), and the data volume of the UE
  Estimated EC per specific UE for an application/service: Can be estimated using EE of NG-RAN, EE of UPF(s) serving the application/service for the UE, and the application/service data volume of the UE
Note 1: For EE of NG-RAN, Network Slice and 5GC, see clause 6.7.1, 6.7.2 and 6.7.4 of TS 28.554.
Note 2: The possible over-consumption of energy by specific UE(s) (e.g. due to located at the edge of the serving cell) is somewhat reflected in the EE of the NG-RAN node.
Note 3: The Estimated EC per specific UE in a network slice/PLMN or for an application/service is related to the NFs (e.g. UPFs) serving the specific UE.
Note 4: Still the Estimated EC per specific UE is (almost) proportional to data volume of the UE. To get more accurate EC per specific UE, coordination with RAN WGs is to be done.

## Slide 6
The management service (defined in SA5, e.g. PerfMetricJob IOC in 28.622) exposes EC/EE information of Network Slice/NF/5GC to a new 5GC NF (defined in SA2, namely EMF).
EMF may estimate the EC per UE (or other granularities, e.g. per PDU Session/QoS flow/application) based on: 1) EC/EE information of Network Slice/NF/5GC; and 2) data volume per UE/PDU Session/QoS flow/application, reported by the UPF/SMF (e.g. User Data Usage events).
EMF exposes the EC/EE per NS/NF, EC per UE (or other granularities) (if available) to other 5GC NFs (e.g. PCF, SMF, AMF, AF (depending on the granularity of EC information)).
5GC NFs performs energy related control (e.g. application/policy/SM/MM control), taking into account the energy related information.
Proposed way forward in Rel-19

## Slide 7
Annex A.1: NWM discussion on SA2/SA5 work split
Proposed conclusion based on the summary of inputs:
SA2 is responsible for collection and calculation of UP energy consumption per specific UE, per PDU Session and per QoS flow (incl. application) granularities.
SA5 is responsible for collection and calculation of UP energy consumption per NF (UPF/gNB) and per network slice granularities.

## Slide 8
Annex A.2: NWM discussion on SA2/SA5 work split
Proposed conclusion based on the summary of inputs:
SA2 is responsible for exposure of energy-related information per specific UE, per PDU Session and per QoS flow (incl. application) granularities to 5GC NF.
SA5 is responsible for exposure of energy-related information per NF (UPF/gNB) and per network slice granularities to 5GC NF.

## Slide 9
Annex A.3: NWM discussion on SA2/SA5 work split
Proposed conclusion based on the summary of inputs:
SA2 is responsible for exposure of energy-related information per specific UE and per Application granularities to the AF.
SA5 is responsible for exposure of energy-related information per network slice to the AF.