## Slide 1
Discussion Paper S2-2407652 – R17 eNS correction - Mapping between NSAGs and S-NSSAIs (August 19 2024)
23.501 5.15.14, 23.501 5.3.4.3.4
When one or more S-NSSAI(s) are associated with NSAG(s), the UE may perform Network Slice based cell reselection and Random Access. If the UE has received NSAG Information from the AMF, the UE shall use the NSAG Information provided by the AMF for cell reselection and Random Access.
A Network Slice AS Group is an identifier of a group of network slices which are associated with it. A Network Slice AS Group association with a group of network slices may be valid in one or more Tracking Areas. An S-NSSAI can be associated with at most one NSAG values for Random Access and at most one NSAG value for Cell Reselection within a Tracking Area (ie one NSAG relates to one or more S-NSSAI(s)x). An S-NSSAI can be associated with different NSAG values in different Tracking Areas.
The NG-RAN provides (and updates) the AMF with the values of the NSAG(s) an S-NSSAI is associated with in a TA using the NG Set Up and RAN Configuration Update procedures (see TS 38.413). The AMF in turn provides this information to the NSSF (29.531 6.2.6.2.3 below (as part of Nnssf_NSSAIAvailability Service API)).
The AMF may, with or without NSSF assistance, configures the UE with NSAG Information for one or more S-NSSAIs in the Configured NSSAI, by including this NSAG Information in the Registration Accept message or the UE Configuration Command message.
The UE determines Random Access configuration among NSAGs that are published in SIB for Random Access and that are associated to the S-NSSAIs triggering the access.
An S-NSSAI can be associated with at most one NSAG values for Random Access and at most one NSAG value for Cell Reselection within a Tracking Area. (23.501 5.15.14)

## Slide 2
Mapping between NSAGs and S-NSSAIs – continue…
23.501 5.15.14, 23.501 5.3.4.3.4 – Zoom on First two bullets - focus on S-NSSAI(s) to NSAG(s) mapping (and vice versa)
When one or more S-NSSAI(s) are associated with NSAG(s), the UE may perform Network Slice based cell reselection and Random Access. If the UE has received NSAG Information from the AMF, the UE shall use the NSAG Information provided by the AMF for cell reselection and Random Access.
A Network Slice AS Group is an identifier of a group of network slices which are associated with it. A Network Slice AS Group association with a group of network slices may be valid in one or more Tracking Areas. An S-NSSAI can be associated with at most one NSAG values for Random Access (RA) and at most one NSAG value for Cell Reselection (CR) within a Tracking Area (ie one NSAG relates to one or more S-NSSAI(s)x). An S-NSSAI can be associated with different NSAG values in different Tracking Areas.
S-NSSAI(s)
NSAG(s)
TAI=1
S1, S2
NSAG100 for CR
NSAG101 for RA
S3, S4
NSAG102 for CR
NSAG101 for RA
S5
NSAG103 for CR
NSAG104 for RA
Say a Requested NSSAI for a UE is S1, S3. UE is in TAI=1.
gNodeB G1 advertised NSAG101 for RA.
gNodeB G2 advertised NSAG104 for RA.
UE can camp on gNodeB G1 since S1 and S3 are mapped to NSAG101 for RA (Random Access).
G1
RAN (G1, G2)
G2

## Slide 3
UE
RAN
NSSF
3
UE camps on a specific RAN node based on match of Requested NSSAI and NSAG advertised by the various gNodeBs (in SIB1)
4
AMF
1
1
Registration req. [Requested NSSAI]
(TS 38.300) Broadcast: SIB1 [NSAG values for Random Access] SIB16 [NSAG value for Cell Reselection ]
(TS 38.413) RAN CONFIG UPDATE [NSAG->S-NSSAI(s) per TA]
2
Nnssf_NSSAIAvailability_Update: [NSAG->S-NSSAI(s) per TA]
Registration req. [Requested NSSAI]
Registration accept [Allowed NSSAI, NSAG->S-NSSAI(s) per TA]
ack
ack
Nnssf_NSSelection req.: [Requested NSSAI]
Nnssf_NSSelection res.: [Allowed NSSAI, NSAG->S-NSSAI(s) per TA]
5
6
7
UE may perform cell reselection based on match of Allowed NSSAI and NSAG advertised by the various gNodeBs (in SIB16).
NOTE: To be able to match Allowed NSSAI against NSAG supported by the cell, the UE uses the mapping of NSAG->S-NSSAI(s) per TA received from the AMF in the Reg. accept.
8
a
NSAG/NSSAI aspects in UE registration procedure (based on 38.300, 38.413, 23.502, 29.531)(RAN3)

## Slide 4
IE/Group Name | Presence | Range | IE type and reference | Semantics description
TAI NSAG Support Item |  | 1..<maxnoofNSAGs> |  | 
>NSAG ID | M |  | INTEGER (0..255, …) | 
>NSAG Slice Support List | M |  | Extended Slice Support List 9.3.1.191 | Indicates the list of slices which belong to the NSAG.
38.413 9.3.1.238 TAI NSAG Support List
This IE contains the slice group mapping for all groups configured at the NG-RAN node per TAI.
IE/Group Name | Presence | Range | IE type and reference | Semantics description
Slice Support Item |  | 1..<maxnoofExtSliceItems> |  | 
>S-NSSAI | M |  | 9.3.1.24 | 
38.413 9.3.1.191 Extended Slice Support List
This IE indicates a list of supported slices.
IE/Group Name | Presence | Range | IE type and reference
SST | M |  | OCTET STRING (SIZE(1))
SD | O |  | OCTET STRING (SIZE(3))
38.413 9.3.1.24 S-NSSAI
This IE indicates the S-NSSAI as defined in TS 23.003 [23].
Mapping of NSAG ID to NSSAI based on 38.413
A problem:
According slide #1 (23.501 5.15.14), An S-NSSAI can be associated with at most one NSAG values for Random Access and at most one NSAG value for Cell Reselection within a Tracking Area.
NGAP protocol (38.413) does not include an NSAG-NSSAI mapping broken down to Random Access NSAG and Cell Reselection NSAG.
Consequentially, AMF does not have a proper mapping of an S-NSSAI to its corresponding NSAG ID for Random Access, and to its corresponding NSAG ID for Cell Reselection NSAG.
Consequentially, AMF does not pass a proper S-NSSAI/NSAG mapping to the NSSF.
Consequentially, NSSF does not pass a proper S-NSSAI/NSAG mapping to the UE.

## Slide 5
Stage 2 - Mapping of NSAG ID to NSSAI based on 23.502
5.2.16.3.2 Nnssf_NSSAIAvailability_Update service operation
Service operation name: Nnssf_NSSAIAvailability_Update
Description: This service operation enables the AMF to update the NSSF with the S-NSSAIs the AMF supports per TA and get the availability of the S-NSSAIs and optionally NSI IDs per TA for the S-NSSAIs the AMF supports.
Inputs, Required: Supported S-NSSAIs per TAI.
The supported S-NSSAIs per TAI is a list of TAIs and for each TAI the S-NSSAIs supported by the AMF.
Inputs, Optional:, Mapping of the Supported S-NSSAIs per TAI to their respective NSAGs.
A list of TAIs and for each TAI a list of S-NSSAIs. For each S-NSSAI in the list – at most one NSAG associated with it for Random Access, and at most one NSAG associated with it for Cell Reselection.
Outputs, Required: A list of TAIs and for each TAI, the S-NSSAIs and optionally NSI IDs supported by the AMF and 5G-AN and authorized by the NSSF for the TAI.
Outputs, Conditional Required: A list of TAIs and for each TAI, the NSAGs authorized by the NSSF for the TAI.
The authorized NSAGs per TAI, is a list of TAIs and for each TAI the authorized NSAGs.
Outputs, Optional: For each TAI, a list of S-NSSAIs restricted per PLMN for the TAI.
5.2.16.2 Nnssf_NSSelection service
5.2.16.2.1 Nnssf_NSSelection_Get service operation
…… Outputs, conditional Optional:
, the NSAG information (defined in clause 5.15.14 of TS 23.501 [2]).
Next slide has a few issues with the above red text

## Slide 6
Stage 2 - Mapping of NSAG ID to NSSAI based on 23.502
Problem #1:
gNodeB G1 and G2 both have advertised NSAGs for RA and NSAGs for CR.
Say a Requested NSSAI for a UE is S1, S3. UE is in TAI=1.
AMF has provided to the UE a many-to-many mapping between NSAGs and the associated S-NSSAIs. The mapping does not indicate whether the mapping is for RA or for CR..
UE now needs to know which gNodeB to camp on (based on Random Access/Cell Reselection Logic).
UE has no idea which gNodeB to camp on, as the NSAG/NSSAI info it has received from the AMF/NSSF was too ambiguous.. Specifically, it was missing the Element of which NSAGs were for RA, and which ones were for CR
Problem #2:
In Nnssf_NSSAIAvailability_Update service operation - Outputs, Conditional Required – why does NSSF returns the NSAGs and the associated S-NSSAIs?? This mapping was just provided to it by the AMF.
All the AMF needs to know is: the NSAGs authorized by the NSSF for the TAI.

## Slide 7
A proposal for fixing NSAG/NSSAI mapping in 23.502
5.2.16.3.2 Nnssf_NSSAIAvailability_Update service operation
Service operation name: Nnssf_NSSAIAvailability_Update
Description: This service operation enables the AMF to update the NSSF with the S-NSSAIs the AMF supports per TA and get the availability of the S-NSSAIs and optionally NSI IDs per TA for the S-NSSAIs the AMF supports.
Inputs, Required: Supported S-NSSAIs per TAI.
The supported S-NSSAIs per TAI, is a list of TAIs and for each TAI the S-NSSAIs supported by the AMF.
Inputs, Optional: Supported NSAGs per TAI, Mapping of the Supported S-NSSAIs per TAI to their respective NSAGs.
A list of TAIs and for each TAI a list of S-NSSAIs. For each S-NSSAI in the list – at most one NSAG associated with it for Random Access, and at most one NSAG associated with it for Cell Reselection.
Outputs, Required: A list of TAIs and for each TAI, the S-NSSAIs and optionally NSI IDs supported by the AMF and 5G-AN and authorized by the NSSF for the TAI.
Outputs, Conditional Required: A list of TAIs and for each TAI, the NSAGs authorized by the NSSF for the TAI.
The authorized NSAGs per TAI, is a list of TAIs and for each TAI the NSAGs and the associated S-NSSAIs. //No need to repeat the mapping
Outputs, Optional: For each TAI, a list of S-NSSAIs restricted per PLMN for the TAI.

## Slide 8
29.531 Table 6.1.6.2.14-1: Definition of type NsagInfo
Attribute name | Data type | P | Cardinality | Description
nsagIds | array(NsagId) | M | 1..N | The list of NSAG IDs, see 3GPP TS 38.413 [21]
snssaiList | array(Snssai) | M | 1..N | This attribute contains the S-NSSAI(s) which are associated with the NSAGs identified by the nsagIds.
taiList | array(Tai) | O | 1..N | This attribute indicates the TA(s) within which the association between the NSAGs identified by the nsagIds and the S-NSSAI(s) is valid. (NOTE)
taiRangeList | array(TaiRange) | O | 1..N | This attribute indicates the TA(s) within which the association between the NSAGs identified by the nsagIds and the S-NSSAI(s) is valid. (NOTE)
NOTE: The absence of both taiList and taiRangeList attributes means the association between the NSAGs identified by the nsagIds and the S-NSSAI(s) is valid across the PLMN |  |  |  | 
nsagInfos | array(NsagInfo) | O | 1..N | When present, this IE shall contain the associations between NSAGs and S-NSSAIs.
29.531 6.2.6.2.3 Type: SupportedNssaiAvailabilityData (AMF to NSSF)
nsagInfos | array(NsagInfo) | C | 1..N | This attribute shall be present if the AMF has indicated the support of NSAG by the UE, and the NSAG information is available to the NSSF. This attribute contains the list of NSAG information.
29.531 6.1.6.2.2 Type: AuthorizedNetworkSliceInfo (NSSF to AMF)(Nnssf_NSSelection Service API)
A problem:
This NSAG/NSSAI mapping of ‘many to many’ does not reflect properly 23.501 5.15.14 (An S-NSSAI can be associated with at most one NSAG values for Random Access and at most one NSAG value for Cell Reselection within a Tracking Area).
Stage 3 - Mapping of NSAG ID to NSSAI based on 29.531

## Slide 9
Proposed new def: 6.1.6.2.14 Type: NsagInfo //NSSF provides an array of NsagInfo in the AuthorizedNetworkSliceInfo
Attribute name | Data type | P | Cardinality | Description
combinedNsagId | CombinedNsagId | M | 1 | An NSAG ID structured attribute. It includes a value for random Access NsagId, and a value for Cell Reselection NSAG ID. See 3GPP TS 38.413 [21] and clause 5.15.14 of TS 23.501 [2]
snssai | Snssai | M | 1 | This attribute contains an S-NSSAI which is associated with the Combined NSAG identified by the CombinedNsagIds.
taiList | array(Tai) | O | 1..N | This attribute indicates the TA(s) within which the association between the NSAGs identified by the nsagIds and the S-NSSAI(s) is valid. (NOTE)
taiRangeList | array(TaiRange) | O | 1..N | This attribute indicates the TA(s) within which the association between the NSAGs identified by the nsagIds and the S-NSSAI(s) is valid. (NOTE)
Attribute name | Data type | P | Cardinality | Description
random Access NsagId | NsagId | M | 1 | This IE shall contain the random Access NsagId.
cell reselection NsagId | NsagId | M | 1 | This IE shall contain the cell reselection NsagId.
Table 6.1.6.2.X-1: Definition of type CombinedNsagId
A proposal for fixing NSAG/NSSAI mapping in 29.531