## Slide 1: FS_MASSS: Way Forward for UDM identifying two SUPIs in same device
vivo

## Slide 2: Background
Background: For activating DualSteer, the two SUPIs shall be in same device. There’re three different opinions on how device and UDM identify the associated two SUPIs are in same device during or after the two registration procedures: Use Registration Correlation information (A), Device sends SUCIs/5G-GUTIs to UDM via AMF (B), or UDM sends GPSIs to device for device activating DualSteer (C). All the options requires NAS impact.
Proposed principle:
  If there’s a way without NAS impact, i.e., over APP layer, it should be selected.
  It will be benefit for, e.g., saving the time in normative phase.

## Slide 3: Solution over APP layer
Procedure descriptions:
  (0) Device uses one of the SUPI for internet service, e.g., SUPI#1
  (1) User uses APP to send a request for subscribing and/or activating DualSteer towards operator’s web portal
  (2) The web portal sends a response with a token, the APP UI displays an acknowledge button and guides user how to toggle the SUPI for internet service, e.g., change different SUPI and/or close a SUPI associated with GPSI#1 for internet service
  (3) User changes the SUPI for internet access according to the guidance displayed in the APP UI, e.g., change to SUPI#2.
  (4) User clicks the button in the APP UI
  (5) The APP sends ACK with the token to the web portal
  (6) For subscribing, the web portal determines whether the two GPSIs are different, for activating, the web portal determines whether the two GPSIs are associated for DualSteer. If yes, it triggers the operator’s platform to configures the UDM with the two SUPIs and corresponding PEIs.
  After the procedure, the UDM can trigger DualSteer policy delivery, device is able to activate DualSteer based on the receiving of the DualSteer policy.
Example procedure of obtaining PEI binding information

## Slide 4: Proposals
(1) UDM determines whether the two SUPIs are in same device based on the PEI binding information
(2) How to obtain the PEI binding information is out of 3GPP scope

## Slide 5: End