## Slide 1: 5G Femto
KI#1 (in TR 23.700-45): SOH questions

## Slide 2: KI#1 principles
P#1: In this release 19, it is only supported for 5G to 4G interworking (i.e., 4G to 5G interworking is not supported).
  Yes: No:

## Slide 3: KI#1 principles – only focused on 5G to 4G IWK
P#2: Based on the local configuration, the AMF checks the correlation information between the target Home eNB ID and the corresponding CSG ID and derives the CSG ID.
  Yes: 8 No: 3
  Who would object to Yes as the way forward? 2
P#3: Based on the local configuration, the RAN checks the correlation information between the target Home eNB ID and the corresponding CSG ID and derives the CSG ID.
  Yes: 4 No: 7
  Who would object to Yes as the way forward? 5
※ For this WT#2, FS_5G_Femto SID (SP-231797) includes:
  "NOTE 2: It is expected that EPC (e.g., MME), E-UTRAN and NG-RAN impacts are avoided.“
  “NOTE 3: It is assumed that the existing CAG concept defined for PNI-NPN is re-used for Femto access control without impacts to PNI-NPN.”

## Slide 4: KI#1 way forward
If we cannot agree on any principles (in slides 1 and 2), the following question will be put to SoH:
Q#1: Is the IWK between 4G and 5G (or vice versa) supported in this release 19?
  Yes: 0 No: 7
  NOTE: The consequences of the above vote are:
    If the majority selected YES, in this case, we need to extend the KI#1 discussion for Q4’24.
    If the majority selected NO, in this case, the conclusion of KI is that no normative work is required and there is no support of handover IWK between 4G and 5G in this release.

## Slide 5
Annex

## Slide 6: Further information on P#3
To avoid unnecessary handover failure, the source NG-RAN may be configured with “CAG and Home eNB Correlation”. During the Handover, the source NG-RAN selects the target Home eNB cell according to the allowed CAG ID of UE and the pre-configured Correlation.