## Slide 1: Discussion on way forward for AIML_CN KI#3: NWDAF-assisted policy control and QoS enhancement
Samsung

## Slide 2: Conclusions for FS_AIML_CN KI#3 in TR 23.700-84
There were two principles concluded for KI#3 in clause 8.3 of TR 23.700-84:
Principle 1: NWDAF provides QoE of the corresponding candidate QoS to PCF based on PCF request
The PCF may send a analytics request or subscription to NWDAF for QoS and policy assistance information analytics. The PCF may include an analytics ID, Filter Information, one or multiple sets of QoS parameters, the candidate value list(s) for each QoS parameter, requesting expected service experience (e.g. QoE), etc.
Based on the PCF request, the QoS and policy assistance information analytics provided by NWDAF may include: expected QoE can be achieved by the candidate QoS parameters (the values of the QoS parameters are within the candidate value list provided by the PCF).
Principle 2: NWDAF provides multiple enhanced analytics IDs to PCF based on PCF request
  The PCF may request one or more analytics from the NWDAF that are used within the same analytics target period, i.e. Observed service experience, QoS sustainability, Network Performance analytics, analytics of the duration and usage of the established QoS Flows.
Observation: Principle 1 and Principle 2 were concluded for KI#3 in the SI stage, as documented in clause8.3 of TR 23.700-84.
Proposed way forward: SA2 to discuss the normative work on supporting Principle 1 and Principle 2 for R19 AIML_CN

## Slide 3: Technical analysis on Principle 1
As it has been concluded, an analytics ID to provide QoE of the corresponding candidate QoS is to be specified
Analytics consumer: PCF
Parameters in consumer (PCF) request:
  An analytics ID, Filter Information, etc.
  One or multiple (target) QoS parameter sets
  [Optional] candidate value list of QoS parameters in each (target) QoS parameter set
  Target/ Requesting expected QoE - FFS
  Other parameters are FFS
Outputs of NWDAF analytics ID:
  One or more expected QoE and the associated candidate QoS parameter set(s)
    the values of the QoS parameters in candidate QoS parameter set are provided by PCF in the list
  Other parameters are FFS
Input parameters of NWDAF analytics ID:
  QoS flow information from SMF, including
    (used) QoS parameter set(s), and
    associated info, e.g. Time stamp, UE ID, QFI, PDU session ID, etc.
  Other parameters are FFS
Terminologies used for KI#3 discussion:
QoS parameter set includes the following parameters and the values of each parameter:
  QoS parameters (in 5.7.2 of TS 23.501): 5QI, ARP, RQA, and optional GFBR, MFBR and Packet Loss Rate for GBR flows
  QoS Characteristics attributes (in 5.7.3 of TS 23.501): Resource Type, Priority Level, PDB, PER, Averaging Window, Maximum Data Burst Volume
  Other parameters are FFS
target QoS parameter sets: provided in the consumer request
candidate QoS parameter sets: generated by NWDAF as outputs
candidate QoS parameter sets are subsets of targeting QoS parameter sets, or they are the same.

## Slide 4: Discussion on proposals for Principle 1 during SA2 164 (I)
In SA2 164, there are three proposals for Principle 1:
Proposal 1: introduce a new analytics ID to provide the QoE and the corresponding candidate QoS to PCF
  Details in S2-2409138 by Samsung, vivo, OPPO, SKT, CMCC, Tencent, IDC, ETRI, Lenovo, DCO, ICS
Proposal 2: enhancements to Observed Service Experience analytics by introducing new inputs and outputs
  Details in S2-2409090 by Nokia
Proposal 3: introduce a new ‘Parameters Determination’ service for supporting QoS and policy enhancement
  Details in S2-2407647 by Huawei
 | Pros | Cons
Proposal 1: new analytics ID | An new analytics ID is to be specified to support Principle 1; Only necessary information related to Principle 1 will be included into the consumer request, NWDAF inputs and NWDAF outputs (as detailed in previous slide) of the new analytics ID; Minimum impact on spec. No impacts on the logic of existing analytics ID(s). | N/A
Proposal 2: enhancements to OSE | No new analytics ID in the spec | Will introduce plenty of new inputs and outputs to OSE which changes the existing logic of OSE; The existing inputs and outputs of OSE are redundant for supporting Principle 1; The complex and computational load of data collection, model training and model inference in proposal 2 will be significantly higher than proposal 1.
Proposal 3: new service | Not clear. | Will specify a new service in TS 23.288 which is similar to the existing Nnwdaf_AnalyticsSubscription Service.

## Slide 5: Discussion on proposals for Principle 1 during SA2 164 (II)
SOH on whether to support new analytics ID for Principle 1 during SA2 164
  An informal SOH was performed in the official session of AIML_CN during SA2 164
  Supporting company of new analytics ID: there was clear majority to support new analytics ID
  Objecting company of new analytics ID: one company only
Observation: there is clear majority to support new analytics ID to provide analytics on QoS and Policy Assistance
Proposed way forward: based on the SOH result and per rapporteur guidance, use S2-2409138 as baseline for KI#3 normative work on concluded Principle 1.

## Slide 6: Proposals for concluded Principle 2
Principle 2: NWDAF provides multiple (enhanced) analytics IDs to PCF based on PCF request. The PCF determines the QoS and policy based on the analytics ID(s) and other information.
No much discussion on Principle 2 during SA2 164 (August, 2024) meeting
Company proposals:
  Introduce a new analytics on QoS Flows level parameters
    Details in S2-2407589 by NTT Docomo, this contribution was merged into S2-2409138 during SA2 164
  Enhancements to existing analytic IDs, including Network performance and QoS Sustainability to support PCF decision making on QoS
    In S2-2407753 by Samsung, vivo, OPPO, SK Telecom, IDC
proposed way forward:
  SA2 to discuss the potential enhancements to analytics IDs to support concluded Principle 2.

## Slide 7
Q & A