## Slide 1: Discussion on Additional ULI
Huawei, HiSilicon

## Slide 2: Background
There are 3 options as documented in the KI#5 conclusion of TR 23.700-06.
SA2 concluded that Additional ULI format will be determined by RAN WG and SA2 will align based on RAN feedback. In SA2#163 meeting, SA2 sent a LS on questions regarding FS_VMR_Ph2 (see S2-2407345) to RAN3 to ask for feedback.
- The MWAB-gNB provides to the AMF an Additional ULI. The Additional ULI is:
- TAC/Cell ID of the cell serving the MWAB-UE if the PLMN serving the MWAB-UE and the PLMN broadcasted by the MWAB-gNB are the same PLMN.
- If the PLMN serving the MWAB-UE and the PLMN broadcasted by the MWAB-gNB are not the same PLMN, which below option used for the Additional ULI will be determined in normative phase.
- option 1: mapped TAC/Cell ID based on geo-location of the MWAB based on input from OAM.
- option 2: geo-location of the MWAB.
- option 3: TAC/Cell ID of the cell serving the MWAB-UE in other PLMN.

## Slide 3: Background
According to the LS on FS_VMR_Ph2 solution impacts to RAN (Access Control and Additional ULI) as documented in R3-247909, RAN3 discussed Additional ULI and the following WA was achieved:
  Additional ULI for WAB consists of TAI and NR CGI, which are determined by the WAB-node, reflecting the WAB-node’s physical location. This solution is compliant with Option 1 and Option 3. It is up to SA2 to support one of Option 1 and Option 3 or both.
  RAN3 is still discussing whether there are issues with applying this solution to WAB-MT access via NTN.
Observation: In case of the PLMN serving the MWAB-UE and the PLMN broadcasted by the MWAB-gNB are not the same PLMN, it is necessary for SA2 to further discuss the optimal option for Additional ULI based on RAN3’s feedback. In addition, SA2 needs to consider the Additional ULI in case of WAB-MT served by a satellite NG-RAN.

## Slide 4: Analysis of different options for Additional ULI
Options | Descriptions of Additional ULI | Potential impacts |  | 
 |  | OAM of the MWAB Broadcasted PLMN | MWAB | CN
Option 1 | mapped TAC/Cell ID based on geo-location of the MWAB based on input from OAM. | Normally, the MWAB-gNB's configuration is managed by the OAM based on the current location of MWAB. The OAM needs to be aware that the PLMN serving the MWAB-UE and the PLMN broadcasted by the MWAB-gNB are not the same PLMN. For example, the MWAB-UE sent the selected PLMN to the MWAB-gNB and then the OAM gets the selected PLMN from the MWAB-gNB. In addition, the OAM provides the mapping info to the MWAB so that the MWAB can map the TAC/Cell ID applied to the PLMN broadcasted by the MWAB-gNB based on geo-location of the MWAB-UE . However, | MWAB needs to inform OAM that PLMN serving the MWAB-UE and the PLMN broadcasted by the MWAB-gNB are not the same PLMN so that the OAM can provide MWAB with mapping info between TAC/Cell ID applied to the PLMN broadcasted by the MWAB-gNB and geo-location. The MWAB derives the mapped TAC/Cell ID of the PLMN broadcasted by the MWAB-gNB based on the actual MWAB-UE location. | The AMF serving UE receives the Additional ULI, which includes TAC/Cell ID information mapped from the actual MWAB-UE location.
Option 3 | TAC/Cell ID of the cell serving the MWAB-UE in other PLMN | No impacts | The MWAB-UE sends TAC/Cell ID of the cell serving the MWAB-UE in other PLMN to the MWAB-gNB. | The AMF serving UE can get the geo-location of the MWAB based on TAC/Cell ID of other PLMN and SLA agreement between different PLMNs
The PLMN serving the MWAB-UE and the PLMN broadcasted by the MWAB-gNB are not the same PLMN.

## Slide 5: Analysis of different options for Additional ULI
MWAB Broadcasted PLMN
(PLMN#2)
BH PLMN
(PLMN#1)
BH gNB
TAC#C
MWAB
Fixed gNB
Area#1
(no fixed gNB coverage)
Area#2
TAC#B
MWAB-gNB
MWAB-MT
It is possible that the deployment and coverage of fixed gNB between BH PLMN and MWAB Broadcasted PLMN are different.
If the MWAB is located in Area#2 and served by the BH gNB which broadcasts TAC#C of PLMN#1, the mapped TAC can be TAC#B of PLMN#2
However, when MWAB is located in Area#1 and served by the BH NG-RAN of PLMN#1, there is no mapped TAC/Cell ID of PLMN#2.
Therefore, it is difficult to map the fixed TAC/Cell ID of PLMN#1 into fixed TAC/Cell ID of PLMN#2.
The above scenario applies to both Option#1 and Option#3
The PLMN serving the MWAB-UE and the PLMN broadcasted by the MWAB-gNB are not the same PLMN.
MWAB-gNB
MWAB-MT
MWAB
Observations: Both Option#1 and Option#3 cannot address the scenario when UE is geographically located a specific area in which there is no mapped TAC/Cell ID of MWAB Broadcasted PLMN.

## Slide 6: Analysis of Additional ULI in case of WAB-MT served by a satellite NG-RAN
If the AMF requests UE location, in the case of NR satellite access, the NG-RAN provides all broadcast TAIs to the AMF as part of the ULI. The NG-RAN also reports the TAI where the UE is geographically located if this TAI can be determined.
The current mechanism for NR satellite access is described in the following:
TS 38.413:
TS 23.501:

## Slide 7: Analysis of Additional ULI in case of WAB-MT served by a satellite NG-RAN
UPF
MWAB-gNB
PLMN serving the MWAB-UE
Satellite
NG-RAN
AMF
MWAB Broadcasted PLMN
N2 message
MWAB-MT
(UE’s ULI
+
WAB-MT’s ULI)
UE’s Serving cell= WAB-gNB’s cell
WAB-MT’s Serving cell = all broadcast TAIs for the selected PLMN
In case of NR satellite access, MWAB-UE selects a PLMN and sends all TACs broadcast by the satellite NG-RAN to the WAB-gNB.
The WAB-gNB provides the Additional ULI which includes all broadcasted TAIs for the selected PLMN of WAB-UE.
Note: it is possible that WAB-UE’s selected PLMN is not same as the PLMN broadcast by the MWAB-gNB.
Observations: Considering the existing format of “NR NTN TAI information” for satellite access, it is proposed to include all broadcasted TAIs for the selected PLMN of WAB-UE in the Additional ULI. In addition, when WAB-UE’s selected PLMN is not same as the PLMN broadcast by the MWAB-gNB, SA2 thinks the design principle of Additional ULI for the both TN and NTN should be unified.

## Slide 8: Proposal
Based on the analysis, the following aspects are proposed :
  Both Option#1 and Option#3 cannot address the scenario when UE is geographically located a specific area in which there is no mapped TAC/Cell ID of MWAB Broadcasted PLMN.
  Considering the Option#2 is already ruled out by RAN3, SA2 has a slightly preference on the Option#3 “TAC/Cell ID of the cell serving the MWAB-UE in other PLMN”, considering the comparison of Option#1 and Option#3 regarding the precision in case of MWAB-UE using NR NTN to connect to the backhaul PLMN.
  SA2 would like to confirm with RAN3 the feasibility to include all broadcasted TAIs for the selected PLMN of WAB-UE in the Additional ULI in case WAB-MT access via NTN. SA2 also thinks the design principle of Additional ULI for the both TN and NTN should be unified when WAB-UE’s selected PLMN is not same as the PLMN broadcast by the MWAB-gNB, but it is under the remit of RAN3 to make the decision.
  The Reply LS on FS_VMR_Ph2 solution impacts to RAN (Access Control and Additional ULI) needs to highlight the above aspects.