## Slide 1: 3GPP TSG-SA WG2#166bis S2-2500916 Albania, 20-24 Januaruy, 2025 (was S2-240xxxx)
Discussion handling of 3GPP and non-3GPP access registration in INS
NEC Corporation

## Slide 2
Indirect Network Sharing is introduced in Release 19 in addition to 5G-MOCN. (23.501)
Figure 5.18.1-2: Indirect Network Sharing in which multiple participating operators' CNs connect to hosting operator's CN to share NR
1. Background

## Slide 3
A network sharing architecture shall allow multiple participating operators to share resources of a single shared network according to agreed allocation schemes. The shared network includes a radio access network. The shared resources include radio resources.
The shared network operator allocates shared resources to the participating operators based on their planned and current needs and according to service level agreements.
In this Release of the specification, the 5G Multi-Operator Core Network (5G MOCN) network sharing architecture, in which only the RAN is shared in 5G System, is supported. The 5G System may also support Indirect Network Sharing deployment between hosting operator (i.e. shared network operator) and participating operator (see clause 6.21 of TS 22.261 [2], Figure 5.18.1-2 and Annex R), in which the RAN is shared. The communication between the shared RAN and the core network of the participating operator is routed through the core network of the hosting operator that connects to the shared RAN.
5G MOCN for 5G System, including UE, RAN and AMF, shall support operators' ability to use more than one PLMN ID (i.e. with same or different country code (MCC) some of which is specified in TS 23.122 [17] and different network codes (MNC)) or combinations of PLMN ID and NID. 5G MOCN supports NG-RAN Sharing with or without multiple Cell Identity broadcast as described in TS 38.300 [27]. Indirect Network Sharing for 5G system, including UE, shared RAN and CP NFs of hosting operator, shall support each participating operator to use more than one PLMN ID.
For Indirect Network Sharing, the shared RAN is broadcasting multiple PLMN IDs, including the PLMN ID which represents the hosting operator and the PLMN IDs which represent participating operators. Multiple PLMN IDs are supported by the serving AMF (i.e. the AMF in the core network of the hosting operator). A UE from a participating operator can select the PLMN ID representing the participating operator in the shared RAN area based on existing procedures specified in TS 23.122 [17]. The serving AMF selects core network functions in the PLMN of the participating operator for the UE, based on home routed roaming architecture principle as specified in clause 4.2.4. In addition, the serving AMF selects the SMF of participating operator possibly considering UE location information and also selects a V-SMF in its own network during the PDU session establishment procedure. The serving AMF determines the serving PLMN ID as follows:
- For procedures involving the Network Function in the participating operator network (e.g. AUSF), the AMF sets the serving PLMN ID to the selected PLMN ID.
- For procedures involving the Network Function only in the hosting operator network (e.g. PCF), the AMF sets the serving PLMN ID to the PLMN ID of the hosting operator.
Editor's note: It is FFS whether the above principles can be applicable for all procedures in the HPLMN ID/EHPLMN ID broadcast option.
NOTE 1: In this Release of specification, the Indirect Network Sharing is only applicable for NR with 5GC of hosting operator and 5GC of participating operator. There are maximum of two SMFs (i.e. V-SMF of the hosting operator and H-SMF of the participating operator) controlling a PDU session.

## Slide 4
5.3.2.4 Support of a UE registered over both 3GPP and Non-3GPP access of TS 23.501
For a given serving PLMN there is one RM context for a UE for each access, e.g. when the UE is consecutively or simultaneously served by a 3GPP access and by a non-3GPP access (i.e. via an N3IWF, TNGF and W-AGF) of the same PLMN. UDM manages separate/independent UE Registration procedures for each access.
When served by the same PLMN for 3GPP and non-3GPP accesses, an UE is served by the same AMF except in the temporary situation described in clause 5.17 i.e. after a mobility from EPS while the UE has PDU Sessions associated with non-3GPP access.
When the 3GPP access and the non-3GPP access for the same UE are served by the same PLMN, the AMF assigns the same 5G-GUTI for use over both accesses. Such a 5G-GUTI may be assigned or re-assigned over any of the 3GPP and Non-3GPP accesses. The 5G-GUTI is assigned upon a successful registration of the UE and is valid over both 3GPP and Non-3GPP access to the same PLMN for the UE. Upon performing an initial access over the Non-3GPP access or over the 3GPP access while the UE is already registered with the 5G System over another access of the same PLMN, the UE provides the native 5G-GUTI for the other access. This enables the AN to select an AMF that maintains the UE context created at the previous Registration procedure via the GUAMI derived from the 5G-GUTI and enables the AMF to correlate the UE request to the existing UE context via the 5G-GUTI.

## Slide 5
2. Discussion
Problem Discussion
According to subclause 5.3.2.4 of TS 23.501 if the UE has registered to a PLMN over 3GPP access and is registering over non-3GPP access then the UE shall provide the 5G-GUTI of the 3GPP access to N3IWF so that the N3IWF select same AMF to which the UE is registered over 3GPP access. Also, according to sub clause if the UE is in home country than the UE shall select the same N3IWF of the home PLMN.
When a UE is registered over 3GPP access to a participating PLMN via a host AMF, the UE is registering to the non-3GPP access and there is no N2 connection exist between N3IWF and host AMF then it is not clear how the network behavior to handle the registration procedure over non-3GPP access is not clear.

## Slide 6
UE
Participating NW (MCC=111, MNC=33I
Hosting NW (MCC=111, MNC=22)
RAN
AMF1
3. Registration Accept (5G-GUTI 1 with MCC=111, MNC=22)
4. 5G-GUTI1 stored
N3IWF
AMF2
5. Registration Request (5G-GUTI1 with MCC=111, MNC=22) over none-3GPP access
1. Registration Request (UE-ID)
UDM
2. AMF1 is registered to the UDM
No N2 connection between N3IWF and AMF1. It is not clear what N3IWF will do?

## Slide 7
Solution 1 (S2-2500920):
When a UE is registered over 3GPP access to a participating PLMN via a host AMF, the UE is registering to the non-3GPP access and there is no N2 connection exist between N3IWF and host AMF then the N3WIF selects an AMF in the participating PLMN as defined in sub clause and
The UDM registers the UE to the AMF of participating PLMN over non-3GPP access and indicate to the AMF of the participating PLMN that the UE is registered for both 3GPP access and non-3GPP access. The participating AMF indicates to the UE that it is registered for 3GPP access and non-3GPP access.
The UE maintains context over participating AMF and host AMF.

## Slide 8
UE
Participating NW (MCC=111, MNC=33I
Hosting NW (MCC=111, MNC=22)
RAN
AMF1
3. Registration Accept (5G-GUTI 1 with MCC=111, MNC=22)
4. 5G-GUTI1 stored
N3IWF
AMF2
5. Registration Request (5G-GUTI1 with MCC=111, MNC=22) over none-3GPP access
1. Registration Request (UE-ID)
UDM
2. AMF1 is registered to the UDM indicating INS registration
6. N3WIF selects AMF 2 of the host as per section of TS 23.501
5. Registration Request (5G-GUTI1 with MCC=111, MNC=22) over none-3GPP access
Registration procedure over non-3GPP access as per TS 23.501
6. Registration Accept (5G-GUTI 2with MCC=111, MNC=33, Registration result 3GPP and non-3GPP access)
7. 5G-GUTI 1 and 5G-GUTI2 stored

## Slide 9
Solution 2 (S2-2500922):
While a UE is registering over 3GPP access to a participating PLMN via a host AMF, the AMF indicates to the UDM that this is INS registratio. When the UE is registering to the non-3GPP access and there is no N2 connection exist between N3IWF and host AMF then the N3WIF selects an AMF in the participating PLMN as defined in sub clause and forwards the registration request message to the AMF in the participating PLMN.
When the UDM receives registration request from the AMF for non-3GPP access registers while the UE is registered over 3GPP access via host AMF, the UDM rejects the registration procedure of the UE.

## Slide 10
UE
Participating NW (MCC=111, MNC=33I
Hosting NW (MCC=111, MNC=22)
RAN
AMF1
3. Registration Accept (5G-GUTI 1 with MCC=111, MNC=22)
4. 5G-GUTI1 stored
N3IWF
AMF2
5. Registration Request (5G-GUTI1 with MCC=111, MNC=22) over none-3GPP access
1. Registration Request (UE-ID)
UDM
2. AMF1 is registered to the UDM indicating INS registration
6. N3WIF selects AMF 2 of the host as per section of TS 23.501
7. Registration Request (5G-GUTI1 with MCC=111, MNC=22) over none-3GPP access
11 Registration Reject ()
9.If the UE is registered over host AMF rejects the non-3GPP access registration
8. Nudm_UECM_Registration Request ( non-3GPP access type)
10. Nudm_UECM_Registration Response ( Reject non-3GPP registration)

## Slide 11
3. Proposal
Following contrbutions are submitted to the meeting:
1. S2-2500920 capturing solution 1 of the discussion paper.
2. S2-2500922 capturing solution 2 of the discussion paper.
It is proposed to discuss these two solutions and choose a solution among them to address the case identified in the discussion paper.