## Slide 1: Discussion on S&F Monitoring List And Transition between S&F mode and normal mode
Huawei, HiSilicon

## Slide 2: Content
1. Satellite List sent to UE
  Editor’s Notes
  What kind of Satellites are included in the list
2. Mode transition
  Scenario-1: Transition from Non-S&F mode to S&F mode
  Scenario-2: Transition from S&F mode to non-S&F mode

## Slide 3: Background/LS from RAN2
RAN2 send an LS (R2-2411197) to SA2 as below:
The issues are
  What kind of satellite is included in the satellite list?
  What is the UE behavior on receiving the list?
RAN2 discussed how an IoT NTN UE capable of store-and-forward operation uses the MME-configured satellite ID list in the access stratum. RAN2 made the assumption that the UE configured with a satellite ID list by MME is not prevented to camp on a satellite operating in normal IoT NTN mode (i.e. with feeder-link connection), and perform subsequent access and data/signalling communication with that satellite.
RAN2 would like to request SA2 to provide feedback on whether the following RAN2 understanding can be confirmed:
RAN2 understanding: The UE configured with a satellite ID list by MME is not prevented to camp on, attempt to access to and communicate with a satellite which is not included in the MME-configured satellite list.
Also, RAN2 would like to respectfully ask the question below to SA2:
Question: If a satellite is included in the satellite list signalled by the MME to a UE, does it mean one of the below options, or possibly other option(s):
the satellite has the UE context but does not necessarily support store-and-forward operation; or
the satellite has the UE context and must support store-and-forward operation (but may be operating in normal IoT NTN mode or in store-and-forward mode when the satellite serves the area where the UE is located)?

## Slide 4: 1. S&F Monitoring List/EN
An EN was added in SA2#166 meeting:
  Editor’s Note: How to handle the specification of the “List of satelliteID(s)” and “S&F Monitoring List” as per conclusions in TR 23.700-29 is FFS.
The satellite list (no matter the “list of satellite ID(s)” or “S&F Monitoring List”) is a tool which is used by the UE to assist with saving power, including:
  The UE can use the list to (re)attempt NAS procedures;
  The satellite list indicates the satellites that may contain MT data.
Also, the satellite list is a tool which is used by the network to save resource, including:
  The satellite list Indicates the satellites that the network synchronizes the UE context with;
  The satellite list Indicates the satellites that the network uses to send MT data;
Form this perspective, this DP proposes:
  Proposal 1A: The UE can use the list to (re)attempt NAS procedures, and to be aware of which satellite(s) may contain MT data.
  Proposal 1B: The network can synchronize UE context to the satellite(s) included in the list, and can send MT data to these satellite(s).

## Slide 5: 1. S&F Monitoring List/EN
From the UE side, the satellite list sent to UE is a recommendation information for UE and it is not necessary to send two different lists to UE.
It is difficult and not appropriate to restrict the UE to shall follow the list:
  If the UE determines a satellite is operated in S&F Mode, in order to ensure the NAS procedure is performed successfully, it is better for the UE to follow the satellite list provided by the MME.
  The UE may also need to access other satellites (in the same PLMN) which are not included in the satellite list, or another RAT type to attain services, e.g.
    UE access a satellite which operates in non-S&F mode;
    UE detects that it is unable to obtain service link from any of the satellite in the list for a long time, e.g. due to UE movement.
  The specification will not be able to predict and document each and every possible reason a UE needs to use a satellite not on the list.
Form this perspective:
  Proposal 1C: The list sent to UE is a recommendation information for UE and it is unnecessary to send two different lists to the UE.
  Proposal 1D: How UE behaves when receiving the satellite list is UE implementation.
  Proposal 1E: UE may access other satellites which are not included in the satellite list, or other RAT type to attain services.

## Slide 6: 1. S&F Monitoring List/what kind of satellites
There are two different kind of satellites:
  S&F satellite which supports S&F operation, e.g., satellite with eNB and e.g. partial MME on board, or full CN on board.
  Non-S&F satellite which supports non-S&F operation, e.g., satellite with only eNB on board, satellite with transparent payload.
As the satellite list is sent by the network to the UE from a satellite operating in S&F mode, it is reasonable that the satellite list includes satellite(s) which supports S&F operation.
But as the satellite moves, the satellite may be operating in normal IoT NTN mode or in store-and-forward mode when the satellite serves the area where the UE is located. In other words, this corresponds to option 2 described in the LS (R2-2411197).
Form this perspective, this DP proposes:
  Proposal 1F: The satellites included in the satellite list are expected to be able to support the UE (e.g. have a UE context) and must support store-and-forward operation (but may be operating in normal IoT NTN mode or in store-and-forward mode when the satellite serves the area where the UE is located).

## Slide 7: 2. Mode change
UE moves from non-S&F mode to S&F mode:
  UE initiates TAU procedure which includes GUTI, e.g. UE moves out of TAI list. Or, UE initiates SR procedure.
  As the (new) S&F MME may doesn’t have UE context, e.g. in TAU procedure, the new MME cannot retrieve UE context from the old MME as the UE context in the old MME is not reachable (i.e. no feeder link), the MME should send cause #9 ("UE identity cannot be derived by the network") rather than S&F Wait Timer, etc. to UE.
UE moves from S&F mode to non-S&F mode,
  UE initiates TAU, or UE initiates SR
  In this case, if the (new)MME doesn’t have the latest UE context, the (new)MME can use the existing mechanism, i.e. cause #9 "UE identity cannot be derived by the network“, to indicate the UE to initiate attach procedure.
Potential options to solve the issue in moving from non-S&F mode to S&F mode:
Option A: MME sends existing cause value to UE
  The (new) MME is aware of UE moves from non-S&F mode to S&F mode；
  And, the (new) MME cannot retrieve UE context from the old MME,
  Then the MME rejects the NAS request by sending existing cause #9 "UE identity cannot be derived by the network"
Option B: UE initiates Attach procedure when transits from non-S&F Mode to S&F mode.
Consensus: When UE transits between S&F mode, if the MME which supports S&F handling doesn’t have a UEs context, the MME sends NAS reject to UE which includes S&F Wait timer, S&F Monitoring List, or both.
Options | UE impact | NW impact
A | UE is aware of transition from non-S&F mode to S&F mode UE indicates to the NW the above mode change | NW is aware of transition from non-S&F mode to S&F mode NW sends existing cause value to UE based on the above mode change
B | UE is aware of transition from non-S&F mode to S&F mode UE initiates attach procedure based on the above mode change | /
summary | Option A impacts both UE and NW. Option B only impacts UE. | 
Proposal 2: UE initiates Attach procedure when transits from non-S&F Mode to S&F mode.
As described in TS 24.301, Cause #9 – UE identity cannot be derived by the network.
  This EMM cause is sent to the UE when the network cannot derive the UE's identity from the GUTI/S-TMSI/P-TMSI and RAI e.g. no matching identity/context in the network or failure to validate the UE's identity due to integrity check failure of the received message.
Table: Comparison of two options

## Slide 8: Summary:
  Proposal on satellite list sent to UE
  Proposal 1A: The UE can use the list to (re)attempt NAS procedures, and to be aware of which satellite(s) may contain MT data.
  Proposal 1B: The network can synchronize UE context to the satellite(s) included in the list, and can send MT data to these satellite(s).
  Proposal 1C: The list sent to UE is a recommendation information for UE and it is unnecessary to send two different lists to the UE.
  Proposal 1D: How UE behaves when receiving the satellite list is UE implementation.
  Proposal 1E: UE may access other satellites which are not included in the satellite list, or other RAT type to attain services.
    Proposal 1F: The satellites included in the satellite list are expected to be able to support the UE (e.g. have a UE context) and must support store-and-forward operation (but may be operating in normal IoT NTN mode or in store-and-forward mode when the satellite serves the area where the UE is located).
Proposal on mode change
  Proposal 2: UE initiates Attach procedure when transits from non-S&F Mode to S&F mode.
Reply to the LS in S2-2500781 (LS Reply) is described on the next slide, S2-2500782 (general description) adds descriptions corresponding to Proposal 1 (including 1A~1F) and Proposal 2 into clause 4.13.9.1, and S2-2500783 (procedure) Add S&F Monitoring List IE into NAS procedures.

## Slide 9: Summary: LS Reply
Based on Proposal 1C, 1D, 1E and 1F, SA2 Reply to the LS (R2-2411197) is as following:
RAN2 discussed how an IoT NTN UE capable of store-and-forward operation uses the MME-configured satellite ID list in the access stratum. RAN2 made the assumption that the UE configured with a satellite ID list by MME is not prevented to camp on a satellite operating in normal IoT NTN mode (i.e. with feeder-link connection), and perform subsequent access and data/signalling communication with that satellite.
RAN2 would like to request SA2 to provide feedback on whether the following RAN2 understanding can be confirmed:
RAN2 understanding: The UE configured with a satellite ID list by MME is not prevented to camp on, attempt to access to and communicate with a satellite which is not included in the MME-configured satellite list.
[SA2 answer] SA2 confirms the above RAN2 understanding is aligned with SA2. SA2 agreed that how UE behaves when receiving the satellite list is UE implementation and has updated specification accordingly (please see the attached CR for details).
Also, RAN2 would like to respectfully ask the question below to SA2:
Question: If a satellite is included in the satellite list signalled by the MME to a UE, does it mean one of the below options, or possibly other option(s):
the satellite has the UE context but does not necessarily support store-and-forward operation; or
the satellite has the UE context and must support store-and-forward operation (but may be operating in normal IoT NTN mode or in store-and-forward mode when the satellite serves the area where the UE is located)?
[SA2 answer] The satellites included in the satellite list are expected to be able to support the UE (e.g. have a UE context) and must support store-and-forward operation (but may be operating in normal IoT NTN mode or in store-and-forward mode when the satellite serves the area where the UE is located).