## Slide 1: KI#2: New Services for VFL (Reminder about agreements from SA2#166 drafting session and additional new points)
SA2#166AHE
Nokia
S2-2500143 (was S2-2411373r01)

## Slide 2: Issue 1: Services between NWDAF VFL server and NWDAF VFL client for VFL training and sample/feature alignment
Company | Option 1: Reuse Nnwdaf_MLModelTraining_Subscribe and/or Nnwdaf_MLModelTrainingInfo_Request | Option 2: define new service (with similarities)
Ericson | Mandatory “ML Model Interoperability Information” input parameter (that is not needed) may be a problem | Having a new service for VFL may be simpler
Apple | For training | For preparation
InterDigital |  | Preferred
OPPO |  | Using a new service for VFL is simpler to be maintenance and will make the logic clear
NTT DOCOMO | use of existing services is okay | If there are many VFL specific parameters, new services are preferred.
Huawei |  | Preferred. similar style as Nnwdaf_MLModelTraining_Subscribe
Vivo |  | Preferred to make the service logic clear
Nokia | acceptable | Preferred to make the service logic clear
Proposal: Option 2: Define new service, but with similarities to Nnwdaf_MLModelTraining service

## Slide 3: Issue 1: Services between NWDAF VFL server and NWDAF VFL client for VFL preparation/training
Company | Request-response | Subscribe-Notify style | both
Nokia | Requires duplicated information | Preferred to avoid sending all information in each training operation | Redundant ption should be avoided
Apple |  |  | preferred
Huawei |  | Preferred | 
Proposal:
a) one service name with different service operation i.e. Subscribe Notify style for trainig
and request/reponse style for prepartion
b) one service name with same service operation i.e. Subscribe Notify style for trainig/prepartion
c) one service name with same service operation i.e. request/reponse style for trainig/prepartion
For normal model training and HFL, we provide two alternative services:
Nnwdaf_MLModelTrainingInfo (Request-response) and Nnwdaf_MLModelTraining (Subscribe-Notify)

## Slide 4: Issue 1: Services between NWDAF VFL server and AF VFL client for VFL training and sample/feature alignment
Proposal: Define new AF and NEF services for the VFL preparationtraining and VFL feature/sample alignment with AF as VFL client. They should be designed with similarity to the Nnwdaf_MLModelTraining service.

## Slide 5: Issue 1: Services between NWDAF VFL server and VFL client for VFL training and sample/feature alignment: Topics for additional discussion:
Inclusion of Feature ID:
Clause 6.2H.2.2.1 already states that Clients may provide list of Feature IDs to the server during preparation phase and server may provide selected Feature IDs to the clients at end of preparation phase
However, Inclusion of those parameters was nor accepted into the service operations at SA2#166 and Ens were requested.
Proposal: align with agreed procedures by adding Feature IDs as optional output parameter in training responses (used during the preparation phase) and optional input parameters in training subscription (used after the preparation phase)
Reuse of HFL concepts for training:
For instance HFL used an iteration round ID during the training.
The same messages are used for multiple training rounds. This can lead to issues if messages are lost or repeated. For HFL, those issues were resolved via a training round ID.
Proposal: Add a VFL training iteration number in subscription request for training and in notifications. Discuss if more parameters from VFL model training might be usefull-.

## Slide 6: Issue 2: Services between NWDAF VFL server and NWDAF VFL client for VFL inference
Company | Option 1: Reuse Nnwdaf_MLModelTraining service and the Nnwdaf_MLModelTrainingInfo service | Option 2: Reuse Nnwdaf_AnalyticsInfo service and the Nnwdaf_AnalyticsSubscription service | Option 3: New service
Ericson | Reuse Training service |  | 
Apple | It’s tricky: while we see the merits or re-using the existing service for inference to minimize impact, it does not make sense in our view to have a training inference to perform inference |  | 
InterDigital | Here we agree with Ericsson that we should maintain consistency (including both subscribe and request/response) for both training and inference |  | 
OPPO |  |  | preferred
NTT DOCOMO |  |  | preferred
Huawei |  |  | The service for training and the service for inference should be separate
Vivo |  |  | preferred
Nokia |  |  | preferred
Proposal: Option 3: Define new inference service with both service operation

## Slide 7: Issue 2: Services between NWDAF VFL server and AF VFL client for VFL inference
Proposal: Define new AF and NEF services for the VFL Inferencewith AF as VFL client. They should be designed with similarity to the Nnwdaf_ service.

## Slide 8: Issue 2: Services between NWDAF VFL server and VFL client for VFL inference: Topics for additional discussion
In clause 6.1.3 many parameters that a VFL server can receive in requests/subscriptions for analtics and that the server can then provide to analytics consumers in responses/notifications are defined:
In Requests/ subscriptions:
Preferred level of accuracy; - Reporting Thresholds; - Maximum number of objects requested (max); - Maximum number of SUPIs requested (SUPImax); - Time when information is needed; - Analytics Metadata Request; - Data time window; - Consumer NF's serving area or NF ID;
In responses/notifications
Analytics Metadata, Timestamp of intermediate result generation and optionally Validity period, and Confidence
Proposal: Discuss whether VFL client involvement is required to handle those parameters and if so add them to VFL inference requests/subscriptions.

## Slide 9: Issue 3: Services between AF VFL server and NWDAF VFL client for VFL inference
Proposal: Define a new NEF service for an untrusted AF as consumer that offers NWDAF detection assistance, VFL preparation and training communication with NWDAF clients, and VFL inference communication with NWDAF clients. Service operations for VFL preparation and training communication should be designed with similarity to the Nnwdaf_MLModelTraining service (see Proposal 1). Service operations for VFL inference communication should be designed with similarity to the service for the VFL inference (see Proposal 3)
Service Name | Service Operations | Operation Semantics | Example Consumer(s)
Nnef_VflTrainingAfClient | Subscribe | Subscribe / Notify | NWDAF
 | Unsubscribe |  | NWDAF
 | Notify |  | NWDAF
Nnef_VflInferenceAfClient | Subscribe | Subscribe / Notify | NWDAF
 | Unsubscribe |  | NWDAF
 | Notify |  | NWDAF
 | Request | Request / Response | NWDAF
Nnef_VflNwdafClient | NwdafDiscovery | Request / Response | AF
 | NwdafRelease | Request / Response | AF
 | TrainingSubscribe | Subscribe / Notify | AF
 | TrainingUnsubscribe |  | AF
 | TrainingNotify |  | AF
 | InferenceSubscribe | Subscribe / Notify | AF
 | InferenceUnsubscribe |  | AF
 | InferenceNotify |  | AF
 | InferenceRequest | Request / Response | AF

## Slide 10: Issue 3: NEF services: Topics for additional discussion
A. Use the same NEF service for training requests/subscriptions when
NWDAF is VFL server and AF is VFL client; and (2) AF is VFL server and NWDAF is VFL client?
B Use the same NEF service for inference requests/subscriptions when
NWDAF is VFL server and AF is VFL client; and (2) AF is VFL server and NWDAF is VFL client?
Observation: NEF procedures differ depending on scenario:
NWDAF external ID only applicable for scenario 2
Different mapping between external and internal IDs
Need to authenticate requests from external AF applicable only for scenario 2
Possible desire to support only one scenario in a deployment
Proposal: Define separate NEF services for scenarios (1) and (2)

## Slide 11: Thank you.