## Slide 1: Discussion on AMF re-allocation with a single logical WAB-gNB
Huawei, HiSilicon

## Slide 2: Outline
LS on FS_VMR_Ph2 solution impacts to RAN (MWAB mobility) (see R3-247910) from RAN3 triggers SA2 to provide feedback on whether either of these single-gNB solutions can be achieved without CN impact.
Therefore, it is necessary for SA2 to evaluate the above solutions and identify the potential CN impacts.
Solution 1: Using single WAB-gNB with single cell and changing TAC
The WAB-gNB establishes a separate NG-C connection with the new AMF.
It reports the initial TAC, TAC1, only to the initial AMF and the new TAC, TAC2, only to the new AMF.
The WAB-gNB cell updates the SI from TAC1 to TAC2.
For UE in RRC CONNECTED state:
  When receiving the SI update, the UE performs an MRU, which is forwarded by the WAB-gNB to the initial AMF. The WAB-gNB includes TAC2 as part of the User Location Information to the initial AMF. Based on TAC2 of the received ULI, the initial AMF initiates an AMF reallocation to the new AMF. There is no handover procedure to be performed for the purpose of UE’s AMF change.
For UE in RRC IDLE/INACTIVE state:
  When receiving the SI update, the UE performs an MRU, which is forwarded by the WAB-gNB to the new AMF. The new AMF retrieves the UE’s context from the initial AMF.
Solution 2: Using single WAB-gNB with two cells and different TACs
The WAB-gNB establishes a separate NG-C connection with the new AMF.
It instantiates a second cell whose SI includes only TAC2, while the first cell’s SI only includes TAC1.
It reports TAC1 only to the initial AMF and TAC2 only to the new AMF.
For UE in RRC CONNECTED state:
  The WAB-gNB initiates an NG handover from the first cell to the second cell for the UE. When the initial AMF receives the HO Required message, it decides to conduct an inter-AMF handover to the new AMF based on the TAC2 included in the Target ID IE of the HO Required message, and forwards the HO signalling to the new AMF. After all UEs have been handed over, the WAB-gNB discontinues operation of the first cell.
For UE in RRC IDLE/INACTIVE state:
  When operation of the first cell is discontinued, the UE reselects the second cell and performs an MRU, which is forwarded by the WAB-gNB to the new AMF. The new AMF retrieves the UE’s context from the initial AMF.

## Slide 3: Analysis of Solution 1
UE | Procedures | Potential CN impacts
CM-CONNECTED state | Option#1A: it is assumed that the WAB with 2 TACs connects to two different AMF set simultaneously. The UE performs Mobility Registration Update, which is forwarded by the WAB-gNB to the initial AMF based on the GUAMI. Based on TAC2 of the received ULI, the initial AMF initiates an AMF reallocation to the new AMF. | New condition to trigger AMF re-allocation.
 | Option#1B: it is assumed that the WAB with 2 TACs can NOT connect to two different AMF sets simultaneously. WAB-gNB updates the TAC in the SI and routes the subsequent UL messages to the new AMF. The UE performs Mobility Registration Update, which is forwarded by the WAB-gNB to the new AMF. The leftover procedures for CN reuse the existing ones. WAB-gNB rejects the DL signalling from the initial AMF with the existing cause value before the Mobility Registration Update is finished. WAB-gNB releases the NG connection with initial AMF after all connected UE are served by the new AMF. | No impacts
CM-IDLE state | Option#1A: If the WAB with 2 TACs connects to two different AMF set simultaneously, then: The UE performs an Mobility Registration Update, which is forwarded by the WAB-gNB to the initial AMF based the GUAMI . Based on TAC2 of the received ULI, the initial AMF initiates an AMF reallocation to the new AMF | New condition to trigger AMF re-allocation.
 | Option#1B: If the WAB with 2 TACs can NOT connect to two different AMF sets simultaneously, then: The UE performs an Mobility Registration Update, which is forwarded by the WAB-gNB to the new AMF based on new TAC2. | No impacts
WAB-gNB
Cell#1
AMF#1
AMF#2
T2: NG setup procedure
NG setup(Global RAN Node ID,TAC#2)
WAB-gNB
Cell#1
AMF#1
NG setup(Global RAN Node ID,TAC#1)
T1: NG setup procedure
WAB-gNB
Cell#1
AMF#1
AMF#2
T2: NG setup procedure
NG setup(Global RAN Node ID,TAC#2)
WAB-gNB
Cell#1
AMF#1
NG setup(Global RAN Node ID,TAC#1)
T1: NG setup procedure
Option#1A
Option#1B
X
Observations: Based on the original descriptions of solution#1, the routing of Mobility Registration Update by the WAB for the CM-IDLE state and CM-CONNECTED state are not consistent, which seems to be under different assumptions that whether the WAB with 2 TACs connects to two different AMF set simultaneously. It is proposed to list Option#1A and Option#1B.

## Slide 4: Analysis of Solution 2
UE | Procedures | Potential CN impacts
CM-CONNECTED state | It is assumed that the WAB with 2 TACs connects to two different AMF sets simultaneously: The WAB-gNB initiates an NG handover from the first cell to the second cell for the UE. When the initial AMF receives the HO Required message, it decides to conduct an inter-AMF handover to the new AMF based on the TAC2 included in the Target ID IE of the HO Required message, and forwards the HO signalling to the new AMF. After all UEs have been handed over, the WAB-gNB discontinues operation of the first cell. | The Source AMF selects Target AMF even though different cells share the same Global RAN Node ID.
CM-IDLE state | It is assumed that the WAB with 2 TACs connects to two different AMF sets simultaneously: UE reselects the second cell which supports new TAC and performs an MRU, which is forwarded by the WAB-gNB to the initial AMF. When the initial AMF receives the new TAC2 from the WAB-gNB, it performs AMF relocation based on the new TAC2 | The initial AMF performs AMF reallocation based on the new TAC
WAB-gNB
Cell#1
Cell#2
AMF#1
AMF#2
TAC2
TAC1
Handover Required
(Target ID)
UE Context Request
Handover Request
AMF#1
AMF#2
N2 msg(TAC#2, MRU)
UE context transfer
UE
WAB-gNB
Cell#1
Cell#2
TAC2
TAC1
UE
Handover
UE in CM-CONNECTED state
UE in CM-IDLE state
X
WAB-gNB
Cell#1
Cell#2
TAC2
TAC1
AMF#1
AMF#2
NG setup(Global RAN Node ID,TAC#1)
NG setup procedure
NG setup(Global RAN Node ID,TAC#2)
Observations: Based on the original descriptions of solution#2, it assumes the WAB with 2 TACs connects to two different AMF sets simultaneously.

## Slide 5: Comparison of Solutions
Solutions |  | UE | Procedures | Potential CN impacts
Solution 1 | Option#1A: It is assumed that the WAB with 2 TACs connects to two different AMF set simultaneously | CM-CONNECTED state | Initial AMF triggers AMF relocation during Mobility Registration Update | Initial AMF triggers AMF relocation based on the new TAC included in the N2 message
 |  | CM-IDLE state |  | 
 | Option#1B:If the WAB with 2 TACs can NOT connect to two different AMF sets simultaneously | CM-CONNECTED state | The existing Mobility Registration Update procedures | No impacts
 |  | CM-IDLE state |  | 
Solution 2: It is assumed that the WAB with 2 TACs connects to two different AMF sets simultaneously |  | CM-CONNECTED state | Initial AMF triggers AMF relocation during NG handover | The Source AMF selects Target AMF even though different cells share the same Global RAN Node ID.
 |  | CM-IDLE state | Initial AMF triggers AMF relocation during Mobility Registration Update | The initial AMF performs AMF reallocation based on the new TAC
Observations: From CN perspective, both Option#1A and Solution#2 require the initial AMF to select new AMF based on new TAC.

## Slide 6: Summary
Based on the analysis of two solutions, SA2 observes the following potential CN impacts:
  Solution 1: Using single WAB-gNB with single cell and changing TAC
    SA2 has different understandings of the assumptions that whether the WAB with 2 TACs connects to two different AMF set simultaneously and identifies two alternatives:
      Option 1A(WAB with 2 TACs connects to two different AMF sets simultaneously):
        CN impacts: Initial AMF triggers AMF relocation during Mobility Registration Update based on the new TAC included in the N2 message for both UE in RRC CONNECTED state and UE in CM-IDLE state.
      Option 1B(WAB with 2 TACs can NOT connect to two different AMF sets simultaneously):
        WAB-gNB updates the TAC in the SI and routes the subsequent UL messages to the new AMF.
        The UE performs Mobility Registration Update, which is forwarded by the WAB-gNB to the new AMF.
        The leftover procedures for CN reuse the existing ones.
        WAB-gNB rejects the DL signaling from the initial AMF with the existing cause value before the Mobility Registration Update is finished.
        WAB-gNB releases the NG connection with initial AMF after all connected UE are served by the new AMF.
        CN impacts: The existing mechanism can be reused without CN impacts, for UE in RRC CONNECTED state and UE in CM-IDLE state.
    SA2 discusses the feasibility of simultaneous NG connection towards different AMF sets for one gNB.
  Solution 2: Using single WAB-gNB with two cells and different TACs
    SA2 thinks this solution assumes the WAB with 2 TACs connects to two different AMF sets simultaneously.
    CN impacts: When UE is CM-CONNECTED state, Initial AMF triggers AMF relocation during NG handover based on the new TAC included in the Target ID. When UE is UE in CM-IDLE state, Initial AMF triggers AMF relocation during Mobility Registration Update based on the new TAC.