## Slide 1: Way Forward on the AIoT architecture options
Intel

## Slide 2: Outline
Identifies architectural similarities between
  T1 architecture with Direct Path, and
  T2 architecture with User Plane option
Proposes to support at least these two architectures in Rel-19
Proposes to use HTTP as transport for the signalling protocol between the AIoTF and the (UE or BS) Reader

## Slide 3: T1 architecture with Direct Path
T1 architecture with Direct Path
Protocol stack for T1 architecture with Direct Path
NOTE: In comparison to TR 23.700-13 Figure 8.1.2-3 the names in the protocol stack have been changed on purpose (for comparison with the T2 architecture) as follows:
  “AIoT” renamed to “AIoT NAS”
  “AIoT Reader Control” renamed to “AIoT-AP”

## Slide 4: T2 architecture with User Plane option
T2 architecture with User Plane option
Protocol stack for T2 architecture with User Plane option
NOTE: In comparison to TR 23.700-13 Figure 8.1.3.2-2 the protocol stack figure has been simplified by omitting the NEF and AF

## Slide 5: Comparison of T1 Direct Path with T2 User Plane
Visual comparison between the two architectures shows striking similarity in that both the UE Reader and the BS Reader communicate with the AIoTF via the AIoT-AP protocol
The main difference is in the nature of the traversed lower layer nodes
  The communication between BS Reader and AIoTF traverses TNL nodes that are outside 3GPP scope (e.g. IP routers) and can be assumed to be contained entirely within the operator’s private network
  In contrast, the communication between the UE Reader and the AIoTF traverses NG-RAN and UPF-PSA. Nevertheless, deployment-wise the N6 interface terminating the UE Reader’s PDU Session can still be made to be contained within the operator’s « walled garden »
The two protocol stacks can be further harmonized by assuming a common transport protocol for AIoT-AP
  NG-AP relies on SCTP which is not ideal for the UE Reader because of the absence of native SCTP support in operating systems
  Even for the BS Reader it is not obvious why SCTP should be used as a transport protocol. Specific TCP-related issues (e.g. Head-of-Line blocking) that led to the definition of SCTP may not be so impactful in the AIoT context, e.g. assuming that the AIoT signalling traffic will be low in volume and with no stringent timing requirements. (BTW it is noted that the 5G SBA relies on TCP and not on SCTP.)

## Slide 6: Proposal: HTTP as transport for both architectures
Protocol stack for T2 architecture with User Plane option
By using HTTP as transport the AIoTF needs to support only one stack for communicating with both BS Readers and UE Readers
NOTE: Whether HTTP should rely on TCP or QUIC can be left for further consideration to relevant stage-3 WGs
Protocol stack for T1 architecture with Direct Path

## Slide 7: Is T1 architecture with Indirect Path (via AMF) needed?
The role of the AMF in the Indirect Path architecture is primarily to serve as a message relay
One argument of the AMF proponents is that the use of the AMF would also allow for re-use of the N2 interface to existing public indoor gNB sites and even for re-use of a common gNB for AIoT an non-AIoT devices
We think that this argument is fallacious because:
  The maximum supported distance between the AIoT device and the BS Reader will often be much shorter than the public gNB range, even for indoor (e.g. warehouse) deployments. Therefore, in many deployments standalone BS Readers will be needed anyway
  The BS Reader is likely to be an inexpensive product that does not compare in complexity with a gNB. Imposing the complexity of the NG-AP stack on a standalone BS Reader would be an overkill
  There is no issue to collocate a standalone BS Reader with an existing gNB on an existing gNB site. The two can co-exist and operate like “ships in the night”, potentially sharing common lower layers (IP and below), including common network domain security
On the other hand, if certain deployments require a CN node located close to the RAN, this node can be an AIoTF proxy (rather than an AMF)

## Slide 8: Proposal
Proposal 1: Agree to progress at least the following two architectures in Rel-19 for normative work
  T1 architecture with Direct Path and Indirect Path (via AIoTF Proxy)
  T2 architecture with User Plane option
Proposal 2: Agree to use HTTP as transport for the signalling protocol between the AIoTF and the (UE or BS) reader
Both proposals are implemented in the companion pCR in S2-2412189