## Slide 1
SA2 Discussion paper on slice validity time (R19) By Oracle/Verizon – 2/17/2025 (SA2 #167)

## Slide 2
According 23.501 R19 5.15.16 - A network slice may be available for all UEs or a limited number of UEs only for a limited time that is known at the network in advance .
According 23.501 R19 5.15.16 - The AMF may receive slice validity time from any of the following data sources: OAM or UDM or NSSF.
Some operators prefer to use NSSF as the only data source due to its centric nature, and due its ability to update the AMF(s) on-the-fly (dynamically).
In R19, Nnssf_NSSelection service does not return slice validity time to the AMF (however, slice availability in the current TA is returned, NSAG information, slice mapping information are returned).
AMF might be configured by default with un-limited slice validity time for all S-NSSAIs
R18 slice validity time background (23.501/502)

## Slide 3
slice validity time gone wrong #1… Nnssf_NSSAIAvailability service un-avilable
AMF
NSSF
Nnssf_NSSelection GET: [Query parameters]
Nnssf_NSSelection GET Response: [slice info, No validity time]
Nnssf_NSSAIAvailability_Subscribe:[subscription data]
Nnssf_NSSAIAvailability_Subscribe response: 503 Service Unavailable
UE
REGISTER [slice info, TA,…]
REGISTER ACCEPT [slice info, No validity time]
UE may establish PDU session on S-NSSAI that is about to expire
Nnssf_NSSAIAvailability_Subscribe:[subscription data]
Nnssf_NSSAIAvailability_Subscribe response: [201 ok, No validity time]
Nnssf_NSSAIAvailability_Notify:[slice validity time]
Nnssf_NSSAIAvailability_Notify response:[204 ok]
UCU:[slice validity time]
UE may need to terminate PDU session
Retry
Call flow is based on 23.502/29.531 R19

## Slide 4
AMF
NSSF
Nnssf_NSSelection GET: [Query parameters]
Nnssf_NSSelection GET Response: [slice info, No validity time]
Nnssf_NSSAIAvailability_Subscribe:[subscription data]
Nnssf_NSSAIAvailability_Subscribe response: 201 ok
UE
REGISTER [slice info, TA,…]
REGISTER ACCEPT [slice info, No validity time]
UE may establish PDU session on S-NSSAI that is about to expire
Nnssf_NSSAIAvailability_Notify:[slice validity time]
UCU:[slice validity time]
Msg was lost
Retry
Nnssf_NSSAIAvailability_Notify:[slice validity time]
Nnssf_NSSAIAvailability_Notify response:[204 ok]
UE may need to terminate PDU session
slice validity time gone wrong #2… Nnssf_NSSAIAvailability Notification gets lost
Call flow is based on 23.502/29.531 R19

## Slide 5
We can see that providing an elementary piece of information (such as slice validity time) in a separate service than the NS Selection service, can cause some race conditions issues.
We can fix slice validity time issues by copy & paste what has been done for slice availability as follows.
Slice validity time info will be provided in NS Selection response. NOTE: the NSSAI in NS Selection is limited to the allowed nssai and configured nssai for a specific UE. Hence, even if NSSF provides slice validity time if a response to NS Selection Get request, Nnssf_NSSAIAvailability providing slice validity time still adds value as it can provide the AMF slice validity time for additional slices.
R19 slice validity time observations (23.501/23.502/29.531)