## Slide 1: VFL inference parameters
Thomas Belling
Nokia

## Slide 2: Problem statement
An NWDAF as VFL server is triggered by an analytics request or subscription to perform inference
The request can contain parameters as defined in Clause 6.1.3 of TS 23.288
The provided analytics can also provide response parameters as defined in Clause 6.1.3 of TS 23.288
It needs to be determined which of those parameters can be handled by the VFL server alone, and which parameters require related interactions with the VFL clients
This issue is reflected in the following EN: Editor's note: It is FFS whether additional parameters are needed to send from the VFL server to VFL client, e.g. parameters used in training phase and parameters from Analytics request. Editor's note: It is FFS additional parameters are needed to send from the VFL client to VFL server
The author believes that the parameters listed in slides 3 and 4 may need to be propagated to / received from VFL clients. Feedback is invited

## Slide 3: From TS 23.288 Clause 6.1.3 Contents of Analytics Exposure: Parameters that may need to be propagated to VFL clients
The consumers of the Nnwdaf_AnalyticsSubscription_Subscribe or Nnwdaf_AnalyticsInfo_Request service operations described in clause 7 provide the input parameters listed below.
Analytics Reporting Information with the following parameters:
  (Only for Nnwdaf_AnalyticsSubscription_Subscribe) Analytics Reporting Parameters as per Event Reporting parameters defined in Table 4.15.1-1 of TS 23.502 [3].
  Analytics target period: time interval [start..end], either in the past (both start time and end time in the past) or in the future (both start time and end time in the future). …
  [OPTIONAL] Data time window: if specified, only events that have been created in the specified time interval are considered for the analytics generation
  [OPTIONAL] Preferred level of accuracy of the analytics ("Low", "Medium", "High" or "Highest").
  [OPTIONAL] Dataset Statistical Properties: information in order to influence the data selection mechanisms to be used for the generation of an Analytics ID
  Time when analytics information is needed (if applicable): indicates to the NWDAF the latest time the analytics consumer expects to receive analytics data provided by the NWDAF
  [OPTIONAL] Preferred granularity of location information: "TA level", "cell level" or "longitude and latitude level".
  [OPTIONAL] Preferred orientation of location information: ("horizontal", "vertical", "both").
  [OPTIONAL] Analytics metadata request: indicates a request from one NWDAF to another NWDAF to provide the "analytics metadata information" related to the produced output analytics. This input parameter indicates which parameters in "analytics metadata information" are required to aggregate the output analytics for the requested Analytics ID(s).

## Slide 4: From TS 23.288 Clause 6.1.3 Contents of Analytics Exposure: Parameters that may need to be returned by VFL clients
Nnwdaf_AnalyticsInfo_Request service operations described in clause 7, the output information listed below, using a Nnwdaf_AnalyticsSubscription_Notify service operation or the Nnwdaf_AnalyticsInfo_Request response, respectively:
  Confidence: probability assertion, i.e. confidence in the prediction.
  [OPTIONAL] For each Analytics ID the Termination Request, which notifies the consumer that the subscription is requested to be cancelled as the NWDAF can no longer serve this subscription, e.g. due to user consent revoked, NWDAF overload, UE moved out of NWDAF serving area, etc.
  [OPTIONAL] Analytics metadata information: additional information required to aggregate the output analytics for the requested Analytics ID(s). This parameter shall be provided if the "Analytics metadata request" parameter was provided in the corresponding Nnwdaf_AnalyticsSubscription_Subscribe or Nnwdaf_AnalyticsInfo_Request service operation.
  - Number of data samples used for the generation of the output analytics;
  - Data time window of the data samples;
  - Dataset Statistical Properties of the analytics output used for the generation of the analytics;
  - [OPTIONAL] Data source(s) of the data used for the generation of the output analytics;
  - [OPTIONAL] Data Processing, if applied on the data collected for the generation of the output analytics;
  (Only for error response or error notification) Revised waiting time: indicates to the consumer a revised waiting value for "Time when analytics information is needed".