## Slide 1: NWM R20 AI/ML Discussion: Proposal on AI/ML sharing/exposure to the UE
Apple, OPPO
S2-2501545

## Slide 2: Analysis of AI/ML sharing/exposure to the UE
The AI/ML NWM moderated discussion has captured a number of separate but potentially related proposal related to the exposure of AI/ML related information/models to the UE, in particular:
  WT1.3: Study how to support model transfer/delivery to the UE according to RAN1/RAN2 considerations documented in 3GPP TR 38.843, including potential enhancements to policy control and OAM
  WT1.4: Study whether and what entities or functions transfer the AI/ML model or information to the UE
  WT2.4: Enhancements to support AI/ML exposure
  WT3.4: Study whether and how 5GC exposes information to UE
It appears that while WT1.3/WT1.4 relate to the exposure of RAN-focused AI/ML models to the UE, WT2.4/WT3.4 are more generic and may comprise other type of 5GC AI/ML related information (e.g. NWDAF analytics). It is unclear whether WT2.4 includes UE and AF or just one entity
All WTs above share the commonality that any information potentially shared with the UE would come from the 5GC

## Slide 3: Proposal for AI/ML sharing/exposure to the UE
Given the previous analysis, it seems reasonable to assume that solutions to the previous WTs could entail large commonalities, and studying them separately could imply large overlapping efforts on similar problems by SA2
  A significant number of companies seem to support one or multiple of the UE exposure related WTs
Therefore, we propose the following re-structure to be considered for the NWM moderated discussion on AI/ML enhancements:
  Group WT’s 1.3/1.4/2.4/3.4 under a single separate WT on exposure/sharing of AI/ML models and information to the UE (detailed wording TBD), including considerations captured in TR 38.843
    UE data collection aspects, exposure to the AF may be captured as separate WTs/KIs
  The corresponding RAN dependencies should be indicated, as well as dependencies to any other SA or CT WGs

## Slide 4: ANNEX: Details on UE exposure proposal in SP-241847

## Slide 5: Background
Rel-18 FS_AIMLsys studied 5GC information exposure to UE in SA2, and documented it in TR 23.700-80 as follows:
  KI description was documented in cl. 5.2 (KI#2)
  9 Solutions were proposed and documented (see cl. 6.0), with numerous companies involved in the discussions
  Evaluation of solutions was documented in cl. 7.2
During the evaluation phase, an LS was sent by SA2 to SA1 and SA3 seeking feedback on requirements and security of network information exposure to the UE (see S2-2205286)
The resulting LS exchange was inconclusive based on the following developments:
  SA3 replied to SA2 that a “Study on Security and Privacy of AI/ML-based Services and Applications in 5G” was being carried out and documented in TR 33.898 (see S3-221621/S2-2205455), but it only addressed and concluded exposure to AF (not UE)
  SA1 did not agree to a reply LS to SA2
The inconclusive LS exchange resulted in a conclusion for KI#2 FS_AIMLsys in cl. 8.2 indicating no Rel-18 normative work was to be pursued, despite further external LS in showing interest on the topic (see e.g. S2-2210182, from 5GAA)

## Slide 6: Use Cases for Rel-20
The UE would benefit from the capability to request and receive NWDAF analytics from the 5GC to support a number of application and network related operations
Examples of such operations/use cases and relevant analytics:
  Analytics exposure to support AIML operation splitting
    This AIML operation is captured in cl. 6.40.1 of TS 22.261 and has not been addressed yet
    Relevant analytics in TS 23.288 could include e.g. slice load (cl. 6.3), NF load (cl. 6.5), network performance (cl. 6.6), User Data Congestion (cl. 6.8), QoS sustainability (6.9) etc. as they would assist the UE to determine how and when to split the AI/ML model taking the network and UE status into account
    Privacy/security aspects were left unaddressed (e.g. the network may prevent the UE from receiving the information which is not private/secured); SA3 should be involved
  Exposure of relative proximity analytics (cl. 6.19 in TS 23.288) to assist UE ProSe operation and/or model transfer among UEs
    Predictions on proximity information to other UEs could be leveraged by the UE receiving the information
    Cl. 6.40.2 of TS 22.261 describes requirements for model transfer among UEs largely not addressed

## Slide 7: Proposal
It is proposed to include the topic of network exposure to the UE as part of an SA2 Rel-20 5G-Advanced study on AI/ML enhancements
  This proposal implies to consider whether and which exposed 5GC-related information to the UE can be considered within 3GPP scope
  Continue and complete the discussion initiated in Rel-18 FS_AIMLsys (TR 23.700-80)
It is further encouraged to have a discussion in SA2 during the Rel-20 5G-A preparation phase on how to include the above, e.g.
  Whether further study/new solutions would be required in SA2
  Whether further LS exchange with SA1/SA3 would be required
  Whether and how to revisit the conclusion of KI#2 of Rel-18 FS_AIMLsys on 5GC information exposure to UE