## Slide 1: Triggering VFL training – Way Forwards
SA2#167
Lenovo
S2-2501547

## Slide 2: Background
Triggers for HFL
  Consumer (AnLF) discovers an MTLF from the NRF based on Analytics ID and other parameters.
  During MLModelProvision service request from a consumer (AnLF). MTLF determines HFL is needed based on:
    Operator policy (e.g. pre-configured list of ML Models),
    Analytic ID,
    Service Area/DNAI
    or data can not be obtained directly from data producer NF (e.g. due to privacy reasons).
  If the NWDAF containing MTLF can not perform as FL Server NWDAF, the MTLF first discovers and selects FL Server NWDAF from NRF by invoking the Nnrf_NFDiscovery_Request service operation
  Co-located AnLF/MTLF scenario is not precluded but not captured in TS 23.288 (it is a deployment option)
  Consumer (AnLF) is not involved in MTLF/FL server selection for ML model training using HFL

## Slide 3: Current status for VFL (Inference and Training)
VFL server supports both AnLF and MTLF functionality
  VFL Inference (as an AnLF) and VFL Model Training (as an MTLF).
NWDAF/AF acting as VFL server registers VFL server capability at NRF
Inference Scenario 1: Analytics Consumer sends analytics request to AnLF supporting VFL server
Inference Scenario 2: Analytics consumer sends analytics request to a “dedicated” AnLF

## Slide 4: Scenarios for triggering VFL training
Scenario 1: AnLF requests ML model from an MTLF which also supports VFL server
  As per agreements MTLF supporting VFL server is also supporting VFL inference (AnLF) functionality
  As per HFL scenario consumer (AnLF) discovers an MTLF from the NRF and requests for an ML model by triggering an MLModelProvisioning service request.
  MTLF determines VFL is needed based on e.g. Operator policy (e.g. pre-configured list of ML Models), Analytic ID
  Consumer (AnLF) is notified that no ML model is provided
  As per HFL consumer (AnLF) is not involved in MTLF/FL server selection for ML model training using VFL

## Slide 5: Scenarios for triggering VFL training
Scenario 2: AnLF requests ML model from a “dedicated” MTLF
  As per HFL scenario consumer (AnLF) discovers an MTLF from the NRF
  If the selected MTLF can not perform as VFL Server, the MTLF first discovers and selects a VFL Server
    Selected MTLF selects an AF to train the ML model
    Option for MTLF to select another MTLF is not precluded as MTLF registers to NRF VFL server capability
  As per scenario 1, consumer (AnLF) is informed that no ML model is provided.
  As per HFL consumer (AnLF) is not involved in MTLF/FL server selection for ML model training using VFL

## Slide 6: Scenarios for triggering VFL training
Scenario 3: Selected AnLF by an Analytics consumer is also an MTLF supporting VFL server functionality
  This is a “special case” where the AnLF selected by a consumer is also an MTLF supporting VFL (VFL server).
  MTLF collocated with AnLF may trigger VFL if there is no associated ML model for the analytics requested by the consumer.
  Analytics consumer selects AnLF as per existing procedures (i.e. does not ensure selection of an VFL server AnLF)
  This “special case” is not precluded (deployment option)

## Slide 7: Proposed way forwards
Capture all described options in TS 23.288

## Slide 8: Thank you.