## Slide 1: Discussion on the epoch issue for 5G Residence time calculation
ZTE

## Slide 2: Issue in the (g)PTP time synchronization over 5GS
The 5G Residence time = TSe – TSi
TSe and TSi are the time offset since the epoch.
The issue is: how to guarantee the DS-TT and NW-TT use the same epoch for the TSi/TSe calculation.
There are several well-known epochs.
  GPS epoch (began at 1980-01-06 00:00 UTC ),
  PTP epoch (began at 1970-01-01 00:00 ATI ),
  …………………
The epoch is the origin of the timescale of a domain.
timescale: A measure of elapsed time since an epoch.
Notes: The GPS epoch began at 1980-01-06 00:00 UTC (Coordinated Universal Time )
The PTP epoch is 1 January 1970 00:00:00 TAI (International Atomic Time)
<dLS> = TAI ─ UTC
NOTE 1— As of 0 hours 1 January 2017 UTC, UTC was behind TAI by 37 seconds. At that moment, the PTP-defined value of <dLS> was +37 seconds, as designated in the applicable Bulletin C (see Clause 2).

## Slide 3: Background – AS level time sync
In the 38.331
  timeInfoType: If timeInfoType is not included, the time indicates the GPS time and the origin of the time field is 00:00:00 on Gregorian calendar date 6 January, 1980 (start of GPS time). If timeInfoType is set to localClock, the origin of the time is unspecified.
  It means, the GPS epoch is used (if timeInfoType is not included), or epoch is not specified if timeInfoType is set to localClock
Observation 1: In the AS layer, the UE know the which epoch is used in air interface (e.g. SIB9).
  The GPS epoch is used (if timeInfoType is not included), or
  epoch is not specified if timeInfoType is set to localClock

## Slide 4: Background
In the 23.501
  The UE, gNB, UPF, NW-TT and DS- TTs are synchronized with the 5G GM (i.e. the 5G internal system clock) which shall serve to keep these network elements synchronized. (clause 5.27.1.1)
  The 5G internal system clock shall be made available to all user plane nodes in the 5G system. The UPF and NW-TT may get the 5G internal system clock via the underlying PTP compatible transport network with mechanisms outside the scope of 3GPP. (clause 5.27.1.2.1)
Observation 2: The gNB and NW-TT, have synchronized with the 5G GM (i.e. the 5G internal system clock). Which epoch is used is not specified. This rely on the deployment/implementation

## Slide 5: Background
In the 23.501 clause 5.27.1.2.2.1 Distribution of gPTP Sync and Follow_Up messages
  The mechanisms for distribution of TSN GM clock and time-stamping described in this clause are according to IEEE Std 802.1AS [104].
In the 23.501 clause 5.27.1.2.2.2 Distribution of PTP Sync and Follow_Up messages
  The mechanisms for distribution of PTP GM clock and time-stamping described in this clause are according to IEEE Std 1588 [126]
Observation 3: Time stamping (i.e. TSi and TSe) follows the IEEE 802.1AS and IEEE 1588

## Slide 6: Background
In the IEEE 1588, there are two types of timescale (clause 7.2.1)
  The timescale PTP: This is the elapsed time since the PTP epoch measured using the second defined by International Atomic Time
  The timescale ARB (arbitrary): In normal operation, the epoch is set by an administrative procedure.
In the clause 8.2 of 802.1AS, it is similar with IEEE 1588.
Both 1588 and 802.1AS define the converting between timescales
In the 802.1AS, Annex C (Timescales and epochs), it provides some example of Timescales and epochs

## Slide 7: Observation
Observation 4: The IEEE 1588 and IEEE 802.1AS does not mandate which epoch to be used.
In the TSN time domain, there are multiple timescales.
When 5G supports integration of TSN network, the UPF/NW-TT needs to synchronize with the GM in the TSN time domain.
Observation 5: The operator know which epoch is used by the outside TSN network, i.e. (g)PTP message of TSN time domain.

## Slide 8: Background
In the ST 2059-2:2015: "SMPTE Standard - SMPTE Profile for Use of IEEE-1588 Precision Time Protocol in Professional Broadcast Applications". (In the 23.501, reference [127])
  The SMPTE Epoch shall be 01 January 1970 00:00:00 TAI.
  Note 1: The SMPTE Epoch is the same as the PTP Epoch specified in IEEE Std 1588-2008.
Observation 5: If the external TSN network use the SMPTE profile, the epoch used in the PTP message is PTP epoch.
Notes: SMPTE Profile for Use of IEEE Std 1588 [126] Precision Time Protocol in Professional Broadcast Applications ST 2059-2:2015 [127];

## Slide 9: Observation
In the 3GPP air interface, the GPS epoch may be used (or not specified)
The gNB and NW-TT, have synchronized with the 5G GM (i.e. the 5G internal system clock), which epoch is used is not specified.
Time stamping (i.e. TSi and TSe) follows the definition in the IEEE 802.1AS and IEEE 1588
The IEEE 1588 and IEEE 802.1AS does not mandate which epoch to be used
When 5G supports integration of TSN network, the operator know which epoch is used by the TSN network according to SLA.
  NW-TT know the epoch used by received (g)PTP message.
  DS-TT also need to know the epoch used by received (g)PTP message. (at least for Up link time synchronization)
If the external TSN network use the SMPTE profile, the epoch used in the PTP message is PTP epoch.

## Slide 10: Proposal:
How to guarantee the DS-TT and NW-TT use the same epoch for the TSi/TSe calculation.
Alt 1: There is nothing to do for the 3GPP std. It can be defined by operator’s Std.
Alt 2: Clarifying in the 23.501, which epoch is used by DS-TT and NW-TT for TSi/Tse is configured by operator’s policy/configuration.
Alt 3: Explicitly clarify, the epoch is used by DS-TT and NW-TT for TSi/Tse is GPS epoch, or PTP epoch.
Alt 4: ?

## Slide 11: Annex
Various 5G internal GM deployment

## Slide 12: Annex
AS level
(g)PTP level
UE
(gNB
(g)PTP level
UPF/NW-TT
GPS epoch
timeInfoType is not included
5G GM
GPS epoch
GPS epoch
GPS epoch?
GPS epoch?

## Slide 13: Annex
AS level
(g)PTP level
UE
(gNB
PTP
SyncE
(g)PTP level
UPF/NW-TT
Epoch?
timeInfoType = local clock
5G GM
epoch?
epoch?
epoch?
epoch?

## Slide 14: Annex
AS level
(g)PTP level
UE
(gNB
PTP
(g)PTP level
UPF/NW-TT
GPS Epoch
5G GM
GPS epoch
PTP epoch?
epoch?
epoch?
timeInfoType is not included