## Slide 1: Topics for 6G study
Lenovo

## Slide 2: Outline
Organize the 6G SID in phases: initial SID and updated SID
  Page 3 ff. show the content of the 6G Initial SID
Initial SID
Updated SID
WID
  Initial SID: includes objectives to be studied without SA1 6G service requirements:
  Study enhancements for Control Plane, User Plane, mobility/session management, QoS, IWK, Sensing, etc.
  Check point for agreed SA1 service requirements
  Updated SID (e.g. after Q2 2026)
  Include potentially additional objectives based on agreed SA1 service requirements for 6G.

## Slide 3: View on 6G Initial SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
1. | Common 6G system architecture aspects | Based on the 5GS SBI architecture, study 6G system architecture which should allow for simplified deployment of new features and services, i.e. with minimal impact to the baseline 6G architecture. Study which NFs and functionalities from 5GS can be re-used, which NFs needs to be re-designed. This may include IWK and migration aspects with 5G/4G. | Study which 5G NFs can be re-used and be common for 5GC and 6G CN. | SA1, SA3, RAN
2. | Introduce SBI for the N2 interface | Study how to enable a direct communication between the RAN and CN NFs in 6G. The following use cases will be studied: Whether to allow direct data/signalling exchange triggered by the CN NFs to the RAN or also by the RAN to the CN NFs. Whether partial (e.g. only limited network services supported like Sensing) or full integration of the RAN in the service-based interfaces. | During the 5GS standardization there are several procedures for which a direct communication between a CN NF and RAN can be beneficial, e.g. MBMS, Ambient IoT, network analytics, etc. New 6G services may also benefit from a direct communication with the RAN. | RAN3
3. | Enhancements to the communicaiton between UE and 6G CN (including 6G NAS protocol) | Study how to design the communication between the UE and the 6G CN NFs. It may include the following aspects: Possible enhancements to the NAS over the control plane; Possible enhancements to the User Plane for exchange with network services; Introduce a new data plane for data collection. | The NAS protocol in 5G has been used not only for MM and SM management, but also as transport protocol for network services (e.g. LPP). The introduction of new 6G services may required the increased data exchange between UE and CN. New way of communication may need to be explored. | SA1

## Slide 4: View on 6G Initial SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
4. | Enhancements to QoS framework | Study enhancements to the QoS framework to support applications with dynamic traffic characteristics | The enhancements for XRM in 5G-A introduced some flexibility for XRM applications with different traffic flows. Further flexibility for applications with dynamic traffic characteristics may be required in 6G. | SA4
5. | ISAC | Study how to support the ISAC service requirements in the 6G system including at least the RAN based sensing with or without UE assistance (it is FFS whether to study the UE-based sensing). Study mechanisms (e.g. AI based) how to improve the accuracy of the sensing result generation. NOTE: The scope of ISAC topic depends on the outcome of Rel-20 5G-A SID. | SA1 specified ISAC service requirements for 5G-A which will not be specified in stage 2 and 3. The 6G network operators are expected to monetize the sensing service in the 6G system. | SA3, RAN
6. | Support of Native AI within the 6G system architecture | 6.1 NWDAF framework enhancements: enhance the existing NWDAF framework supporting new AI/ML learning techniques and define new analytics to enable intelligent automation and improved service delivery. 6.2 AI for Network: Study how to enable "native AI" support within the system architecture. Study whether and how a new signalling plane is needed to be defined to support AI-related communications to AI-enabled functions across the system architecture including UE, RAN and core network functions. NOTE: WT 6.2 depends on stage 1 requirements 6.3: Unified Data Collection: Study whether and how a unified data collection framework can support AI-related operations. The aim is to support a data collection from different sources including OAM, RAN and CN NFs and retrieving data for different types (e.g., sensing data, AI-generated data) in a unified way ensuring efficient data management and reduced complexity. | Support for AI/ML in the 6G system having as basis the existing NWDAF framework. | RAN, SA3 SA1 for AI agent requirements

## Slide 5: View on 6G Initial SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
7. | Network slicing | Study whether and how to improve the network slicing to avoid extensive configuration of the UE. For example: Minimize the pre-configuration in the UE. Avoid configuration of area restrictions for a network slice. | The network slicing feature in 5GS (which includes multiple sub-features) relies on the support and configuration in the UE. The 6G CN offers the possibility to re-think the network slicing to make it less dependent on UE support and configuration. | 
8. | Integration of non-3GPP access into 6GS | Study the integration of non-3GP access in the 6G system to provide easier deployment and offer a more seamless continuity experience for the users, e.g., by enabling seamless mobility between 3GPP and non-3GPP access and network-triggered handovers. | Non-3GPP technologies can provide backup connectivity in case of failures, can offload the 3GPP access, and can empower multiaccess connectivity. The 5GS was designed to integrate non-3GPP accesses and align the RAN-CN interfaces between 3GPP and non-3GPP accesses. Simplified integration should be studied in 6G. | 
9. | Energy Efficiency | Study the support of mechanism which lead to energy efficiency, e.g. enable multiple energy states for NFs/RAN, consider energy-related analytics and/or AI, consider energy budget information. | The energy efficiency is important feature to achieve emission/ CO2 neutrality in 6GS deployments. | SA1, SA5
10. | Compute as a Service (CaaS) | Study how to provide compute resources to 3rd party service providers (i.e. Compute as a Service). Study how to expos network-based compute services on-demand (e.g. similar to the exposure of existing network services). NOTE: This objective depends on outcome of Rel-20 5G-A SID on ISAC | SA1 studies the service requirements to utilize the distributed compute resources and exposes them to third parties via standardized APIs. | SA1, SA5

## Slide 6: Summary
Proposal
  Agree on initial 6G SID by SA2#170 meeting including:
    General system architecture aspects based on the 5GS SBI architecture
    Support of new 6G functionalities (e.g. AI/ML, unified data collection, SBI-based RAN)
    Improvement of existing 5GS functionalities (e.g. enhancements to QoS framework, Network slicing, Integration of non-3GPP access)
  Check the agreed 6G service requirements by SA1 (e.g. Feb. 2026) and update the objectives of the 6G SID