## Slide 1: 6G System Scope
NOKIA, Spark NZ Ltd

## Slide 2: Outline
This document proposes Technical areas that need to be addressed as part of 6G System Study in Rel-20.

## Slide 3: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
1 | Architecture principles | Architecture principles and assumptions that would apply for 6G System | High level design principles are critical to study and document. | None
2 | 6G System Architecture | 6G System Architecture – Roaming & Non-Roaming | It is critical to study the system architecture that will be applicable for 6G UE(s) and 6G Radio. It is also critical to study architecture requirements for 6G use cases in SA1 TR 22. 870. | None
3 | Registration, Connection and Session Management procedures | Modular NAS framework with distributed NAS termination impact to RM, CM and SM procedures should be studied. System procedure impact due to NAS protocol optimizations. | In general, system impact due to optimizations to NAS protocol must be studied. Modularity is critical for support of different types of devices; similarly orthogonality from network standpoint, enabling also differentiated security. | SA3, RAN2, RAN3
4 | 6G Identifiers & Subscription aspects | Temporary and permanent identifiers, Temporary and permanent subscription, Onboarding and system impact due to network selection for PLMN and SNPN, SNPN ID, Equivalent SNPN list support. | It is important to define UE identifiers, enable new business models also for PLMNs and SNPNs to support temporary services besides the permanent subscription model | SA3, RAN2, RAN3
5 | QoS enhancements | Enhancement needed to support adaptive QoS framework for adaptive and high bandwidth applications, mobile AI traffic | As the traffic grows, need a mechanism to improve QoE and capacity utilization for increased traffic due to AI/ML, other apps. | RAN2, RAN3

## Slide 4: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
6 | Resiliency | Support for 6G System Resiliency, especially control plane resiliency | Standards enhancements needed for resiliency must be specified. Zero down time is critical | RAN2, RAN3
7 | Basic and auxiliary services | SMS, PWS, IMS multimedia services (MMTEL), Emergency services, Basic location services, basic time sync (with the ability for 3GPP system to have the same time reference), considering also GNSS independent positioning and time sync support. Access specific enhancements needed for IMS should be part of 6G SID. NOTE: IMS specific enhancements (access agnostic) must be in a separate study, if needed. | Important to support existing services and services beyond connectivity for feature parity, revenue generation | RAN2, RAN3, SA3
8 | Interworking with 5G | Single registration based Interworking with 5G needs to be specified, | Critical for success of 6G deployment | RAN2, RAN3
9 | Access agnostic system | Support for non-3GPP access functionality. Non-3GPP access related specifics of RM and CM states and registration procedures. | Important to support n3Ga from day-1 for wifi calling, traffic steering switching and splitting between 3GPP and non-3GPP access. | RAN3, SA3
10 | Network slicing | Support for network slicing smooth interworking and mobility between 5G and 6G for network slicing, discussion on the UE impacting features to be supported in the first release and any improvement of URSP rules support for network slicing consider enhancements that improve monetization | 6G support for network slicing needs to be studied | RAN2, RAN3, SA3
11 | Fixed wireless access | Study any optimizations needed for FWA, critical to enable mobility and UP optimizations needed for FWA devices | FWA is a growing market that would benefit from simplified mobility procedures and improved UP optimization to meet traffic demand | RAN2, RAN3

## Slide 5: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
12 | Energy savings and energy related work. | Ensure energy efficient system from day-1. Study system impact due to energy savings and other aspects related to energy. | 6G System must be energy efficient from day-1; Energy savings mindset is critical | RAN2, RAN3, SA5
13 | AI/ML native 6G System | Native AI/ML for 6G System, including data collection for AIML | Native integration of AI/ML is essential to fully leverage the benefits for 6G System | All other SA WGs, 3GPP RAN WGs
14 | PDU Session types & User plane architecture | Enablers needed for enhanced UP architecture, SSC modes and related aspects. Protocols to be supported for PDU Sessions, including unstructured, ETH and IP sessions. Transparent integration 6GS in industrial ethernet networks especially using the bridge model. | Growing traffic will require optimizations in UP architecture, also enable different topology for varying deployment needs | RAN2, RAN3
15 | Edge Computing, Compute Offload and AI as a Service | Enablers for the support of edge computing for the optimal use of locally deployed services and content (including, e.g., edge application server selection and traffic steering) Enablers for compute offload for low latency or compute intensive applications such as XR Enablers for AI as a service use cases | These enablers would be critical for providing improved user experience for low latency or compute intensive applications especially for wearable devices unlocking new value opportunities for the CSPs through the ability to optimally utilize available resources | None
16 | Exposure framework | Use of CAPIF for core exposure and functional split between NEF & CAPIF, Enabling authorization framework also for in-band and on-path exposure | Enforcing use of CAPIF is critical for support of unified exposure framework | SA6, SA3
17 | In-band and On-path application Network interaction | Introduce a capability to securely exchange information and expose services between application (client/UE and server/AS) and network (UPF) in-band and on-path with regards to application’s end-to-end communication. | Allowing apps to interact with the network on-path and in-band wrt. their app layer session is preferred by many app providers and also enables the lowest latency communications channel between the apps and the network | SA4, SA3

## Slide 6: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
18 | Data storage architecture | Data storage architecture related to subscription, policy, exposure and other aspects needed for 6G. | Classic date storage architecture is critical for managing subscription, policy and exposure. | None
19 | System aspects of security | Architectural and system procedure impact due to security | It is essential to study the architectural and procedural impact for security aspects | SA3
20 | PNI-NPN and Femto | Need to introduce the ability for PLMN to support localized network and Femto. Support of Closed Access Groups (CAG) concept including access control and mobility between non-CAG cell and CAG cell (5G and 6G). | Ability to support different deployment models | RAN2, RAN3
21 | NTN | Support for NTN integration – study roaming & interworking for TN-NTN, Multi-orbit support. Study GNSS-independent NTN operation for devices.​ | Support for NTN is critical for day-1 to maximize similarities between TN and NTN​ | RAN1, RAN2, RAN3, SA3​
22 | Managing UE data connectivity | Ability for an operator to control and manage UE data connectivity | Operator needs to be able to configure the policies for UE to manage connectivity | None
23 | LPWA | Define system enablers needed for LPWA | Foundational enablers needed for LPWA will be good to specify for forward compatibility | 3GPP RAN
24 | Sharing scenarios | Study the ability to share any resource: RAN, core network, compute, | Enabling controlled sharing is critical for resiliency, unforeseen events, Energy efficiency etc. | None
25 | Support for industrial communication. | How to integrate 6G system in industrial ethernet network (Ethernet PDU and 6G as a bridge model) How deterministic services offered in 5G are made available in 6G (e.g. Dejittering) and which ones are needed | The 5G to 6G transition should be smooth and backward compatible. The important features of 5G should be supported in 6G as well. | None

## Slide 7: Summary
It is proposed that the technical areas identified in this proposal are included in the 6G System Study item scope for Rel-20.