## Slide 1: Title: Ericsson view on 6G SID Scope Content
Source: Ericsson
Agenda: 30.7.1
For Discussion

## Slide 2: Outline
6G study item structure and progress
6G SID Scope Content
Summary

## Slide 3: 6G study item structure and progress
SA concluded to have a checkpoint in Dec-25:
  “SA WG2 6G SI completion is no later than March 2027. TSG SA will have check point in December 2025 to further review SA WG2 6G SI completion date and make final decision on whether it is December 2026 or March 2027.”
The 6G SID is expected to be approved at SA#108 (June-25)
  Proposal: include an initial list of technical areas for study in the SID
During the initial phase of the 6G study, additional technical areas to be studied can be proposed and discussed
  Proposal: The 6G SID can be updated in 2H25 to include the additional technical areas for study
Proposal: The 6G SID should reflect this work structure:
  Objectives targeting Dec-25:
    Study initial set of technical areas (including lessons learnt from 5G)
    Discuss what additional technical areas to be studied
    Agree on baseline architecture, incl. principles assumptions, by Dec-25
  After Dec-25:
    Study the additional technical areas, building on the baseline architecture
    Continue to study the initial set of technical areas, as needed
Agreements on baseline architecture already in Dec-25 allows more time to work on the new 6G services

## Slide 4: Core network for existing and new services
Support existing services
  Build on the industry’s investments in 5GC
  Identify aspects, features, NFs etc. that can be reused from 5GC to a large extent, e.g. SBI, mobility, QoS, roaming and features that may need streamlining, updating, simplification etc., e.g., slicing, Non-3GPP Access.
Enable new 6G capabilities
  Enable new business innovation & monetization in 6G, e.g.
    Sensing (ISAC)
    AI native core network & management
    Immersive communication
  Extended capabilities, e.g.
    Data collection and management

## Slide 5: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
1 For Dec-25 | 6G System architecture baseline | Study and identify aspects, NFs etc that can be reused from 5GC. Focus on analyzing existing basic functionality (mobility, session, RAN-CN functional split, QoS model, UP model, slicing, roaming, policy control, user data management, exposure framework etc) to support legacy services (voice incl roaming, MBB, FWA). Focus on business-relevant multi-vendor interfaces and a standalone architecture for 6G RAT. | A baseline architecture should be agreed by Dec-25. This enables work to continue on the new 6G services. | RAN
2 For Dec-25 | Interworking | Study/define the principles for: Interworking between 5G and 6G Interworking between 4G and 6G It is assumed that interworking between 6G and 2G/3G is not required | Interworking with 5G is a key aspect to enable 6G deployments | 
3 For Dec-25 | Support for basic/regulatory communication services | Study how to support Voice, SMS and Emergency services via 6G RAN, including interactions with legacy voice services. It is our assumption that a 6G voice solution should be based on IMS. | 6G voice support is required for business and regulatory reasons from day 1 | 

## Slide 6: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
4 After Dec-25 | Simplification and enhancements | Study simplification opportunities of core network architecture based on learnings from 5G. Consider areas of improvement, e.g. consolidation or split of NFs/NF Services. | The number of NFs have increased with every release, not always showing actual commercial needs | 
5 After Dec-25 | Massive IoT | Study required support for Massive IoT. Build on learnings from 4G M-IoT deployments. Consider areas of improvement, e.g. simplified architecture with reduced number of options, avoid DoNAS. | Ensure that a solution for M-IoT is supported from the first release of 6G, building on learnings from 4G M-IoT | RAN
6 After Dec-25 | New value add services – e2e Integrated Sensing and Communication (ISAC) architecture | Study support for ISAC services | Enable new use cases and business opportunities for operators | RAN
7 After Dec-25 | New value add services – support for AI based management | Based on SA5 lead, study enablers for intent-based management of the network | Motivated by enabling operation efficiency, zero touch management etc. | SA5
8 After Dec-25 | New value add services – immersive comm services | Study capabilities to support immersive communication based on the relevant stage 1 KPIs. | New communication services discussed already in 5G, will evolve into 6G. Different models considered; e.g. MNO provided and OTT application service provider | SA1
9 After Dec-25 | Multi-purpose data architecture | Based on SA5 lead, study architecture and enablers for a distributed data management architecture for data collection, that is common for RAN, Core and OAM. SA2 should be a user of the data architecture and integrate it with relevant SA2 features. | A common data architecture can be utilized by features studied as part of other key objectives such as AI, exposure, sensing etc. | SA5/RAN3
NOTE: The “After Dec-25” topics are not reflecting a specific priority order

## Slide 7: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
10 After Dec-25 | Network slicing | Study support for network slicing in 6G including interworking with 5GS. Study whether network slicing can be simplified compared to 5G. | Ensure the basic (deployed) functionality as a minimum is working across 5GS and 6G. | RAN
11 After Dec-25 | Support for NTN | Goal should be to re-use to a large extent the solution defined for 5GS | NTN is assumed to be part of the initial 6G release | RAN
12 After Dec-25 | Non-3GPP access | Solution for interworking between non-3GPP access and the Core Network for 6G. Strive for a common solution for all non 3GPP accesses. | Define a single 6G solution based on learnings from 4G and 5G | 
NOTE: The “After Dec-25” topics are not reflecting a specific priority order

## Slide 8: Summary
Structure the 6G SID in two phases:
  Objectives targeting Dec 2025:
    Study initial set of technical areas
    Discuss what additional technical areas to be studied
    Agree on baseline architecture, incl. principles and assumptions, by Dec-25. The agreement should also include the technical areas to be studied after Dec-25.
  After Dec 2025:
    Continue to study the initial set of technical areas, as needed
    Study the additional technical areas, building on the baseline architecture
Core Network for 6G should support existing services and enable new 6G capabilities
  Continue monetize the evolution of 5GC based services, leveraging 5GS QoS framework, slicing, roaming, exposure etc.
  Extend capabilities e.g. for Data collection and management, AI native core network & management
  Enable new business innovation & monetization in 6G, e.g. Sensing/ISAC, Immersive communication.