## Slide 1: Areas of NEC interests in 6G architecture
NEC

## Slide 2: Outline
8 Areas for 6G SID Scope Content for Architecture requirements
Listed 6G workshop considerations then architectural topics following structure of TR22870 for 6G use cases in SA1
The sequence number does not show prioritizations

## Slide 3: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
1 | Basic network architecture | Study the basic 6G architecture including: Network Functions and interfaces (e.g., SBI) that support UE communication (e.g., Voice/SMS, IP or non-IP traffic) and beyond-communication services (e.g., AI/Computing/Sensing). Core network architecture supporting interaction with UE/RAN/Application Function. Support for Multi NAS/Modular NAS/Distributed NAS and related security issues. NGAP as an SBI-based interface. Support for 5G-6G Dynamic MRSS. Integrated RAN CU-UP and UPF. Dual Registration support. Cloud and AI-Native design from Day 1. | Outcomes in 6G workshop | SA3 RAN3 CT1/CT4 SA5
Note: the sequence number does not show prioritizations

## Slide 4: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
2 | Supporting operator provided multimedia services and IMS enhancement | Study 6G system to support for IMS Multimedia Telephony Service including: Real-time resource allocation and adaptation within the network. Efficient network capabilities for Multimedia Telephony Service, simplifying UE and network operations for voice-centric, satellite-access UEs, or devices with AI agents. Seamless continuity of IMS Multimedia Telephony Service between 6G and 5G VoNR for users moving between the two. Regional/national regulatory requirements for IMS Multimedia Telephony Service. | System and Operational Aspects, TR22870, SA1 | RAN WGs, SA3, CT1
3 | Energy saving | Study energy efficiency and saving architecture including: End-to-end Energy Efficiency improvements in the 6G system compared to the 5G system. Differentiated energy efficiency services to subscribers. Based on UE indication, the network applies power-saving technology to improve UE energy efficiency according to user requirements. Energy-related information collection from the radio access network (e.g., per UE granularity) to consider the impact of UE location (e.g., cell edge vs. cell center) on energy consumption. | System and Operational Aspects, TR22870, SA1 | SA5/CT1/CT4
Note: the sequence number does not show prioritizations

## Slide 5: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
4 | Computation Service | Study computation as a service consumed by UEs or authorized third parties including: Architecture to leverage computational resources by UEs or authorized third parties. APIs allowing authorized third parties to retrieve availability information about computational resources (e.g., storage, AI processing units, xPUs, etc.). Monitoring and reporting of computational resource usage. Discovery and selection of computation resources. | AI, TR22870, SA1 | SA5
5 | Data Service | Study data as a service consumed by UEs or authorized third parties including: Architecture for data service (e.g., collect, store, retrieve, expose). APIs allowing authorized third parties to retrieve data. Data plane protocols in 6GS. | AI, TR22870, SA1 | SA5
6 | AI Agent communication | Study AI Agent integration in 6GS including: Architecture for Agent communications. APIs allowing authorized third parties to consume Agent-based services. Access from UEs to AI Agents in 6GS. | AI, TR22870, SA1 | 
Note: the sequence number does not show prioritizations

## Slide 6: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
7 | Sensing | Study the 6G framework for integrating communication and sensing tasks including: RAN and UE-based sensing. Sensing Data Support, including detection, collection, processing, and exposure of sensing data. Fusion of 3GPP and non-3GPP sensing. | Integrated Sensing and Communication, TR22870, SA1 | RAN WGs, SA3
8 | Ubiquitous Connectivity . | Study Ubiquitous Connectivity including: Ubiquitous coverage through seamless integration of terrestrial and non-terrestrial networks. Resilient notification: Addressed user expectations for satellite-reliant communications in areas lacking terrestrial coverage. A notification mechanism was proposed to inform users when incoming calls or messages fail due to poor satellite reception. Multi-Orbit Satellite Access for Different Services: Examined potential benefits of using multi-orbit satellite networks (LEO, MEO, GEO) within 5G systems. This capability could enhance service experiences by leveraging different orbital characteristics, though simultaneous UE connections across orbits were deemed out of scope. | Ubiquitous Connectivity, TR22870, SA1 | SA3/CT1/Ct4
Note: the sequence number does not show prioritizations

## Slide 7: Summary
This contribution outlines key study topics for 3GPP 6G architecture development.
It encompasses fundamental network design aspects, including core architecture, network functions, and interfaces, as well as support for specific services such as IMS-based multimedia telephony, computation, data, and AI agent communication.
The contribution also emphasizes energy efficiency, ubiquitous connectivity, and integration of sensing capabilities.
These study areas will be crucial in defining the capabilities and architecture of future 6G networks, enabling innovative applications and meeting the evolving needs of users and operators.