## Slide 1
Discussion for 6G Study on Interworking and Migration
Agenda item: 30.7
Source: Samsung
Document for: Discussion
3GPP SA WG2 Meeting #168
07 – 11 April, 2025, Goteburg, Sweden
S2-2503377

## Slide 2: Lesson Learned from 5G
Standalone architecture only from day one
In 6G, it is proposed to consider only standalone architecture for 6G
5G Rel-15 introduced too many network architecture options
  5 options (2, 3, 4, 5, 7) standardized
  Only 2 options (2, 3) deployed
SA deployments are delayed due to the existing NSA operation
5G Network Architecture
6G Network Architecture
6G RAN
6GC
Commercially
deployed options
LTE
EPC
LTE
5GC
NR
NR
5GC
LTE
NR
5GC
NR
Option 2
Option 3
Option 5
Option 4
Option 7
5GC
LTE

## Slide 3: Migration/Architecture Options for 6G
Seamless interworking with 5G system
  Single registration vs dual registration
No interworking with 2G and 3G system
Seamless interworking with 4G system?
  General consideration to avoid interworking with 4G
  Scenarios needs to be further discussed
Migration solutions will be needed for 6G standalone architecture
MRSS (5G+6G spectrum sharing) and 6G-6G carrier aggregation
MRSS / CA can be baseline option, but some operators want to have more aggregation options for the flexibility in deployment
  5G-6G Dual Connectivity
  5G-6G Dual-stack
Migration/Architecture Options
Interworking with legacy 3GPP systems
5G cell
(5G band)
6G cell 1
(5G band)
6G cell 2
(new 6G band)
6G CA
Spectrum
Sharing

## Slide 4: Proposals for 6G System Architecture Study
1. Migration scenarios from 5G deployment to 6G/5G deployments
2. Interworking Architecture and Procedure
2-1. Architecture and procedures for supporting Inter-RAT mobility with single registration
2-2. Architecture and procedure for supporting with dual registration for the UE supporting dual stack; one accessing 5G System and the other accessing 6G System
Interworking to provide smooth migration with less network impact
As the transition from Non-Standalone (NSA) to Standalone (SA) proved complex and difficult, 6G SA only should be provided from day one.
Simple and less impact to the legacy system is preferred. For migration from 5G to 6G, mechanism that could work for inter-vendor operation is necessary.
Seamless service continuity should be supported when the UE moves between 5G and 6G system.
Justification
Objectives