## Slide 1: Apple’s View on 6G SID Scope
Apple

## Slide 2: 6G System Architecture Design Principles
6G System Architecture is an evolution of 5GS to support 6G RAN
  Reuse of 5G NFs and addition of new 6G NFs for new services
  Selective extensions on top of existing NAS to support the control of new services
  Standalone Architecture support from day 1
Strive to maintain maximum backward compatibility while enabling enhancements for 6G
Reduce deployment options
Support for new services not to be constrained by legacy design

## Slide 3: Proposed topics for initial 6G study
Three categories are identified:
  Core Architecture
  New Services
  5GS features that are candidate for re-design or enhancement for 6G

## Slide 4: Core Architecture
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
1 | 6G Core Network Architecture | Identifiers Functional division and interfaces Interworking with 5G Mobility Management Session Management QoS and policy to support new services Unified exposure framework across 5GS and 6GS General enhancements to SBI framework and optimizations (e.g. support for HTTP/3 and QUIC, manage the number of new NFs for 6G features) | 6GC is an evolution of 5GC to support 6G RAN and new 6G services. This item should investigate and determine the features and functionalities: to be reused from 5GS to be developed for 6GS. | SA1, SA3, RAN, CT4
2 | Evolved NAS | Support the control of new services while preserving the fundamental MM and SM functionalities over the Control Plane | 6GS needs to facilitate the exchange of NAS messages between the UE and several new NFs in 6GS, considering that new services are going to require new NFs. | None
3 | Support for Basic Services | Support for basic services in non-roaming and roaming scenarios (voice service, emergency services and SMS based on IMS; PWS, location services, etc.) | Support for basic services is required without fallback to legacy systems. | SA1
4 | Network Migration | Support of 5G/6G migration | Support migration between 5G and 6G. | SA1, RAN

## Slide 5: New Services
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
1 | Native AI/ML | AI for Network: AI/ML lifecycle management operations incl new NFs and services E2E cross-domain AI/ML interactions (UE-RAN-6GC-AF) enabling interoperability and controllability Use of device intelligence as an input to system optimization, considering user consent and privacy Network for AI: Optimized resource usage and traffic handling for AI/ML-based applications Adaptation and configuration of AI/ML-based applications Awareness of AI/ML-based application KPI | Main components and principles of AI-Native 6G Networks: AIML data collection and model management framework across devices, network nodes, air interface protocol layer modules and network functions, ensuring multi-vendor interoperability AIML modules which are, where relevant, augmenting or replacing conventional rule-based components within air-interface, network functions, and end-user applications. System architecture that ensures future-proof and forward-compatibility for potential AIML augmentation in protocol stack and services. | SA1, RAN
2 | Integrated Sensing and Communication | Support of UE-based Mono-static Sensing Support of UE-centric Bi-static Sensing Ensure privacy including users that are not involved in the sensing operation | Support of ISAC in 6G | SA1, RAN

## Slide 6: 5GS features candidate for re-design or enhancement for 6GS
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
1 | Network Slicing | Simplification of network slicing functionality | The 5G network slicing procedures involve a great amount of complexity. Roaming and slice mapping between HPLMN and VPLMN makes slice configuration even more complicated. Many add-on features create a complex framework of feature dependency. Additionally, most network slicing features are designed with UE involvement; however, UE does not benefit from all the features. UE slice selection depends on enforcing network-provided policy on UE side (URSP), but it is not known to the network whether UE can interpret and enforce the network provided policy completely or only partially. | SA1
2 | Non-3GPP Access | Simplification of untrusted non-3GPP access support Support of ATSSS over re-designed non-3GPP access | The non-3GPP access design in 5GS is based on a tight integration of non-3GPP access. 6GS needs to address market needs where such tight integration has seen no successful market deployment and allow solutions with no or limited UE impacts. | SA3
3 | Architectural framework for user consent management | Enhance the 6GS architecture to support an evolved user consent management framework | User consent management needs to evolve to allow a more dynamic consent mechanism and to cater to wide range of procedures like data collection, exposure, analytics, traffic management | SA3
4 | Privacy preserving traffic management | Enhanced traffic management for end-to-end encrypted traffic without compromising user privacy (e.g. integrate MASQUE framework with 6GS architecture) | 6GS needs a collaborative way for network operators to manage end-to-end encrypted traffic without compromising user privacy | SA3
5 | Integration of Satellite access (NTN) | Unified design for ubiquitous coverage System level integration and interworking to provide consistent service provisioning across TN and NTN | Satellite access (NTN) provides complementary coverage to TN. Allow for seamless integration of TN and NTN to manage and provide services over both access types. | SA1, RAN

## Slide 7: Summary
Proposed topics aim to provide a complete package for the initial 6G study scoping based on an evolution of 5GS architecture and features
  Other 5G features that are candidate for re-use in 6G can be discussed in a second phase of SID scoping discussions
  Core Architecture topics should take priority for initial discussions with the goal to get them included in the first approved version of the 6G SID
SA2 should strive to minimise architecture options
NWM discussion between SA2#168 and SA2#169 should focus on finding consensus on topics from the three categories
  Highest priority is to agree on the Core Architecture topics to find the framework for further 6G scoping