## Slide 1: UE and network Coordinated Computing in 6GS
OPPO, China Unicom, LG Electronics, CATT, CMCC, vivo, SKT, China Telecom

## Slide 2: Why UE and network Coordinated Computing is needed?
Edge Computing business model (“To B” only) in 5G has not been shown as a very successful commercial case, the Computing/EC design should cover both “To C” and “To B” models in 6GS.
Delay time is a key factor influencing User Experience.
For the new delay sensitive services (e.g. Intent-based AI chatting, online gaming, XR), delay time comprises connectivity delay time and computing delay time.
The legacy QoS design in previous generations (i.e. 4G and 5G) only addresses the connectivity delay time, while the new services are emerging, computing delay time becomes more critical for the computing centric services.
6G system design should aim to coordinate the communication and computing resource allocation between the UE and 6G network to satisfy the overall latency requirement (i.e. round-trip latency plus computing latency) for new emerging services.
6G Network Functions should be able to support in-network Computing for new emerging services, e.g., Intent-based AI chatting, online immersive gaming, XR media computing, by using high-performance network resources (e.g. xPUs), to increase the user experience.
Coordinated computing requires the whole ecosystem (i.e. Device vendor, Device Chipset vendor, Service Provider, Network vendor, Mobile Network Operator) to get involved to provide differentiated user experience for comprehensive new services.

## Slide 3: UE and network Coordinated Computing
Potential new functionality in 6GS:
Provide Computing Resource offloading to network as a service to UE under the control of MNO network;
Support the (re-)discovery of Computing Resource Offloading Function by the UE in 6GS;
Support Computing resource management with a new NF or Session Management Function in core network;
Support UP Function (e.g. PSA UPF, L-PSA UPF, etc.) (re)selection by leveraging Computing resource;
Allocate Computing resource as reserved resource to application during Session Management, which can be triggered by UE or AF during Session Manage Establishment or Modification procedure;
UE knows where, when and how to request Computing support from network.

## Slide 4
Backup
The use cases for new business models will be discussed in SA1 in May

## Slide 5: Business Models for 6G Coordinated Computing - 1
Model A (Semi-dynamic, monthly based charging model):
  Bob is playing XX service (e.g. XR/online immersive gaming/Intention based AI chatting, etc.) via public cellular network (e.g. PLMN A), the XX client in Bob’s device detects the low quality of user experience caused by delay.
  The XX client communicates with its server about the low QoE under the PLMN A and is aware that PLMN supports Computing/Edge Computing via SLA, then the XX client notifies Bob about a 1-day free trial/monthly payment plan to use Computing/Edge Computing.
  Bob accepts the 1-day free trial and the XX client requests Bob’s device to use a PDU Session supporting Computing/Edge Computing based on the UE Policy in the device.
  After trying Computing/Edge Computing for 1-day, if Bob feels better gaming experience with Computing/Edge Computing is worthy of buying a monthly based plan, he can go for it.
  By providing Computing/Edge Computing infrastructure, the PLMN A operator can charge the XX SP via properly configuring the UE Policy in Bob’s device. By enabling the usage of UE Policy in the device, the device vendor can share the revenue with XX SP or PLMN A via SLA. Another benefit for UE is to save UE battery and leverage the computing capability limitation at the UE side.

## Slide 6: Business Models for 6G Coordinated Computing - 2
Model B (Dynamic, duration based charging model):
  Bob subscribes with PLMN A to use PDU Session supporting Computing/Edge Computing for several online immersive gaming services to improve user experience, PLMN A can charge Bob based on duration of the services using the Computing/Edge Computing. The according UE Policy is provisioned to Bob’s device after successful subscription in case dedicated PDU Session supporting Computing/Edge Computing is required.
  When Bob is playing XX service (e.g. XR/online immersive gaming/Intention based AI chatting, etc.) via public cellular network (e.g. PLMN A), the XX client in Bob’s Device detects the low quality of user experience caused by delay in rush hour.
  The XX client communicates with its server about the low QoE under the PLMN A and is aware that PLMN supports Computing/Edge Computing via SLA, then the XX client notifies Bob about the expected duration for rush hour.
  Bob acknowledges the notification from the XX client and accepts the request from the XX client to use a PDU Session supporting Computing/Edge Computing for a computing duration based on the UE Policy provisioned in the device.
  When then rush hour passes away, the XX service is switched back to a bearer not requiring Computing/Edge Computing support.
  By providing Computing/Edge Computing infrastructure, the PLMN A operator can charge bob based on the duration of using a PDU Session or a bearer requiring Computing/Edge Computing support. By enabling the dynamic request to use Computing/Edge Computing, the device vendor and XX SP can share partial of the revenue with PLMN A operator via SLA. Another benefit for UE is to save UE battery and leverage the computing capability limitation at the UE side.

## Slide 7
Thank you!