## Slide 1: vivo view on 6G AIML

## Slide 2
AI Native support in 6G System
Native AI support in CN, RAN, UE
Multi-vendors AI/ML Model sharing
with e.g. open Model format
Distributed Al/ML i.e. AI embedded in 6G NF (optional for UE)
6G Network
AI
CN
AI
RAN
AI
UE
AI
AF
CN
RAN
AF
NW state data
Data/Info/ML Model Exchange
(e.g. data collection, Federal Learning)
Statistics/Prediction
/Recommendation?
Statistics/Prediction/
Recommendation?
Centralized Al/ML Platform
Digital Twin Network
Network Resiliency
Data/Info/ML Model Exchange
(e.g. data collection)
Unified Data collection Framework
AI/ML based Network Performance Evaluation
Common AI/ML Framework across 3GPP WGs

## Slide 3
5G AIML Standardization Overview in SA2
1) Introduce the concept of NWDAF(Network Data Analytics Function) to produce data analytics for network automation.
2) Only one network data analytics is supported i.e. slice specific network data analytics
1)Define general framework for data collection and data analytics exposure. NWDAF consist of data collection/model training and model inference
2) 9 more network data analytics supported e.g. Observed Service Experience
R15: Analytics Concept
R16: monolithic Arch
1) Decompose monolithic NWDAF into Model Training logical function/Analytics logical function and Analytics Data Repository Function
2) Data collection framework enhancement via DCCF (Data collection coordination Function)
3) 5 More network data analytics supported
R17: distributed Arch
1) Architecture enhancement e.g. model performance monitoring/multi-Vendor ML Model sharing/Horizontal FL/ /data analytics in roaming
2) Data collection framework enhancement via UPF data exposure/DCCF relocation
3) 6 More network data analytics supported
R18: Arch enhancement
In 5GA, R15-R18 eNA(enablers for Network Automation) is a pre-study for AIML in SA2, which is to study and specify how to collect data and feedback data analytics to the network and AI/ML algorithm is not in the scope
In R19 and R20 , SA2 FS_AIML_CN is to further investigate and identify potential architecture enhancements to support AI/ML including VFL signaling storm prevention and UE data collection for UE side model training.
It is propose to develop 6G Architecture with the support of native AI/ML, which will consider AI/ML related work in SA2 and other related working groups, e.g. AI/ML lifecycle framework and data collection framework.
2016 | 2017 | 2017 |  | 2018 |  |  | 2019 |  |  |  | 2020 | 2021 |  | 2022 | 2023 | 
~ | Q1 | ~ | Q4 | Q1 | ~ | Q4 | Q1 | Q2 | Q3 | Q4 | ~ | Q1 | Q2 | ~ | Q1 | Q2
NWDAF
1 UC
NWDAF
10 UCs
AnLF
MTLF
DCCF
15 UCs
ADRF
model
AnLF
MTLF
DCCF
21 UCs
ADRF
model
Perfo. Monitor
Model sharing
Horizontal FL
Roaming Enh.
UPF
Data

## Slide 4
5G AI/ML Framework in Core Network
NWDAF(Network Data Analytics Function) provides analytics to consumers e.g. 5GC NFs to assist intelligent procedures
Data collection framework for AIML
  DCCF (Data Collection Coordination Function) is to coordinate data collection to avoid duplication data collection
  ADRF(Analytics Data Repository Function) is to store and retrieve the collected data and analytics
  MFAF (Messaging Framework Adaptor Function) is a logical Messaging Framework to improve the data exchange
Observations
  Only NWDAF has AIML capability and other 5G NF has no AIML capability
  NWDAF only provide statistics/prediction to NF consumer, which will be taken into account by NF consumer to make decision
  Data collection framework for AIML is defined ,which is not extended to support other cases e.g. energy efficiently
  NWDAF communication with RAN is not supported
NEF
NWDAF
AF
PCF
AMF
SMF
UPF
Nnef
Nnwdaf
Naf
Npcf
Namf
Nsmf
N4
UDR
Nudr
CHF
Nchf
OAM
RAN
UE

## Slide 5
6G AI/ML Framework in Core Network
Fig1: 5G AI/ML Framework with centralized NWDAF AIML capabilities
Fig2: 6G AI/ML Framework with all 6G NFs AIML capabilities(optional)
Key Work Tasks for 6G:
Architecture support for 6G NFs (including 6G AI Function) with built-in AI/ML capabilities
  Whether and how one 6G NFs (with built-in AI/ML capabilities) communicate/coordinate with another 6G NF or AI function
  Whether and how 6G NF communicate/coordinate with RAN/UE
  Study corresponding use case(s)

## Slide 6
Background in 5G: NWDAF additionally support recommendation?
Usually NWDAF only provide statistics/prediction to consumer and in R19 AIML_CN further study whether and how NWDAF additionally support recommendation e.g. recommended candidate QoS parameters set.
Recommendation is ruled out in R19 5GA as only centralized NWDAF is AIML capable and recommendation from NWDAF may have to be aware of NF logic and consequently have big impact on overall network architecture
Proposal: In 6G AI era, assuming 6G NF with built-in AI/ML capabilities e.g. AI Agent embedded in 6G NF(s), it is worthy further study whether and how 6G NF leverage AIML to get additional assistance besides statistics/prediction within 6G NF(s)
Multi-Objective Optimization
Recommended？
(e.g. recommend QoS parameters set)
Expected Output
(e.g. Service MoS>4)
Output
(statistics/prediction)
Input data
Inference
Fig1: 5G AI/ML supporting statistics/prediction
Fig2: 5G AI/ML additionally supporting recommendation?

## Slide 7
Key Work Tasks for 6G:
AI/ML assisted 6G basic procedures e.g. MM/SM/policy, etc.
  Single 6G NF(with built-in AI Agent) locally makes decision and executes tasks with its local data and/or other 6G NF data
  In order to avoid conflicts and make more global optimization, multiple 6G NFs(with built-in AI Agents) work together and collaboratively makes decision and executes task(s)
Note: AI Function is to assist 6G NF e.g. model training and does not need to know NF logic and decision-making, executing tasks is still performed by 6G NF
AI/ML assisted 6G NF decision making/ executing task in 6GS
Fig1: 5G AI/ML only supporting statistics/prediction
AI Agent (per latest SA1 current discussion): an automated intelligent entity capable of e.g. interacting with its environment, acquiring contextual information, reasoning, self-learning, decision-making, executing tasks (autonomously or in collaboration with other Al Agents) to achieve a specific goal
Fig2: 6G AI/ML supporting AI Agent?, besides statistics/prediction
Notes: UE centric NW类似与slice，HW A core利用与一个agent（神奇的盒子）去编排，分析各域需要的资源，最终形成一个E2E slice。

## Slide 8
Key Work Tasks for 6G:
Unified data collection framework to support AI/ML related activities e.g. data collection, data storage, data exposure, data privacy and security management, model sharing/delivery, etc.
  UE data collection (e.g. for UE side model) and data collection Framework for AI/ML in 5G will be considered.
Unified Data collection supporting AIML Activities
Fig1: Data collection for 5G AI/ML in 5G
Fig2: Unified Data collection for Multi purpose e.g. AIML sensing
Notes: UE centric NW类似与slice，HW A core利用与一个agent（神奇的盒子）去编排，分析各域需要的资源，最终形成一个E2E slice。

## Slide 9
Key Work Tasks for 6G:
Unified AI/ML Framework across SA/RAN including
  Unified AI/ML terminology
  Unified AI/ML feature Alignment
  Unified AIML lifecycle management
  ….
Study on 3GPP AI/ML Consistency Alignment in SA Plenary
In Rel-18 and Rel-19, most working groups in TSG SA, CT and RAN have already performed SIs and/or have WIs relating to the AI/ML topic and misalignments/inconsistencies may exist among 3GPP working groups
The study will investigate ongoing AI/ML work in TSG CT, TSG RAN and TSG SA Working Groups and identify instances of any potential misalignment and/or inconsistencies and provide information on any potential outcome to the respective WGs to resolve any issues
The study is led by TSG SA in close collaboration and inputs from TSG CT/TSG RAN
Note: see approved SID at SP-241368.zip and TR report at TR 22.850
Notes: UE centric NW类似与slice，HW A core利用与一个agent（神奇的盒子）去编排，分析各域需要的资源，最终形成一个E2E slice。

## Slide 10
Key Works Tasks for 6G AIML
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
1 | Native AI support in 6G | Key Work Tasks： WT-1: AI/ML native architecture for 6G system Wt#1.1: Architecture support for all 6G NFs (including 6G AI Function) with built-in AI/ML capabilities e.g. AI Agent embedded in 6G NF(s) WT#1.2: AI/ML(e.g. AI Agent) assisted 6G basic procedure e.g. MM/SM/policy, etc. WT#2: Unified data collection framework to support AI/ML related activities e.g. data collection, data storage, data exposure, data privacy and security management, model sharing/delivery, etc. Note: UE data collection and 5GC data collection Framework for AI/ML will be considered WT-3: Unified AI/ML Framework across SA/RAN e.g. Unified AI/ML terminology/feature and Unified AIML lifecycle management WT-4: Multi-vendors AI/ML Model sharing with e.g. open Model format | Integrating AI/ML frameworks natively into the 6G network for intelligent automation, optimization, and improved efficiency | RAN, SA3 and SA5
Notes: UE centric NW类似与slice，HW A core利用与一个agent（神奇的盒子）去编排，分析各域需要的资源，最终形成一个E2E slice。

## Slide 11
Notes: UE centric NW类似与slice，HW A core利用与一个agent（神奇的盒子）去编排，分析各域需要的资源，最终形成一个E2E slice。