## Slide 1
Samsung View on 6G Architecture
3GPP SA2#168
7 – 11 April 2025, Goteburg, Sweden
S2-2503602
New Opportunity
TCO reduction
Agenda item: 30.7
Source: Samsung
Document for: Presentation

## Slide 2
Samsung View on 6G Architecture (1/2)
1. Embedded AI
Each NF and RAN with native support of AI functionalities
2. AI collaboration across NFs
- Collected Data, Model Delivery
- AI-based decision among MM, SM, Policy in the control procedure
3. Cross domain AI across RAN, CN, OAM
TCO reduction
Native AI
1. Identifying legacy features/services to be deprecated to relieve backwards compatibility issues
2. Redesigning over-complicated features or multiple options without well-justified use cases
3. Removing duplicated functionalities across RAN and CN (e.g. paging)
Compact and Simple Architecture
Keep it simple
Energy Efficient operation compliant to regulations as service requirements
Macro-level Energy management to reduce total energy use
B2B support to manage carbon emissions
Energy Saving
S2-2503602
Migration scenarios from 5G deployments to 6G/5G deployments
Interworking and Migration
2. Interworking architecture and procedure
2.1 Support of Inter-RAT mobility with single registration
2.2 Support of dual registration/dual stack for accessing 5G and 6G
- Fill the gap period when 6G coverage is not nation-wide
6G SA only from day one
Notes: Migration scenarios from 5G deployment to 6G/5G deployments
2. Interworking Architecture and Procedure
2-1. Architecture and procedures for supporting Inter-RAT mobility with single registration
2-2. Architecture and procedure for supporting with dual registration for the UE supporting dual stack; one accessing 5G System and the other accessing 6G System
(S2-2503377)

## Slide 3
Samsung View on 6G Architecture (2/2)
TCO reduction
Data Management with User Consent
1. Architecture for “Service Plane” for 6G Services (e.g. Sensing, AI)
2. Data and signaling mechanisms for 6G services in the service plane
3. Discovery and Selection of Service Plane Entities
4. Data management functionality with consideration of user consent
Service Plane
1. QoS framework to handle correlated service flow(s) together in a unified manner.
2. QoS framework to support effective QoS control for immersive communication e.g. dynamic in-time QoS control adjustment.
3. QoS framework to consider whole the data path to end user.
Immersive Communications
When user related data is used within the network for e.g., sensing, AI/ML, user privacy protection must be ensured
S2-2503602
Dynamic/On-demand network sharing
Network sharing for disaster, network failure and overloaded situation
Dynamic activation of network sharing, Hosting Network RAN selection per area
Minimization of service interruption during network sharing is activated
Inter-operator monitoring for the shared network resources
Network Resiliency and Always-On connections
Notes: 1. Migration scenarios from 5G deployment to 6G/5G deployments
2. Interworking Architecture and Procedure
2-1. Architecture and procedures for supporting Inter-RAT mobility with single registration
2-2. Architecture and procedure for supporting with dual registration for the UE supporting dual stack; one accessing 5G System and the other accessing 6G System

## Slide 4
View on 6G SID Scope Content for Architecture requirements (1/2)
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
X | Compact and Simple Architecture | 1. Identify impacts of legacy features/services that are rarely deployed, in the architectural perspectives, and study the network architecture to address them efficiently in 6G while alleviating backwards compatibility issues 2. Identify and redesign features defined over-complicated or multiple options without well-justified use cases, e.g., network slicing, XRM, edge computing, etc. 3. Identify areas for improvement on RAN and CN functions, e.g., optimize functionalities in RAN and CN that are defined for duplicated or similar purposes | 6G system architecture should be compact and simple by avoiding duplicated functionalities across RAN and CN, and identifying legacy features/services to be deprecated. | RAN WGs, SA3, SA5
X | Native AI | 1. Identify impacts on system architecture and NF behaviors for embedding and supporting AI functionalities at the NFs. 2. Support of collaboration and/or interworking among AI functions at different NFs (e.g., MM, SM, Policy, etc.) in the control procedure. 3. Architecture and protocol design to support collaboration and/or interworking of AI functions across RAN, CN and OAM for, e.g., data collection, model training, inference, performance monitoring etc. NOTE: “Service Plane” can be used for collaboration and/or interworking between AI functions. | Native support of AI functionalities across 6G network to improve the overall performance of 6G system and user experience by federation or collaboration of AI functions at heterogeneous NFs, RAN and OAM Single AI/ML-based local optimization cannot not guarantee the performance improvement of the overall system. Native network AI/ML could contribute to achieve cost-efficient network management and optimize network overall performance. | RAN WGs, SA3, SA5
X | Energy Saving | 1. Energy-related regulations in different regions should be taken into account to formulate them as service requirements 2. Macro-level energy management system to reduce total energy use in the network and achieve cost-optimal methodology 3. B2B support to manage carbon emissions, e.g. as a platform for carbon emission trading | Native AI leads to core network consuming significant amount of energy 6G network should comply with energy-related regulations and enhance corporate social responsibility Not only regulation but also B2B scenarios would be considered for additional revenue | RAN WGs, SA5
X | Migration and Interworking | 1. Migration scenarios from 5G deployment to 6G/5G deployments 2. Interworking Architecture and Procedure 2-1. Architecture and procedures for supporting Inter-RAT mobility with single registration 2-2. Architecture and procedure for supporting dual registration/dual stack; one accessing 5G System and the other accessing 6G System | As the transition from Non-Standalone (NSA) to Standalone (SA) proved complex and difficult, 6G SA only should be provided from day one. Simple and less impact to the legacy system is preferred. For migration from 5G to 6G, mechanism that could work for inter-vendor operation is necessary. Seamless service continuity should be supported when the UE moves between 5G and 6G system. | RAN WGs, SA3, SA5
S2-2503602

## Slide 5
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
X | Service Plane | Support of accommodation of 6G services in a separate plane from the control/user plane functions for independent scalable deployment of 6G services 1. Architecture and protocol of service plane for 6G services (e.g., sensing, network AI, AI agent, data management, user consent management, configurations for UE) 2. Data and signal transmission mechanisms for 6G services in the service plane 3. Discovery/selection mechanisms for service plane entities 4. Data management functionality with consideration of user consent | 6G architecture should be designed to support new characteristics of 6G Services (e.g. sensing, AI/ML) which are different than traditional telecommunication services When user related data is used within the network for e.g., sensing, AI/ML, user privacy protection must be ensured | RAN WGs, SA3, SA5
X | Network Resilience and Always-on Connections | 1. New architecture and functionalities for dynamic/on-demand network sharing 2. How to support detection/prediction of need for network sharing (e.g., disaster occurrence, network failure, overloaded situation) 3. How to support network sharing activation, including shared network resource selection (e.g., host network RAN) for a given area 4. Service interruption minimization (e.g., via mobility management) during network sharing activation 5. Inter-operator monitoring for the shared network resource, e.g., monitoring the shared resource usage (e.g., represented by traffic volume in a shared network) and quality of connectivity service via the shared resource (e.g., QoS and shared network coverage) | Global telecommunications sector has experienced numerous/significant incidents which led to internet outage and disruptions in industry applications (see clause 5.4.1 of TR 22.870). Conventional approach such as MINT in 5G deals with limited scenario. Consideration of the network system transition for enabling stateless operations and seamless deployment in the cloud, network sharing could be enhanced to provide the resilience by offering an alternative network in more flexible fashion and more various scenarios of network failure. | RAN WGs, SA3, SA5
X | Immersive Communication | 1. QoS framework to handle correlated service flow(s) together in a unified manner. 2. QoS framework to support effective QoS control for immersive communication e.g. dynamic in-time QoS control adjustment. 3. QoS framework to consider whole the data path to end user. | To support rich immersive communication and media service to actual end users, QoS framework for 6G is required, where different service flows could have correlation or dependency among/within their media traffics. Moreover, we may need consider in time probably more fluctuated network situation and changing traffic characteristics. TR 22.870 [PR.9.x.2-1] Subject to operator policy, the 6G system shall support the synchronization of independent traffic flows of one or more applications, to be delivered to more than one device (i.e., UE or tethered devices) | RAN WGs, SA4
S2-2503602
View on 6G SID Scope Content for Architecture requirements (2/2)