## Slide 1: Topics for SA2 6G Study
Agenda Item: 30.7
Vodafone

## Slide 2: Overview
The adoption of 5GC has not been fast and many operators are unenthusiastic about another major change in the core network. We should examine the commercial drivers for any change to the core network for a new 6G RAT.
We need strong focus on the cost and energy efficiency for 6G.
Migration is important.
Simplify procedures & discontinue features without market traction.

## Slide 3: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
1 | Reuse 5GC, evolve 5GC, or new Core? | identify key pain points with 5GC identify modifications to use with 6G RAN and justify (identify business drivers) | The adoption of 5GC has not been fast and many operators are unenthusiastic about another major change in the core network. We should examine the commercial drivers for any change to the 5GC for 6G RAN (beyond adding an optional 6G RAT Type IE to N2-AP and related subscription control). Note that quantum safe security is needed independently of any new RAT and is not driven by 6G. | 
2 | Migration to 6G (if no inter-RAT dual connectivity) | Amongst other tasks, study techniques for: Handover to 5G in case 6G connection quality degrades very early in the 6G connection Signalling free idle mode mobility between 5G <-> 6G to enable idle mode mobiles to be easily pushed to the 6G layers | We should study how e.g. a high 6G frequency capacity layer can give good customer service without lower frequency 6G coverage. | Results are useful for plenary level decisions on migration.
3 | Simplification of procedures / non-continuation of unused 5G features with 6G RAT | - Study which 5GC procedures do not need to be supported with 6G RAT, and which procedures need radical simplification | A number of 3GPP features have failed to gain market traction while others have proved unduly complex. There is a need to consider what to do with these features with a 6G RAT. Examples: Not continue: sidelink; Multicast/broadcast; LADN;… | 

## Slide 4: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
4 | AI | Identify how AI in the core can reduce the cost per Giga Byte Identify potential new services enabled by AI in the core network Identify how AI framework in CN can assist other parts of the network (e.g. RAN) | We need to ensure we can improve cost efficiency and energy efficiency. Our studies on AI should have a strong focus on achieving this. | 
5 | Inter-System / Inter-RAT Mobility | Study: How to ensure 6G-5G-4G-5G-6G mobility works Connected mode N26 mobility from 6G to 4G (but not 4G to 6G) – aim for zero MME impact | Areas of 4G only coverage are likely to continue to exist. Better to avoid facing same situation as in Rel 15 design where 4G to 5G mobility failed after the UE touched 2G or 3G. The MRSS concept and focus on 6G Carrier Aggregation implies that we have a 6G terrestrial coverage layer that matches or exceeds 4G/5G coverage. At the edge of terrestrial coverage (i.e. edge of 6G), the mobile needs to be handed over to 4G Satellite access. | 
6 | RRC Inactive | Investigate RRC Inactive and alternative solutions for fast idle-active change taking into account a multi-RAT environment | Adoption of RRC Inactive is not universal. It requires duplication of functionality in RAN and Core which is complex to deliver. Also, the benefits of RRC Inactive require the mobile to remain on that RAT, however during early days of Generation N, the mobile frequently falls to Generation N-1; while later on, the RAN pushes mobiles to Generation N+1. | RAN (2)

## Slide 5: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
7 | Roaming | - Preserve with zero changes - Start all studies from the roaming architecture | Roaming devices are important and are the basis of much of the low, mid and high end IoT services. Expectation is for massive increases in the number of IoT devices is huge. We should ensure that 6G caters for the roaming IoT market sector Designing non-roaming architectures and then adding roaming afterwards generally causes problems. It is almost always better to start with a high-level design (stage 2) based on roaming. If needed, workload can be reduced by not specifying the stage 3s for some interfaces in the first release. | 
8 | Enable MNO to operate across multiple countries | Study how to enable Core Network Functions to operate across multiple countries, e.g. remove all LI aspects from AMF | Having replicated core networks in every (small European) country is expensive. LI is the major barrier to sharing one core network between multiple countries. It would be useful to study architecture changes that enable CN centralisation while enabling LI to be handled nationally. | SA3-LI
9 | Day 1 (regulatory) voice support | Identify what issues prevented day 1 support for (regulated) voice in 5G Identify techniques to mitigate these issues with 6G RAT | Release 15 (“main drop”) fully supported VoNR and emergency calls. However, deployments of VoNR were delayed. We should study what were the main issues (e.g. lack of contiguous 5G coverage; late IoDT of AMF-MME handovers; late IoDT of inter-RAT measurement reports; Cell ID format on LI interfaces; etc) and how to find solutions to them for a 6G RAT. | 

## Slide 6: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
10 | Sensing | Study architecture | Our architectures normally involve UEs registered on the network, in radio communication with the network, and enable IP data transfer. None of these seem to apply to sensing. New architecture modules may need to be considered. | 
11 | Increase use of SBI and open interfaces | Study use of SBI for N4 interface Study how to remove options from N4 to improve multi-vendor opportunities | The functional split across the N4 interface has options that inhibit multi-vendor operation. | 
12 | SCTP replacement | Study the replacement of SCTP with more modern protocols in the core network | SCTP seems to be only used within the telco industry and the pool of developers is getting smaller. Moving to more modern protocols should help future enhancement and maintenance of the CN. | Could allocate to RAN 3?

## Slide 7: Proposal
The items on the previous 3 slides should be included in SA2’s Release 20 Study on Core Network support for a new 6G RAT.