## Slide 1: CATT views on SA2 6G SID
Contact: Ming Ai
aiming@catt.cn

## Slide 2: Outline
Overall view on 6G SID Scope for 6G Architecture (CATT interested 11 topics)
  System Architecture
  6G New NAS
  Full Service based Architecture for 6G System
  Data Plane for Unified Data Framework
  Native AI & AI Agent Communication
  Location Service and Sensing Service Integration
  Terrestrial and Satellite Networks Convergence for 6G
  6G QoS Architecture
  Computing and Network Coordination
  Energy Efficiency and Energy Saving
  Distributed Autonomous Subnetwork
Summary

## Slide 3: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
1 | System Architecture | Design a new 6G Core, identify which NFs should be re-used, re-designed and new added. Support of full service-based architecture, at least including service-based N2 and N4 interfaces. Support of RAN and CN functionalities split. Support of 6G Standalone Architecture as the baseline. Support of new 6G RAT (including satellite access and terrestrial access) and non-3GPP access, architecture design should minimize access dependencies. IMS-based voice. Support of interworking with 5G system. Network exposure. | New 6G Core enables the 6G network to natively support the connectivity and beyond connectivity services. Full service-based architecture enables an intelligent, simple architecture with flexibility, scalability and sustainability. CN-RAN functionalities split enables CN and RAN functionalities independent evolution. Standalone architecture is preferred, to avoid too many architecture options. Integrating terrestrial networks and satellite networks for ubiquitous coverage and resilient services. Interworking with 5G system fulfills most operators’ deployment requirements. | RAN WGs, SA3

## Slide 4: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
2 | 6G New NAS | Support new NAS for connectivity and beyond connectivity services. Study NAS termination and routing in core network for security, connectivity services and beyond connectivity services; and high-level procedures. | 6G New NAS natively support the connectivity and beyond connectivity services. In 5G, the evolution of 5GC NFs has dependence with AMF. Furthermore, AMF is the bottleneck of the message transmission. | RAN WGs, SA3

## Slide 5: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
3 | Full Service based Architecture for 6G System | Study the new service-based architecture for 6G system All CP interfaces within the 6G CN are service-based All interfaces (N4) between CP and UP are service-based; All interfaces between the CP and Data Plane are service based; The interface between the 6G RAN and 6G CN is service-based; Enhance the service performance and reliability; Note: The interfaces between UP (N3/N6/N9) are not required to be the SBI. | The SBA and SBI are introduced in 5G CP from the day-1, but there are interfaces are not SBI-based, e.g. N4, N2, Nx. The RAN can be running on the same general IT-based hardware and software platform as the CN. Use the SBI interfaces for all the CP interfaces can decrease the different types of interfaces and protocols for the 6G system and decrease the deployment cost. | RAN WGs

## Slide 6: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
4 | Data Plane for Unified Data Framework | Introduce Data Plane to support unified data framework (including data collection, transmission, processing and storage) for different use cases, e.g., sensing service, AI/ML service. Architecture, network function and high-level procedures of Data Plane. Support Data Plane between UE, RAN, and CN NFs. Data service exposure. | Beyond traditional communication, some new 6G services emerging, such as Sensing service, AI/ML service, brings some new data-related requirements. Current 5G data collection methods are varied and across different use cases, introduces complexity to architecture. An Unified data management framework needs to be considered at the beginning of 6G architecture design. Traditional CP for signaling data, UP for user connectivity service data, and an additional Data plane is preferred for operator’s beyond connectivity service data. | RAN WGs, SA3, SA5

## Slide 7: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
5 | Native AI + AI Agent Communication | 6GS Architecture model to support native AI, including e.g. defining new NF(s) and interfaces for 6G AI; How to leverage AI in UE, RAN and CN NFs functionalities and procedures to support communication services, potential new beyond communication services (e.g. Sensing) and improve system performance, e.g. MM+AI, SM+AI; How to support AI as a Service (e.g. AI related data collection, model training and analytics sharing) in 6GS, and between 6GS and the third party (i.e. external AF); How to support AI applications and services, e.g. AI Agent Communications and applications | In 5GS, the NWDAF-based network data analytics framework cannot meet the 6G requirements of AI-based system control and service provision, neither the across-domain AI coordination. In 6GS, a new AI native system architecture design is expected and considered, e.g. by incorporating AI in functionalities of UE, RAN and most (if not all) of CN NFs, even AI-Agent in some NFs. | RAN WGs, SA3, SA5

## Slide 8: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
6 | Location Service and Sensing Service Integration | Architecture to support location service and sensing service integration. Network functions and high-level procedures to support location service and sensing service. Location service and sensing service exposure. | Location service is an important and mandatory function in 6G. And the sensing service has requirement on location. The logic for both location service and sensing service involves calculating based on the collected wireless measurement signals. Independent design would lead to functional duplication and complex network deployment. A new integrated design is conducive to system simplification. | RAN WGs, SA3, SA5

## Slide 9: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
7 | Terrestrial and Satellite Networks Convergence for 6G | Support of new 6G RAT for satellite access How to support high level procedures (e.g., registration/session management) for terrestrial and satellite networks convergence How to support service continuity when UE moves between terrestrial and satellite networks, including between multi-orbit satellite networks. How to maintain connectivity through satellite networks when terrestrial networks become unavailable, e.g., due to disasters. Support positioning for satellite networks with GNSS independence. IoT support over 6G NTN Whether and how to support diverse IoT connectivity types over satellite networks Support IMS Voice over GEO Support robust notification Whether and how to support robust notification. | Unlike 5G where satellite was an add-on feature, 6G requires native convergence of terrestrial and non-terrestrial networks from the beginning to ensure service availability/continuity across satellites access and maintain critical communications when terrestrial networks become unavailable. GNSS-independent positioning is needed for system resilience in areas with limited GNSS coverage. 6G IoT NTN aims to provide seamless global connectivity for diverse IoT devices to meet the exponentially growing connectivity demands in remote areas. IMS voice services over GEO require to overcome the significant propagation delay while ensuring voice quality. Poor satellite coverage conditions require alternative notification methods to ensure users receive alerts about incoming communications. | RAN WGs, SA3, SA5

## Slide 10: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
8 | 6G QoS Architecture | Study the unified 6G Policy and QoS Architecture for different connectivity services and beyond connectivity services. QoS control granularity ; QoS control mechanism (CN control, UE control , UE+CN control, QoS binding); Policy rules for UE, RAN, CN NFs; Packet filters for QoS binding. Study the unified 6G QoS parameters New QoS parameters are introduced; Procedures to provide dynamic QoS parameters. Study how to leverage AI for the QoS Policy rules decision; QoS parameter selection; Service identification. | Beyond connectivity services are estimated to be introduced in the 6GS, how to enforce the service data QoS shall be studied in 6G. Difference services, including connectivity services and beyond connectivity services shall use the same unified 6G policy and QoS architecture and unified QoS parameters to make the 6G simple to support new AI and sensing services. Immersive communication will introduce new QoS parameters, needs to study whether new QoS parameters are introduced for the beyond connectivity services (e.g. AI, sensing services). AI can be used to improve the QoS rules and QoS parameters selection and service flow detection. | RAN WGs

## Slide 11: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
9 | Computing and Network Coordination | Whether and what computing power resources can be provided and/or managed by the 6G network. Architecture, network function, and high-level procedures to support the coordination between computing and communication. How to support offloading computing from the end-user device to the network, including how UE requests to use computing capabilities should be discussed. How to support the computing coordination between the device, the network and the edge/cloud servers. How to monitor computing power status. How to support computing capabilities exposure. | With the development of network cloudization technology, 6G networks are expected to provide computing power resources to enhance the utilization of idle computing power in core network and to meet the high computing power demands of new services (such as, XR rending). Also, because of the limited computing power of one single device such as XR terminal, it is necessary to coordinate distributed computing resources to achieve on-demand computing offloading from the end-user device to the network and/or the edge/cloud servers. | SA5

## Slide 12: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
10 | Energy Efficiency and Energy Saving | 6GS Architecture to support Energy Efficiency and Energy Saving, including e.g. defining new NF(s) and interfaces for 6G energy control; Coordinated system energy efficiency and energy saving between CN, RAN and UE; UE awareness and assistance to 6G network energy efficiency and energy saving; AI assisted 6G system energy efficiency and energy saving. | In 5G, enhancements to the system for energy efficiency and energy saving are done in later releases (i.e. R17/18/19), which hinders the potentials of applying some more effective energy saving mechanisms due to e.g. backward compatibility issues. Considering the sustainability and low carbon emission target of 6GS, it is important to support energy efficiency and energy saving in initial 6G architecture design. | RAN WGs, SA5

## Slide 13: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
11 | Distributed Autonomous Subnetwork | Architecture to support Distributed Autonomous Subnetwork Network functions and high-level procedures to support Distributed Autonomous Subnetwork. Support of interworking with Network Slicing and SNPN. Note: Subnetwork is an extension of the PLMN network; It provides network services with a certain degree of autonomy, localization, topology hiding, cross domain collaboration and diversified functions in specific areas during specific time periods based on the needs of individual customers. | In 5GS, network slice is too complex, the interaction between SNPN and PLMN is also complex which requires the envolvement of N3IWF. In 6G, a more flexible and efficient mechanism should be considered. | RAN WGs, SA3

## Slide 14: Summary
6G Architecture will have following new enablers for new services:
  Native AI &s AI-Agent communications;
  Data plane for Unified Data Framework;
  Computing and Network Coordination;
  Integration of Sensing with communications, and Location,
  …..
  SA2 6G study shall have a suitable time period, i.e. set the SID completion date to March 2027, to allow more technical discussions.