## Slide 1
Discussion for 6G Study on Network Resilience
Agenda item: 30.7
Source: Samsung
Document for: Discussion
3GPP SA WG2 Meeting #168
07 – 11 April, 2025, Goteburg, Sweden
S2-2503733

## Slide 2
Network Resilience and Always-on Connections
Global telecommunications sector has experienced numerous/significant incidents which led to internet outage and disruptions in industry applications (see clause 5.4.1 of TR 22.870). For zero-outage network, 6G network should be self-adaptive and self-healing with enabling zero-touch network construction e.g. in the case of network failure due to overcrowding or disaster situations
Restoration solutions for 5GC have been standardized, but it is reactive-fashion with inevitable endurance of network outage/failure during the restoration period, which is not sufficient for zero-outage network
Offering an alternative network (e.g., via network sharing) during the restoration period or even before the network failure could be a timely approach to pursue zero-outage network
Conventional approach such as MINT in 5G deals with limited scenario and requires substantial pre configuration
Mobile network system are transitioning from hardware based to software based system, enabling stateless operations and seamless deployment in the cloud. With consideration of this transition, network sharing could be enhanced to provide the resilience by offering an alternative network in more flexible fashion and more various scenarios of network failure
Related 6G SA1 requirement is mentioned in clause 5.4.1.2 of TR 22.870: [PR 5.4.1.6-1] Subject to regulatory requirements and operator’s policy, 6G network should support suitable means to detect, isolate and recover from network failure
Motivation/Justification
6G network should be self adaptive and self healing with enabling zero touch network construction, e.g., in the case of network failure due to overcrowding or disaster situations

## Slide 3
6G System Architecture Study Objectives
New architecture and functionalities for dynamic/on-demand network sharing
How to support detection/prediction of need for network sharing (e.g., disaster occurrence, network failure, overloaded situation)
How to support network sharing activation, including shared network resource selection for a given area
Service interruption minimization (e.g., via mobility management) during network sharing activation
Inter-operator monitoring for the shared network resource such as monitoring the shared resource usage (e.g., represented by traffic volume in a shared network) and quality of connectivity service via the shared resource (e.g., QoS and shared network coverage)
Proposed Key Objectives
Stateless and cloud native operations enabling dynamic network sharing to timely offer an alternative network in more flexible fashion to enhance network resilience
CN (MNO1)
CN (MNO2)
MNO 1 (host)
MNO 2 (participant)
Participant CN – Host RAN connection establishment
Host RAN
Fig. 1. Exemplary scenario for dynamic network sharing for reaction to network failure*
Fig. 2 . High level expected functionalities for dynamic network sharing
Detection/prediction of network outage
Shared RAN node selection
Connection establishment with participant NW and the shared NW (host NW)
Service interruption minimization (in cooperation with RAN)
Shared network resource monitoring
Core network of MNO1
Core network of MNO2
Core network of MNO1
Core network of MNO2
Hosting NW
Zero-touch
network re-construction
*Note that the target scenario is not limited to RAN failure case.