## Slide 1: Rel-20 6G Priorities
CableLabs, Charter Communications, Comcast

## Slide 2: Outline
6G should build on the principles of 5G, specifically on –
  Access-agnostic core network
  New features specified to work across different access networks
Backward compatibility with previous generation of 3GPP and non-3GPP networks
Support for non-3GPP access from the first release of 6G specifications
New feature parity across access-network types for reduced fragmentation, and improved interoperability

## Slide 3: MSO View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
1 | Inherent non-3GPP access support | From Day 1, 6G UE can access network services (e.g., data, voice) through 3GPP access and/or non-3GPP access (e.g., Wi-Fi, wireline). Access-agnostic control mechanisms between core and AN. | Non-3GPP access continues to transport the majority of network traffic and is essential to complement 3GPP access for any operator. | RAN2, RAN3, SA3
2 | Native multi-access support | Support for fast user plane policy-based traffic management. Enhanced policies considering link and access-based metrics. Enhanced traffic differentiation to accommodate new multimedia streaming. | Seamless, simplified connectivity across access networks is crucial for user experience. | RAN2, RAN3, SA3
3 | Support and identification of diverse device types across access networks | Support devices with different capabilities including robust authentication and authorization mechanisms for each. Identification of a device across access networks. | Unified management of all the user’s devices, irrespective of the underlying access, allows the operator to be a one-stop shop for all of the user’s connectivity needs. | RAN2, RAN3, SA3
4 | Differentiated services | Enable differentiated QoS per individual device, per user-of-device, and per service. Mechanisms to ensure consistent QoS across access networks. | Different devices/users/apps have different network demands which need to fulfilled dynamically and effortlessly. | RAN2, RAN3, SA3
5 | AI/ML capability across access networks | Collection and exposure of network analytics from non-3GPP access. Support operation of AI/ML applications both on core and AN edge. | AI/ML mechanisms need to encompass all domains data to be effective. | RAN2, RAN3, SA3
6 | Non-3GPP ISAC | Incorporating non-3GPP sensing within the 6G sensing framework. | Non-3GPP sensing data & mechanisms complement and augment the sensing service. | SA3
7 | Non-3GPP AIoT | Extend the AIoT framework to include non-3GPP access nodes and spectrum. | Extending the coverage of where the AIoT service can be offered. | SA3
MSO- Multi System Operators

## Slide 4: Summary
Built-in Day-1 support of non-3GPP access within the 6G system
Seamless integration and operations between different access networks
Diverse device support across access networks
Differentiated QoS based on device/user/app needs
Extending support for 6G services like AI/ML, ISAC, AIoT in an access-agnostic way, including non-3GPP access resources