## Slide 1
Huawei, HiSilicon
Security Level:
Rel-20 SA2 Ambient IoT Proposal
3GPP TSG SA2#168 S2-2503844
Goteborg, SE, April 7th – April 11th, 2025
Agenda Item: 30.6

## Slide 2
R20 AIoT use case #1: Recyclable logistics crate management
Recyclable logistics crate is the trend to replace disposable plastic foam boxes to avoid environment pollution. Add electronic labels on the crate for inventory, stock in/out, path tracing, temperature monitoring. And enable end-to-end visibility and management.
Packaging
Farm
Transport
Processing
Re-load
Shelves
Disposal
Recyclable crates
tag attached
Enabled by Ambient IoT
Recycling crates E2E management
UC1: Stock in/out
Inventory
UC2: Status tracking during Transport
UC3: Checkpoint
Stock in/out, automatic inventory accuracy 99.99%
Automatic reading of crates in check point, accuracy 99.99%
Continuous monitoring and update of crates’ temperature, location etc.
Existing solutions issues cannot ensure continuous coverage and the cost is not acceptable.
Consumer requirements:
  Wide area continuous coverage
  Device ultra low power consumption and maintenance-free, device cost ~ 0.5$
  Cell level positioning
Market space forecast: ~3.7 billion recyclable logistics crates in fresh/automotive/electronics industries in 2027
Consumers expressed the desire to support recyclable logistics crate management since 2023

## Slide 3
R20 AIoT use case #2: Infrastructure condition monitoring
Bridges are parts of outdoor public infrastructure and smart bridge condition monitoring is important for safety and maintenance.
Market space forecast: hundreds to thousands of sensors per bridge
Types of sensor used for monitoring status of bridge: displacement, strain, deflection, tilt, cable tension, temperature, acceleration, wind direction and speed, corrosion, crack etc.
Consumer requirements:
  Outdoor wide area coverage
  Device ultra low power consumption and maintenance-free, device cost ~ 0.5$
various sensors
Disadvantages of other solutions
Machine vision: conditions such as rain or night monitoring result low accuracy which is not enough to meet the demands
Wired sensor: reliable, but the layout cost is high and complex, and the cost of monitoring equipment is too high

## Slide 4
R20 AIoT use case #3: Smart grid
In electronic power industry, temperature monitoring is required to monitor the running status of equipment. In this high voltage environment, the battery has safety risks.
AC current transformer
AC switch
AC breaker
Solution 1:
Manual inspection + wired connection
High maintenance costs: About 1200 devices need to be monitored at a time, and the manual inspection is at high labor cost.
Complex networking: Wired devices are deployed at multiple sites, resulting in high deployment costs.
Low accuracy: The measurement accuracy is affected by factors such as magnetic field, load, and reflection.
Poor timeliness: The infrared thermogram used for temperature measurement cannot directly locate the point. Therefore, manual fault locating is required.
Solution 2:
infrared thermometric graph
Disadvantages of existing solutions
Consumer requirements: battery-less for environment safety in extreme condition
Market space forecast: ~ 0.6 billion sensors in power transmission connections, transformer cables and power distribution lines, etc.
There are research projects to study battery-less sensor solution: laboratory stage from 2024, field test in 2025-2026 and expected to be commercial in 2027.

## Slide 5
Proposal of R20 AIoT use cases
In Rel-20, Ambient IoT should additionally support outdoor use cases to meet urgent market demand.
Outdoor inventory and command are clear use cases, and sensor use cases also have ready market demand.
There is interest in positioning, hence applicable scenarios, requirements, type of solution, etc. need further discussions
Proposal 1: Rel-20 Ambient IoT supports outdoor inventory, outdoor sensor, and outdoor command use cases. Applicable scenarios, extent, and requirements of positioning use case support in Rel-20 should be further discussed.
Representative use case (rUC) | Analysis
rUC5: Outdoor inventory | Example use case recyclable logistics crate management has inventory requirement Inventory functionality has been studied in Rel-19, it can be easily extended from indoor to outdoor
rUC6: Outdoor sensor | Example use case smart grid and infrastructure health monitoring has DO-A traffic type sensor report requirement In Rel-19, the air interface for DO-DTT and DT traffic types is not sufficient for the DO-A traffic type The functionality for sensor with DO-A traffic types should be specified in Rel-20
rUC7: Outdoor positioning | rUC7 includes use cases with cell level positioning, and higher positioning accuracy requirements Cell level positioning, e.g. recyclable logistics crate management, can be achieved via an inventory procedure For higher accuracy requirements, the scenarios, solutions, and market demand should be further discussed towards Rel-20.
rUC8: Outdoor command | Example use cases may also need device management, command procedure could also be supported Command functionality has been studied in Rel-19 bundled with inventory procedure, it can be easily extended from indoor to outdoor

## Slide 6
Device C is needed to support outdoor use cases
  Device 2 studied in Rel-19 targets indoor use case and cannot support outdoor use case.
  Based on indoor pathloss model InF-DH NLOS, the maximum distance of device 2 is 62.86m
  If outdoor pathloss model UMA NLOS is assumed, the maximum distance of device 2 is only 33.23m
  The maximum distance of NR macro site is 500m or 1732m based on TR 38.830.
    Proposal 2: For outdoor use cases, ‘Device C’ defined in TR 38.848 should be supported.
  Active transmitter
  1 mW to 10 mW power consumption
 | MPL(dB) | InF-DH NLOS Max distance(m) | UMA NLOS Max distance(m)
Device 2 | 72.1 | 62.86 | 33.23

## Slide 7
Proposal of R20 SA2 Ambient IoT scope
 | Scope | Comment
Scenarios | Logistics crate management Infrastructure condition monitoring Smart grid | 
Representative use cases | Outdoor inventory Outdoor command Outdoor sensor Outdoor positioning (see comment) | Applicable scenarios, extent, and requirements of positioning use case support in Rel-20 should be further discussed.
Traffic type | DO-A DT DO-DTT | Relationship between use case and traffic type: Outdoor sensor <-> DO-A Outdoor command (write/disable)<-> DT Outdoor inventory and command (read) <-> DO-DTT
Device type | Type C | 
Topology | Topology 1 | 
Final scope of SA2 Ambient IoT will be aligned with RAN

## Slide 8
Consideration on topology 2
SA2 had extensive study of T2 in rel-19 and several architecture options are captured in TR 23.700-13.
TSGs should jointly select a single T2 architecture option for the RAN & SA WIDs. It is not suitable to standardize multiple architecture options for T2.
SA2 shall not to repeat the same technical issue discussion as in rel-19, and focus on concluding T2.
More insight into the commercialization opportunities for T2 is required, to allow RAN & SA to find the most efficient standardization method in Rel-20.

## Slide 9
Gap analysis between Device C and Device 1
Features |  |  | Passive Device (Type 1) | Active Device (Type C)
Registration Management | Mobile Originated Registration |  | Not Support | Support
 | Tag ID | Permanent ID | Support | Support
 |  | Temporary ID | Support | Support
Data Transmission | Service Operation |  | DO-DTT: Inventory/Read DT: Write/Kill | DO-DTT: Inventory/Read DT: Write/Kill DO-A: device originated sensor data report
Mobility Management | TAU-like mobility management |  | Not Support | Support

## Slide 10
Proposal of R20 SA2 Ambient IoT work task
WT# (estimate TU) | Work Task description
WT#1 (TU = 4) Architecture to support DO-A traffic type and device C | WT#1.1 (TU=2) : AIoT device C management Study registration management, mobility management Device C identifier, and identification of device C by network Data profile (subscription) management for device C by network
 | WT#1.2 (TU=2): AIoT data transfer Support AIoT device autonomous communication with network (DO-A) Exposure of AIoT services for device C and DO-A traffic type, to third party AF
TU estimate: 4 for study phase + 4 for normative phase