## Slide 1: 6G System Architecture and Services Priorities
Charter Communications, Inc

## Slide 2: Outline
Charter Communications’ Prioritized View on 6G SID Scope Content
Summary

## Slide 3: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
1 | Network Convergence, Access Agnostic, Seamless Mobility | Provide access agnostic service between Cellular (TN & NTN), WiFi, Wireline accesses to a common core network (i.e., all accesses converge to the same core network, to provide 6G services). Seamless transition among and across all access networks. Non-3GPP network control plane procedures should not be dependent on 3GPP networks. Control plane procedures independent of any access. | Users can connect and access services anytime and anywhere. | RAN, SA3, CT
2 | Native Multi-access Data Sessions | Leverage native MA PDU sessions with data flow across different accesses. Strive to offload traffic from 3GPP network to non-3GPP (WiFi & Wireline) networks. 3GPP tight integration with WiFi. | Current industry reports indicate that more than 70% of wireless traffic is over WiFi. GSMA-Voice-over-Wi-Fi-Whitepaper | SA3, CT
3 | QoS differentiation over non-3GPP access | QoS distinction over non-3GPP networks (e.g., L4S, DSCP marking, etc.). | Current industry reports indicate that more than 70% of wireless traffic is over WiFi. | RAN, SA3, CT
4 | Enhanced 5G SBA based on 5GC evolution | 6G standalone architecture while 6G coexist with 5G. Extend SBI between RAN & Core. Leverage QUIC vs HTTP/2 + TLS1.2 for all SBI. Incorporate MASQUE on CP and UP between UE and Core Network, enabling a common transport across accesses. | Operators will increase ROI for 5G while gaining 6G ROI. QUIC is receiving more industry adoption and provides native security & privacy, multi-stream, and latency control. | RAN, SA3, CT

## Slide 4: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
5 | Network Exposure | (in)direct network information exposure via APIs to (un)trusted parties. Network information/data related to a particular service. | Network as a Service (NaaS) and increase end users QoE. | RAN, SA3, SA4, CT
6 | Energy Efficiency and Sustainability | Improved reduction on network power consumption. Improved Energy as a Service feature. Energy Efficiency to be native/considered in all 6G features (when possible). | SA1 TR22.870-0.2.0 include initial requirements to improve e2e EE for the network and UE in 6G (i.e., PR5.6.1.6-1). Such as: UE and network coordination for energy efficiency improvements (UE and NW). | SA3, CT
7 | AI-Native Support | Enhance AI capabilities developed in 5G. Inclusion of cloud resource orchestration. | Improve OPEX, network resiliency, network automation, efficiency and user experience. | RAN, SA3, SA5, SA6, CT

## Slide 5: Summary
Charter prioritizes the following topics as in scope for a 6G SA2 Study:
Non-3GPP support in 1st release of 6G system
Network Convergence, Access Agnostic, & Seamless Connectivity
Multi-Access Native System
QoS differentiation over non-3GPP access
Leverage 5G SA network investment and Service Based Architecture.
Enhance Network Exposure functionality, to enable NaaS
Energy Efficiency considered in all 6G features
AI-Native Support